## Slide 1: Injector Status and Upgrades for MOLLER
Hall A Collaboration Winter Meeting
January 15 – 16, 2025
Riad Suleiman

## Slide 2: Outline
Parity Violation Experiments at CEBAF
MOLLER Requirements
Injector Status and Upgrades for MOLLER:
  Source: 200 kV Gun, Polarized Photocathodes
  Beamline: Solenoid Magnets, 200 keV Wien Filters, SRF Booster
  Helicity Controls: Helicity Generator Board, Helicity Decoder Board
  Parity-Quality Beam : RTP HV Driver, IA HV Driver, Helicity Magnets Control
Future Plans

## Slide 3: Parity-Violating Experiments at CEBAF
PV Experiment | Energy (GeV) | Pol (%) | I (µA) | Target | Apv (ppb) | Charge Asym (ppb) | Position Diff (nm) | Angle Diff (nrad) | Size Asym(δσ/σ)
HAPPEx-I 1998 – 1999 | 3.3 | 38.8 68.8 | 100 40 | 1H (15 cm) | 15,050 | 200 | 12 | 3 | <10-3
G0-Forward 2003 – 2004 | 3.0 | 73.7 | 40 | 1H (20 cm) | 3,000-40,000 | 300±300 | 7±4 | 3±1 | <10-3
HAPPEx-II 2004 – 2005 | 3.03 | 87.1 | 55 | 1H, 4He (20 cm) | 1,580 | 400 | 2 | 0.25 | <10-3
G0-Backward 2006 – 2007 | 0.359, 0.688 | 85.8 | 60 | 1H, 2H (20 cm) | 9,700-37,400 | -30±300 | 47±9 | 1.2±0.5 | <10-3
HAPPEx-III 2009 | 3.484 | 89.4 | 100 | 1H (25 cm) | 23,800 | 200±10 | 3 | 0.5±0.1 | <10-3
PVDIS 2009 | 6.067 | 89.0 | 105 | 2H (20 cm) | 60,000-160,000 | 100 | 100 | 40 | <10-3
PREx-I 2010 | 1.056 | 89.2 | 70 | 208Pb (0.5 mm) | 657±60 | 85±1 | 4 | 1 | <10-4
QWeak 2010 – 2012 | 1.162 | 88.7 | 180 | 1H (34 cm) | 226.5±9.3 | 20.5±1.7 | -4.6±0.2 | -0.07±0.01 | <10-4
PREx-II 2019 | 0.953 | 89.7 | 70 | 208Pb (0.5 mm) | 550±18 | 20.7±0.2 | 2.2±4 | 0.3±0.3 | <6x10-5
CREx 2019-2020 | 2.18 | 87.1 | 150 | 48Ca (5 mm) | 2668±113 | -88±26 | -5.2±3.6 | -0.13±0.08 | <6x10-5
MOLLER 2027-2029 | 10.6 | 90 | 65 | 1H (125 cm) | 35.6±0.74 | <10 | <0.6 | <0.12 | <10-5
An overview of how parity-violating electron scattering experiments are performed at CEBAF,
P.A. Adderley et al., Nuclear Inst. and Methods in Physics Research, A 1046 (2023) 167710 https://doi.org/10.1016/j.nima.2022.167710

## Slide 4: MOLLER Requirements
MOLLER Apparatus is designed for nominal beam energy: GeV with low RF trip rate (<6/hour)
65 µA with 90% polarization (max 70 µA for target studies)
Fast helicity reversal:
  1920 Hz, 10 µs settle time, 64-window pattern, 128-window delay
Slow helicity reversals:
  Insertable half-wave plate (IHWP)
  Wien Filters
  ge-2 ( GeV)
Feedbacks on:
  Helicity-correlated beam charge
  Helicity-correlated position and angle
  Polarization orientation
Small helicity-correlated beam asymmetries
Adequate adiabatic damping of transverse phase-space (for both and ) – a factor of 100 is desired, a factor of 10 is required. Ideally,
Acceptable beam halo (MOLLER Halo Monitor: to be specified, Compton Polarimeter: <100 Hz/µA)

## Slide 5: From Beginning-to-End
Gain-switched Diode Laser and Fiber Amplifier
Attenuator
HWP PC LP
PSS
Shutters
Rotatable Strained
Superlattice GaAs
Photocathode
Vacuum
Window
15° Dipole Magnet
ge-2 Reversal
IHWP
RHWP
RTP
Cell
Delayed
Helicity Fiber
HV Supply
(-2 kV – 2 kV)
HV Supply
(-105 – 105 V)
CEBAF
Hall
T-Settle
Fiber
Charge and Position
Feedbacks
Laser
Electron Beam
Com. Fiber
Controls
Helicity
Fibers
Charge
Feedback
(IA)
LP HWP LP
IA
Target
BCMs
BPMs
6.8 MeV
Helicity Magnets
DAQ
nHelicity
Fibers
Position
Feedback
Helicity Generator
V-Wien Filter
H-Wien Filter
Spin Solenoids
10.6 GeV
200 keV

## Slide 6: 200 kV Gun – Spherical Electrode and 18" Chamber
Upgraded from 130 kV to 200 kV: less space-charge forces → higher transmission
Optimized beam optics and longer charge lifetime
Commissioned and delivering beam right now
Cathode Pierce angle = 16 degrees
Anode tilted by angle = 2.0 degrees
Biased Anode (+1kV)
https://doi.org/10.1103/
PhysRevAccelBeams.27.123401

## Slide 7: Polarized Photocathodes
Now running from Puck #3 (QWeak sibling)
Have extra two SLSP photocathodes in Preparation Chamber
Jefferson Lab, ODU, and UCSB collaborations are successfully prototyping new high-polarization high-QE photocathodes:
Puck # | Photocathode Material | Note
8 | SLSP-5247-1 | PREx-I, QWeak (July 2009 - January 2015)
9 | SLSP-5756-4 | PREx-II and CREx (January 2015 – July 2023)
3 | SLSP-5247-4 | (December 2023 – present)
10 | SLSP-5757-3 | Sibling of 5756 wafer
31 | SLSP-75104​-1 | Measured 0.7% QE and 90% polarization in micro-Mott
https://doi.org/10.1063/5.0170106
https://pos.sissa.it/456/215/pdf

## Slide 8: Solenoid Magnets
Six new solenoids in keV region: uniform field at center – less aberrations
All powered counter-wound: no coupling or spin rotation (), only focusing ()

## Slide 9: 200 keV Wien Filters
Vertical Wien
Spin Solenoids
Horizontal Wien

## Slide 10: 200 keV Electron Beam Spin Manipulation
Long.
Vertical
LEFT
RIGHT
LEFT
RIGHT
Polarized Electron Source
Vertical Wien
Spin Solenoids
Horizontal Wien
HV conditioned to 22 kV
Will be able to rotate spin to 110 degrees
https://jacow.org/napac2022/papers/wepa20.pdf
Use for Polarization Feedback

## Slide 11: SRF Booster
Booster replaced warm RF Capture and ¼ Cryo-unit:
  Parity-quality beam (MOLLER)
  Matched to 200 keV gun energy
  Resolves coupling
  Mitigate emittance growth
Quantity | Booster | ¼ Cryo-unit
Kinetic Energy | MeV | MeV
 | 0.3 µm rad | 0.5 µm rad
 | 0.2 µm rad | 0.5 µm rad
Coupling Angle |  | 
Deflection |  | 
Quantity | Booster | ¼ Cryo-unit
Kinetic Energy |  | 
 | 0.3 µm rad | 0.5 µm rad
 | 0.2 µm rad | 0.5 µm rad
For more data:
• JLAB-TN-23-005
• https://doi.org/10.18429/ JACoW- NAPAC2022- WEPA12

## Slide 12: Helicity Generator Board
Built 13 boards and distributed to MOLLER
Recent firmware additions:
  New Helicity settings for MOLLER:
    Free Clock Mode at 1920 Hz, 10 µs T_Settle, 510.85 µs T_Stable
    64-window patterns: Thue-Morse-64, 16-Quad, 32-Pair
  Fixed Line-Sync Mode
  Added Soft Reset functionality
Recent hardware changes:
  Changed IA0 and IA1 fiber outputs to Helicity Flip and nHelicity Flip
Board is supported by Jefferson Lab Fast Electronics Group

## Slide 13: Helicity Generator Settings
1
30
29
28
27
…
7
…
1
Switch
Open: Pseudo-random Patterns
Closed: Toggle Pattern
30-Bit Shift Register
Pseudo-random Bit out
Pseudo-random Bit
(0 or 1)
Shift Left
OR
XOR
XOR
XOR

## Slide 14: Helicity Decoder Board
MOLLER fast helicity reversal with delay reporting could cause mis-identification of real helicity of some of events in counting mode (these are random events), diluting measured asymmetry
Board developed by: MOLLER Collaboration (Ohio University), Jefferson Lab Fast Electronics Group and Accelerator Division
Will be used by all data acquisition systems using helicity signals
Board will not reconstruct real helicity or real 30-Bit Shift Register
Board has four input signals: T_Settle, Delayed Helicity, Helicity Pattern, and Pair Sync
For each counting event:
  Now: Delayed Helicity and Pattern are recorded in Rings of helicity-gated SIS3801 Scaler. Offline analysis then attempts to construct real helicity, a complicated process due to delay and randomness of events.
  New Board: board will keep records of helicities spanning last 30 patterns – to be able to construct 30-bit shift register seed of pseudo-random helicity generator – and position within pattern. And for each event, these records are read along with event. Offline analysis (anytime>n-patterns) will calculate real helicity using helicity predictor. Will be able to correctly identify helicity of every event.

## Slide 15: Electron Beam Travel Time
With 10 µs T_Settle time, travel time from photocathode (Pockels Cell) to Hall target becomes relevant. Also, time it takes for helicity board signals to propagate to Laser Hut and to Halls.
It takes electron beam about 4.3 µs per pass to reach Hall.
Total distance at 5 passes is about 6.5 km
Fiber length from Injector Service Building (ISB) IN01B05 to Counting House was measured to be 1705 ft. With n=1.45, it takes 2.5 µs for helicity signals to travel in fibers to Hall DAQ
  All these travel times will be accounted for in this new Helicity Decoder Board such that recorded events have correct helicity at Physics Interaction Time
Built 20 Production Boards, tested and ready for distribution:
  Five in use: 2 MOLLER, 1 Hall B, 1 Hall D, 1 Injector Mott Polarimeter
  Contact Chris Cuevas to get your board

## Slide 16: Decoder Board I/O and Features
Input:
  T_Settle
  Delayed Helicity
  Helicity Pattern
  Pair Sync
  External 250 MHz FADC Clock (ECL) – Board has 250 MHz internal clock
  Trigger and Sync Signals
Output:
  Four NIM helicity outputs: T_Settle, Delayed, Pattern and Pair Sync
  Data words for each trigger event
Add programable common delay (0-32 µs) for input helicity signals:
  To fix time delays due to beam travel time and helicity signal distribution to Hall
  Will be measured for each board in a specific DAQ
  Will sync helicity of beam at Physics Interaction Time in Hall
NIM or Fiber, programmable

## Slide 17: Board Programmable Common Delay
How to set input common time delay:
  Helicity Board: 60 Hz Beam Sync (354 µs)
  Electron Beam: VL, 60 Hz Beam Sync, 50 ns pulses
  First, check relative timing of electron VL Generator and Helicity signal on laser table
  Adjust board common delay to match relative timing at laser table
VL
Generator
RTP
Cell
Delayed
Helicity
Fiber
HV Supply
CEBAF
Hall
Target
DAQ
Helicity Generator
ISB
60 Hz Beam Sync
Real
Helicity
Fiber
Check relative timing
Helicity Decoder Board
Check relative timing
Trigger
Board Common Input Delay (0-32 µs)

## Slide 18: UVA Prototype RTP HV Driver
Use Rubidium-Titanyl-Phosphate (RTP) Pockels cell to produce Right-handed and Left-handed circularly-polarized laser light
Use an opto-diode HV to switch between ±800 V
Switching time µs and ringing amplitude
https://doi.org/10.48550/arXiv.2106.09546

## Slide 19: New JLab RTP HV Driver
Use solid-state switch – MOSFET
Prototype under development and testing
Designed and built by Steven Covert and Jim Kortze

## Slide 20: IA HV Driver and Helicity Magnets Control
New Intensity Attenuator (IA) HV Driver is planned in FY2025
Use ±105 V precision Operational Amplifier
Switching time µs
IA system for each Hall (A, B, C, and D)
New Helicity Magnets controller is planned in FY2025
Switching time µs
Four air-core magnets made of Litz wire are installed in Injector MeV region
KD*P PC
LP
λ/2 WP
LP

## Slide 21: Future Plans
This Run Period:
  Parity-quality beam studies in Injector and Hall A
  Install RTP HV Driver
This coming Scheduled Accelerator Maintenance:
  Install IA HV Driver
  Install Helicity Magnets Control
  Upgrade Isolated Rack of Helicity Generator
  Laser Room Cleanup
Possibility of new 6.8 MeV Wien Filter for polarization feedback