## Slide 1
The eRHIC Interaction Region

## Slide 2
Your Guide:
B. Parker,
BNL-SMD
Time Tunnel
The eRHIC Interaction Region
Try to Envision a Viable Future Layout
Give Overview of Technical Challenges
Finally Look for Feedback/Discussion
Try to Envision a Viable Future Layout
Give Overview of Technical Challenges
Finally Look for Feedback/Discussion
Your Guide:
B. Parker,
BNL-SMD

## Slide 3: eRHIC IR, Version 2.5, Optics Summary
Cold Region
Cold Region
Warm Region
90⁰ phase advance and large b for Crab Cavities
Smaller peak betas to reduce the chromaticity
While magnet apertures differ, the optics are the same for the forward and rear sides.
16 mrad “Dogleg Dipoles”
The Version 2.5 hadron beta function peaks are lower with respect to earlier optics in order to reduce the hadron beam chromaticity.
Neutrals and some forward off-momentum particles are detected within the first warm region shown here.
These optics are designed to be favorable for Crab Cavities.
We could look to design a secondary focus beyond 45 m.
Detection of forward particles after Crab Cavities seems ok.

## Slide 4: eRHIC IR, Version 2.5, Layout Summary
Hadrons
Electrons
Synrad
The hadron beta functions are symmetric but the bending is antisymmetric.
Electron bending comes after the IP in order to avoid synrad background.
IP
Cryostat
Cryostat
Cryostat
Cryostat
Cryostat
Cryostat
Crab Cavities
Crab Cavities
Crab Cavities
Crab Cavities
Warm Quad
Warm Quad
4.5m Region
10 mrad total crossing angle
10 mrad additional electron bending
16 mrad hadron dogleg
16 mrad hadron dogleg has spectrometer function for forward going particles
ZDC
Yellow boxes outline the cold beam tube apertures.

## Slide 5: eRHIC IR, Version 2.5, Forward Layout Details
Strong quadrupole focusing takes place in these, Q1 & Q2 apertures
Strong dipole bending in this B1 aperture
Low field “sweet spot” shielded
regions for incoming electrons in these apertures.
Note that the coordinate system in these figures is aligned with the center of the 4 mrad neutron cone (neutral vector) indicated by the hatched region on the plot.
4 mrad neutron cone acceptance

## Slide 6: Public Service Spot: Magnets & Maxwell Tutorial
¼ Symmetry Bare Quadrupole Coil
The longest range field external field component from a quadrupole falls off as (Rcoil/R)3.
So the external field “remembers” the size of the coil structure.
Higher order harmonics cause the field magnitude in the vicinity of the coil to be even larger.
The quadrupole coil thickness grows according to ln(Router/Rinner) gradient dependence (high field = thick coil).
For yoke fields more than say 2 T, the yoke saturates and field will leak into cutout regions (cannot hide there).
However, note that there is a zero in the coil field distribution close to the middle of the coil structure.
R = 100 mm
Average R = 55.5 mm
For this figure we plot #Scaled_B, the field distribution in the coil structure divided by the maximum field in the coil. At the 100 mm indicated spot #Scaled_B is about -0.2.
By0 Region

## Slide 7: Public Service Spot: Magnets & Maxwell Tutorial
¼ Symmetry Simple Sweet Spot Coil
R = 100 mm
Scaled Vertical Field at Coil Midplane
By/BMAX
X, Y (mm)
Linear on the
inside
Reverses in the coil
Now have zero at X=100 mm
Adding the second outer quadrupole coil show here contributes an additional 11% to overall magnetic field efficiency and slightly decreases the peak field.
But now we have created a field reversal “sweet spot” at the desired, X = 100 mm, location.
The field magnitude grows with distance from the zero crossing sweet spot point. It depends on how large the electron region we must shield whether or not we can use a passive iron shield for the final bit of field reduction.

## Slide 8: Public Service Spot: Magnets & Maxwell Tutorial
Scaled Vertical Field at Coil Midplane
By/BMAX
X, Y (mm)
Zero field inside the passive iron shield
Adding racetrack coils above and below the desired sweet spot region further enhances magnetic field efficiency and decreases the coil peak field.
But having conductor above/below the region of interest can dramatically reduce local field non-linearities and expand the size of the low-field sweet spot region.
This coil configuration has good field quality with little influence from the passive iron shield. Unlike active shielding, these sweet spot coils have the same polarity yielding better efficiency. Optimizing the coil end turn positions is the major remaining challenge.
¼ Symmetry Final Sweet Spot Coil
Racetrack Coil
Racetrack Coil

## Slide 9: eRHIC IR, Version 2.5, Q1 Forward Details
Q1 Version 2.5 Parameters
Magnetic Length = 1.975 m
Main Gradient = 136.9 T/m
Field @ e-Beam < Few Gauss
The Version 2.5 Q1 magnet is longer than before and its aperture had to be increased to maintain desired forward experimental acceptance.
Note that the Q1 sweet spot region comes much closer to the main coil than the previous generic solution.
The Q1 outer coils contribute y36% of the total gradient and the peak field now reaches 6.2 T on the main coil
Field quality is close to 1 x 10-4 at Rref=20mm (i.e. about 1 Unit).
Field inside elongated shielded region is less than 1 gauss in the main body.
Q1, Version 2.5 Optics, Full Model
Coil ends do not preserve the body cross section, so we must carefully optimize end turns. Combining magnetic and superconducting materials, “magnetic cloaking,” may be helpful. https://wiki.bnl.gov/eic/index.php/Magnetic_Cloak

## Slide 10: eRHIC IR Q0 Forward: New Parameters Comparison
Q0 Version 2.5 New Parameters
Magnetic Length = 1.465 m
Main Gradient = -213.0 T/m
Field @ e-Beam < Few Gauss
Q0 Version 2.1 Old Parameters
Magnetic Length = 1.400 m
Main Gradient = -170.0 T/m
Field @ e-Beam < 10 Gauss
An aggressive re-design is in progress in order to support the new, optics Version 2.5, Q0 magnet goals (that is based upon the latest Q1 design work).
Q0, Version 2.1 Optics, Full Model

## Slide 11: eRHIC IR, Version 2.5, Forward Layout Details
Note that the coordinate system in these figures is aligned with the center of the 4 mrad neutron cone (neutral vector) indicated by the hatched region on the plot.
Main Beam 3.5 mrad
4 mrad neutron cone
Q1
Q0
B1
Dp/p = 20% Po
3.5 mrad
ZDC
Forward
Detector
Roman
Pots
Dp/p = 50% Po
Measure as much as possible before the next cold accelerator region.
Q2, has HERA style “butterfly shape chamber”
Q2 Front

## Slide 12: eRHIC IR, Version 2.5, B1 Forward Details
B1 Version 2.5 Parameters
Magnetic Length = 2.9 m
Dipole Field = 4.6 T
Field @ e-Beam < Few Gauss
For those already familiar with the RHIC DX magnet, this is in effect a septum version of that magnet.
Since the external field for a dipole falls off more slowly than from quad, (Rcoil/R)2, and the B1 coil radius is so large, expected that it would be hard to make a sweet spot close to the coil.
But the slower fall-off led to smaller residual field non-linearity over the sweet spot region and there is no need for any Q1-style racetrack coils.
We are constructing a 1 m long Direct Wind version of the inner coil now in FY’15 using LDRD funds.
B1, Version 2.5 Optics, ¼ Symmetry Model
Field Magnitude, |B|, Mapping at the coil in Tesla
With a full 3d model we find that because the B1 end-fields change much less rapidly than for Q1, it is much easier to preserve the sweet spot throughout the magnet ends.
Passive, sweet spot shield is located just outside the main coil

## Slide 13: eRHIC IR, Version 2.5, Rear Side Layout Details
Rear Q0
Rear Q1
Rear B1
Hadrons
Electrons
Synrad
Design provides a small field in these cutout regions in order to give outbound electrons an additional 10 mrad deflection
Avoid large coil fields by keeping hadron apertures small as possible
On the rear side we provide additional aperture for increased acceptance around the e-beam direction
IP
Detector Space

## Slide 14: eRHIC IR, Version 2.5, Q1 Rear Side Details
Cold yoke cutouts at 10 mrad
Main coil and aperture for the incoming hadron beam
Outbound electron and synchrotron radiation beams
Outbound electron and synchrotron radiation beams
Weak dipole coil to deflect outbound electrons and off-momentum particles
Magnetic “septum”
Rear Side: Q1 Yoke Cutaway View

## Slide 15: eRHIC IR, Version 2.5, Q1 Rear Design Details
Main Q1 Coil
Yoke
Yoke
Weak dipole coil to deflect electrons
By Dipole Coil On
By Dipole Coil Off
Plot of By at Q1 Magnet Midplane with Coil & Yoke Structure Overlay
Field in this “septum” is ~1 T
On the rear side we can shrink the hadron aperture and avoid large coil peak fields. So our thin yoke section remains unsaturated and can shield the cutout region.
Weak Dipole Coil

## Slide 16: eRHIC IR, Version 2.5, Continued
Q0
Q1
B1
Q2
Q0
Q1
B1
Q2
Space for electron triplets
Space for electron triplets
Challenge: space for forward detectors
Challenges: cleanly pass the synrad and provide useful rear acceptance
Need different e-beam magnet designs for the rear & forward sides

## Slide 17: eRHIC IR, Version 2.X Optics, Options and Opportunities
The eRHIC optics and layout shown is optimized for clean forward separation between neutrals and off-momentum charged particles @ 0.8PO in a dedicated warm beam line section.
Do you anticipate any scenario where detecting forward particles with momenta closer to PO becomes important?
With the production of prototype magnets we are exploring the limits of superconducting magnet technology (e.g. the work with Dejan Trbojevic on optics to reduce peak betas).
Even for conventional (warm) magnets we need to continue iterating the IR layout an magnet parameters with feedback from experiments in order to ensure that everything works (e.g. here are rear side e-beam magnet apertures etc.).
Is the 10 mrad downstream bending useful or does it cause more problems than it solves?
X
This quad is almost off.
Shift Crab Cavities closer.
Create a secondary focus?
Redo the matching to arcs.