## Slide 1: Development of μRGroove detectors
Siqi He
On behalf of UTSC-MPGD Group
2025 SoLID Collaboration Meeting , Jan-10-2025

## Slide 2: Outline
Introduction
10cm×10cm μRGroove
50cm×50cm μRGroove
Low-mass Cylindrical μRGroove
Summary & Outlook

## Slide 3
Large area MPGD for trigger/tracking
  ATLAS New Small Wheel Micromegas:
    Production complication of Bulk production
    Cluster rate: 6-7kHz/cm2 at small radius area
    99% tracking efficiencies while single layer efficiency is ~80 - 90%
    Average spatial resolution reconstructed by CC: ~350μm
CERN-LHCC-2013-006, ATLAS-TDR-020
MM chamber in ATLAS NSW
Sala, ATLAS NSW performance studies, Pisa Meeting 2024

## Slide 4
CERN-LHCC-2015-012, CMS-TDR-013
  CMS Forward Muon System GEM:
    mechanical limitation of Self-stretch process
    Expected hit rate: 2-144kHz/cm2
    average efficiency is ~93.8%
    Spatial resolution of prototype: ~267μm
Large area MPGD for trigger/tracking
GEM chamber in CMS MS
Archana, Experience with the Triple-GEM detectors at the LHC CMS experiment, Pisa Meeting 2024

## Slide 5
Large area MPGD for trigger/tracking
G. Bencivenni at J.Phys.Conf.Ser. 1498 (2020) 012003
  micro-Resistive WELL:
    Single stage MPGD without tension requirement
    Simple structure and Easy assembly
    Various prototypes: Good spatial resolution (<100μm) and High rate capability (1~10MHz/cm2)
μRWELL
Matteo at, The μ-RWELL for future HEP challenges, MPGD2024

## Slide 6
micro-Resistive Groove
  QMM > QμRWELL: less parasitic capacitance of readout strips and longer drift distance of the avalanche charge for MM.
  Large area means much larger capacitance which will significantly reduce signal amplitude.
  X and Y readout strips of 2D strip-readout MPGD only receiving ~50% of the total induced charge.
  The cathode of μRGroove itself can be used as 1D-readout strip.
    Decoupled X&Y readout strips, no induced charge sharing effect, increased signal amplitude.
    Compatible with all the techniques developed for the μRWELL manufacture.
    Easy clean, which is one of the most important performance for the end user.
Siqi He, RD51 Mini-Week, 02/27/2023
μRGroove
L. Scharenberg et al 2024 JINST 19 P05053

## Slide 7
10cm×10cm μRGroove
  Two version prototypes of 10cm×10cm
  Groove pitch: 200μm, 2 grooves are connected as 1 X strip
  For 2D-version, Y pitch: 400μm, Y width: 260μm
  For 3D-version, Y/V pitch: 400μm, Y/V width: 60μm/350μm angle of YV: 45°
  To verify μRGroove structure and charge sharing effect.
2D-readout (XY) μRGroove
X strips
Y strips
3D-readout (XYV) μRGroove
X strips
Y strips
V strips

## Slide 8
Effective Gain and energy resolution
XY-μRGroove
Gas: Ar/iC4H10 (95/5)
Source: 8.1keV Cu X-ray
Effective gain up to 104
(by signal amplitude spectrum)
Energy resolution is about 25%
As the drift electric field becomes larger, the gain increases almost linearly, and the energy resolution remains unchanged.

## Slide 9
Induced charge sharing effect
For 2D-μRGroove with this Layerstack, 2DQY ≈ 2DQx
For 3D-μRGroove with this Layerstack, 3DQY + 3DQV ≈ 2DQY ≈ 3DQX
When the distance from the top and bot readout to the DLC is different, the induced charge will be different.
Avoiding the charge sharing can significantly increase the induction signal.

## Slide 10
Detection efficiency & Spatial resolution
The combined efficiency is about 95.6% and enter plateau at ~430V
Spatial resolution is better than 80μm
Charge radio of X/Y is about 1.89
Only X and Y readout is tested with V-strip float at first .
Drift: 2kV/cm
Gas gap: 5mm
The combined efficiency is about 97.9% and enter plateau at ~410V
Spatial resolution is ~76μm for X readout and 70μm for Y readout
Charge radio of X/Y is about 1.013
2D-μRGroove
X strips
Y strips
~1°
Incomplete alignment results in slightly worse spatial resolution for X strips
3D
2D
at CERN SPS beamline

## Slide 11
50cm×50cm 2D-μRGroove
The central 10cm×10cm area is connected to the electronic system for testing with the rest readout strips grounded
Same setup of beam test
2 readout strips are replaced by a PEP GND line in each 128 readout strips;
Dead Area (TOP): 2/128=1.5625%

## Slide 12
Beam test of 50cm×50cm μRGroove
The combined efficiency is about 96.9% and enter plateau at ~450V
Spatial resolution is ~93μm for X readout and ~81μm for Y readout
Charge radio of X/Y is about 1.049
Drift electric field is 2kV/cm with 5mm gas gap.
Much Larger capacitance causes smaller signal amplitude at the same working voltage and higher voltage entering plateau.
Incomplete alignment results in worse spatial resolution for X strips

## Slide 13
Rate capability of Fast-grounding μRWELL
Matteo, Update on Technology Transfer of µ-RWELL , Last RD51 Collaboration Meeting
Fast Grounding is the key design for high rate capability
Fast grounding μRWELL:
PEP-groove design
PEP-dot design
Similar to 50cm×50cm μRGroove

## Slide 14
For both designs，rate capability >10MHz/cm2
Rate capability of Fast-grounding μRWELL

## Slide 15
Still ongoing
Rate capability of Fast-grounding μRGroove
2 readout strips are replaced by a PEP GND line in each 128 readout strips;
50cm×50cm μRGroove is designed as PEP-groove fast grounding.
Testing will be conducted and hopefully similar results will be obtained

## Slide 16
Max size：D=323.8mm，L=847mm
Material budget:  0.5%X0
Spatial resolution by CC method(<5): 200μm
Detection efficiency for MIP：95%
BESIII c-GEM
Size：D=168.5mm，L=600mm
Material budget:  0.6%X0
Spatial resolution by CC method(<3): 460μm
Detection efficiency for MIP：>95%
INFN-LNF c-RWELL prototype
Max Size：D=207.5mm，L=712mm
Material budget: No public data found yet
Spatial resolution: 432μm (5T)
Detection efficiency：90%
CLAS12 c-Micromegas
Low-mass Cylindrical MPGD

## Slide 17
A Cylindrical μRGroove prototype
Drift HV
DLC HV
V readout
U readout
1st C-μRGroove prototype for STCF-ITKW:
  Size of active area: D=131.0mm, L=100.0mm;
  Out cylinder is drift and inner is μRGroove-PCB
  Both cylinders contain independent support structures
  Detachable mechanical design
  Low-mass electrode design
1st Prototype
Total material budget: ~0.23%X0

## Slide 18
Gain and energy spectrum measurement
Setup：
  Gas: Ar:iC4H10/95:5
  Source: 55Fe
  Readout from X strips (cathode)
  V strips are grounded
  Ortec142AH/671 + MCA
  Gain measured by signal amplitude spectrum
Energy resolution: 26%;
Effective gain: 4000~10000;
Similar signal amplitude on X&V readout strips;
Good stability if the humidity can keep low enough;
~1h@gain : 5100
3 sectors not work (8 sectors in total);
Bad gain uniformity, caused by the gas(flow);

## Slide 19
Beam test
Setup：
  Gas: Ar:CF4:CO2/45:40:15
  Readout from U strips (top cooper of μRGroove)
  V strips are grounded
  3 micromegas trackers
  APV25+SRS+mmDAQ
C-
MM1
MM3
C-μRGroove
465mm
646mm
925mm
0mm
MM2
2024. 06-07
C-μRGroove

## Slide 20
Detection efficiency and spatial resolution
Spatial resolution for perpendicular tracks: 83~93μm.
Detection efficiency >95%.
  Charge Center of gravity(CC) for perpendicular tracks
Find the middle area.
Alignment and rotation correction
Position correction of circular surface
Wrinkles may degrade spatial resolution
reconstructed position
truth hit position
: middle point
  After correction

## Slide 21
First result of micro-TPC
Constant ratio timing
Position correction of circular surface
Alignment
&rotation cor.
Time advanced
correction
A algorithm of μTPC has been developed
with the incident angle is >8°, the spatial resolution obtained by the μTPC is better(~114μm).
μTPC

## Slide 22: Summary
10cm×10cm planar μRGroove
  Maximum Gain > . Energy resolution ~25% with nice stability
  Combined efficiency is about 95.6% for 3D-version and 97.9% for 2D-version
  Spatial resolution is about 70-80μm for both versions.
50cm×50cm planar μRGroove
  Combined efficiency is about 96.9%
  Spatial resolution is better than 100μm
1st Cylindrical μRGroove
  Max gain is 4000-10000, Energy resolution ~26% at first test.
  For perpendicular tracks: Detection efficiency >95%, spatial resolution <100μm
  For oblique incident tracks: preliminary result of μTPC is ~120μm

## Slide 23: Outlook
Test the rate capability of 50cm×50cm μRGroove
Develop μTPC algorithm and Analyze beam data of C-μRGroove beam test in magnetic fields
Improve the C-μRGroove prototype, mainly about uniformity and wrinkle issues
Optimize the detector structure, such as Thick-μRGroove (with 75μm APICAL)
Gap=5mm
Pitch=200μm
Width=90/70μm
Thickness=75μm
DLC ~50MΩ/□
75μm-Thick μRGroove

## Slide 24: Backup

## Slide 25: Super Tau-Charm Facility
STCF is an e + e- collider operating at =2～7 GeV with a peak luminosity of cm-2s-1.
Track detection under extremely high luminosity requires the ITK performance includes:
  Ultra-Low Material Budget (<0.3%X0)
  Good Spatial resolution (<100μm)
  Handle high occupancy operated in μTPC mode
  ……
Detector Candidates: μRGroove
Possible Solutions：
Cylindrical MPGDs
LINAC
400 m
Collider Ring
1000m
Detector
Damping Ring
150 m

## Slide 26
Beam test: Setup
Beam line: SPS - H4
Particle: 150GeV/c Muon
Electronics: SRS + APV25 + mmDAQ
μRGroove gas: Ar/iC4H10 (90/10)
Micromegas trackers gas: Ar/CO2 (93/7)
μRGroove

## Slide 27
C-μRGroove: Low-Mass Electrode
LM Drift & GND are both made
Zhou Lin, RD51 Collaboration Meeting, 21/06/2023
DLC: Diamond Like Carbon

## Slide 28
C-μRGroove: Manufacture
Drift electrode
Rohacell foam
Kapton/GND
Kapton/GND
Rohacell foam
V strip film
Det.&U-strip film
Total material budget: ~0.23%X0

## Slide 29
C-μRGroove: Electrodes design
μRGroove/U Strips
V Strips
Layer stack of μRGroove
Layer stack of V readout
U/V 2D strip-readout, pitch of U strips is 0.4mm, Pitch of V strips is 0.8mm, angel between UV is 15

## Slide 30
Beam test with magnetic filed
Magnet
μRgroove1&2
μRgroove3
C-μRGroove
143mm
493mm
663mm
0mm
Setup：
  Gas: Ar:CF4:CO2/45:40:15
  Readout from X strips (cathode)
  V strips are grounded
  APV25+SRS+mmDAQ
  Distance between forward and backward triggers is ~8m
  3 μRGroove trackers
  0.5-1.5Tesla magnetic filed
2024. 09-10

## Slide 31
Beam test with magnetic filed
0 Telsa
1 Telsa
For perpendicular tracks, CC method
For 150GeV/c muon,
@B=1T
Spatial resolution is ~94μm as a reference @B=0T
For perpendicular tracks, CC method
Spatial resolution is ~400μm
Bias: ~1.592mm, sigma: ~400μm
Lorenz angle: ~17.7°
Trackers’ hit map shift caused by long distance between triggers.
Further analysis based on μTPC needed

## Slide 32
The Size of 3-layer ITKW
Size of active area:
Layer0: D=131.0mm, L=100.0mm;
Layer1: D=131.0mm, L=380.0mm;
Layer2: D=229.4mm, L=650.0mm;
Layer3: D=327.9mm, L=920.0mm;