## Slide 1: Update on Ce+BAF Injector Baseline Simulations
Concept of e+ injector
Simulation of e+ capture
Design of energy selection chicane
Results of start-to-end e+ beam tracking
A. Ushakov, J. Benesch, J. Grames, S. Ogur, V. Lizarraga-Rubio,
R. Rimmer, Y. Roblin, D. Turner, S. Wang
Jefferson Lab

## Slide 2: Pol. e+ Injector Critical Risk Areas mA e‒ Source, High Power Targets, Capture Cavity
Conceptual Development
Improve design of e+ injector
Develop pCDR
High current e‒ source (<10 mA @ 10 MeV)
Up to 90% polarization
Long life time
Target Test Area
S. Habet, PhD Thesis, Dec 2023
 | Simul. | Goal
Energy [MeV] | 123 | 
Current [nA] | 170 | > 50
Polarization [%] | 65 | > 60
[%] | 0.6 | < 1
[ps] | 2 | < 4
[m·rad] | 1.5e-3 | < 4e-5
 | Simul. | Goal
Energy [MeV] | 123 | 
Current [nA] | 170 | > 50
Polarization [%] | 65 | > 60
 | 0.6 | < 1
 | 2 | < 4
 | 1.5e-3 | < 4e-5
Scheme of e+ Injector at LERF
JLab LDRD “A high-intensity, polarized-beam prototype photogun for the Ce+BAF positron source”, PI: M. Bruker, proposal awarded, FY25-FY26

## Slide 3: Simulation Model of e+ Injector
Start-to-end simulations (Geant4 + elegant)
e+ generated by 1 mA @ 120 MeV e- in W target with thickness of 4 mm
Considered NC and SC focusing solenoids
NC SW standing wave capture cavity
Added quads to energy selection chicane
Added matching sections before and after chicane
e+ accelerated to 123 MeV in C100 cryomodule
Bunch compression is not yet implemented/studied
Scheme of e+ Injector

## Slide 4: Simulation Model of e+ Injector
Different NC and SC options for focusing solenoid
  1.6 T NC solenoid with 41 cm coil length (field map provided by Jay Benesch)
  2.5 T SC solenoid with 25 cm length (simplified model, elegant)
Capture cavity: 1.497 MHz, 11 cells, 4 cm iris radius, 4 MV/m
Chicane:
  Bending angle of rectangular dipoles: 0.2 rad
  5 cm quad half width, 5 cm radius of beam pipe
  Rectangular collimators: 1.5 cm X half width, 5 cm Y half width
41 cm Coil Solenoid
1.24 m Target to Cavity Distance
Cavity with 4 cm Aperture Radius
Field Profile on Beam Axis
Concept of Focusing and Bucking Solenoids (Jay Benesch)
Target

## Slide 5: Capture with NC and SC Solenoid #1 and NC Cavity inside NC Solenoid #2
Steps used for design of energy selection chicane:
Calculated Twiss parameters at exit of capture cavity for 60 MeV or 20 MeV positrons
Defined chicane parameters (typically at chicane entrance beta X = 3 m, beta Y = 1 m, maximal dispersion at middle of chicane and low dispersion at start and end)
Calculated required parameters of matching section
Tracked all positrons and optimized phase of SRF for lowest energy spread and highest e+ current
 | Target | NC Sol. #1 with 41 cm Coil |  |  | 25 cm SC Solenoid #1 |  | 
γ | Ne+ | B1Sol | B2TW | N2TW | B1Sol | B2TW | N2TW
Δγ/γ = ±0.1 | Target Exit |  |  | NC Cavity Exit |  |  | NC Cavity Exit
 | e+/10M e- | T | T | e+/10M e- | T | T | e+/10M e-
120 | 51530 | 1.615 | 0.901 | 43389 | 2.500 | 0.463 | 40189
40 | 172960 | 0.542 | 0.321 | 82840 | 0.868 | 0.130 | 60015

## Slide 6: Momentum-Time Distribution at End of NC Capture Cavity (NC Solenoid)
High Polarization Mode
Capture of 60 MeV e+ at Target
High Current Mode
Capture of 20 MeV e+ at Target

## Slide 7: XX’ Distribution at End of NC Capture Cavity (NC Solenoid)
High Polarization Mode
High Current Mode

## Slide 8: Momentum vs X before Collimator #1 (NC Solenoid)
High Polarization Mode
High Current Mode

## Slide 9: Momentum-Time Distribution before C100 (NC Solenoid)
High Polarization Mode
High Current Mode

## Slide 10: Momentum-Time Distribution after C100 (NC Solenoid)
High Polarization Mode
High Current Mode

## Slide 11: XX’ Phase Space before C100 (NC Solenoid)
High Polarization Mode
High Current Mode

## Slide 12: XX’ Phase Space after C100 (NC Solenoid)
High Polarization Mode
High Current Mode

## Slide 13: e+ Current along Beamline for Source with NC Solenoid and Ie- = 1 mA
High Polarization Mode
High Current Mode
221 nA
405 nA

## Slide 14: Energy Spread along Beamline (NC Solenoid)
High Polarization Mode
High Current Mode
0.6%
1.4%

## Slide 15: Bunch Length along Beamline (NC Solenoid)
High Polarization Mode
High Current Mode
3.8 mm
5.4 mm

## Slide 16: NC and SC Solenoids for Capture of 60 MeV e+ (High Polarization Mode)
 | NC Sol. #1 with 41 cm Coil Length |  |  |  | SC Sol. #1 with 25 cm Length |  |  | 
 | B1 = 1.615 T and B2 = 0.9 T |  |  |  | B1 = 2.5 T and B2 = 0.463 T |  |  | 
 | e+ Current | dE/E | Bunch Length | Norm. Emi X | e+ Current | dE/E | Bunch Length | Norm. Emi X
 | [nA] | [%] | [mm] | [mm·rad] | [nA] | [%] | [mm] | [mm·rad]
NC Cavity | 19245 | 35.0 | 65.0 | 45.2 | 38494 | 31.2 | 18.2 | 82.9
Matching Section | 7483 | 32.6 | 25.8 | 25.5 | 9532 | 28.3 | 9.8 | 36.7
Chicane + Matching | 450 | 2.8 | 4.1 | 4.0 | 785 | 4.1 | 5.2 | 4.2
C100 | 221 | 0.6 | 3.8 | 1.8 | 261 | 0.8 | 5.1 | 2.2
Positions and dimensions of magnets and cavities were kept the same except for solenoid #1

## Slide 17: NC and SC Solenoids for Capture of 20 MeV e+ (High Current Mode)
 | NC Sol. #1 with 41 cm Coil Length |  |  |  | SC Sol. #1 with 25 cm Length |  |  | 
 | B1 = 0.542 T and B2 = 0.32 T |  |  |  | B1 = 0.868 T and B2 = 0.13 T |  |  | 
 | e+ Current | dE/E | Bunch Length | Norm. Emi X | e+ Current | dE/E | Bunch Length | Norm. Emi X
 | [nA] | [%] | [mm] | [mm·rad] | [nA] | [%] | [mm] | [mm·rad]
NC Cavity | 17487 | 46.0 | 52.4 | 26.9 | 16756 | 35.0 | 82 | 51
Matching Section | 4258 | 41.7 | 19.6 | 6.8 | 7777 | 23.7 | 6.1 | 11
Chicane + Matching | 497 | 4.2 | 7.3 | 1.9 | 982 | 3.7 | 4.9 | 1.6
C100 | 405 | 1.4 | 5.4 | 1.1 | 659 | 1.4 | 5.1 | 1.2
Positions and dimensions of magnets and cavities were kept as for capture of 60 MeV e+
Field strength of magnets and cavities have been adjusted for optimal capture of 20 MeV e+ (highest current at the end of e+ beamline)

## Slide 18: Emittance at End of e+ Beamline
High Polarization Mode
High Current Mode

## Slide 19: Would an Emittance Filter Help to Improve other Beam Parameters?
High Polarization Mode
High Current Mode
Polarization does not depend on emittance

## Slide 20: Polarization vs Energy at End of e+ Injector
High Polarization Mode
High Current Mode
Polarization of drive e‒ beam of 90%

## Slide 21: Summary and Outlook
We are working on concept of e+ injector
Realistic field of capture solenoid has been used
Different capture solenoids (NC and SC) were considered
Start-to-end tracking was performed
Next steps
Continue optimization of e+ beamline
Design bunch compressor
Design emittance filter (beam cooling system)

## Slide 22
Backup Slides

## Slide 23: Dispersion along Beamline (NC Solenoid) and Kept Low at End
High Polarization Mode
High Current Mode
Dipole:

## Slide 24: e+ Exiting Target Captured and Transported up to the End of C100
High Polarization Mode
High Current Mode

## Slide 25: Distribution of Power Deposed by 1 mA @ 120 MeV e‒ Beam (FLUKA)
 | Power [kW]
Target | 18.11
Compensation Solenoid | 0.74
Coil of Main Solenoid | 0.02
Iron of Main Solenoid | 0.06
W10Cu Absorber inside Main Solenoid | 18.88
TZM Absorber (99.4% Mo, 0.5% Ti, 0.1% Zr) | 58.66
W10Cu Absorber upstream Cavities | 12.50
Solenoid around Cavity | 0.12
Cu Cavities | 6.50
Total Absorbed Power | 115.56 (96.3%)
Beam Power at z = 275 cm, r < 3cm | 3.20
 | Photons | Electrons | Positrons
Yield per primary e- | 0.123 | 0.029 | 0.005
Mean Energy [MeV] | 12.7 | 49.6 | 35.7
Power [kW] | 1.57 | 1.44 | 0.19
Fraction in Total Beam Power | 49.1 | 44.9 | 6.0
Cu Coil
W10Cu
W10Cu
TZM
Target
Cu Cavity*
Steel
Cu Coil
Compensation
Solenoid