## Slide 1
Pablo Campero, Brian Eng, Mindy Leffel, Mary Ann Antonioli, and DSG
EIC Ansys Fluent Simulation Report Tuesday, July 15, 2025

## Slide 2: Table of Contents
Glossary
Simulation Model
System Information
Geometry and Mesh
  Mesh Size
  Mesh Quality
  Orthogonal Quality
Simulation Setup
  Models
  Material Properties
  Cell Zone Conditions
  Boundary Conditions
  Reference Values
  Solver Settings
Run Information
Solution Status
Report Definitions
  Residuals
  Report Plots
Contours
XY Plots

## Slide 3: Glossary
Acronyms used in the report are as follows:
CFD: Computational Fluid Dynamics
EIC : Electron Ion Collider
HD: Hadron Direction
LD: Lepton Direction
HCAL: Hadron Calorimeter
EMCAL: Electromagnetic Calorimeter
pfRICH: Proximity Focusing Ring Imagining Cherenkov
MPGD: Micro Pattern Gaseous Detector
TOF: Time Of Flight
dRICH: Dual-radiator Ring Imaging Cherenkov

## Slide 4: Simulation Model
Table of contents
3D model consists of the beampipe, 22 detectors, and an enclosure
For simplicity, detectors in the model were represented by cylinders, allowing a CFD thermal simulation manageable by current DSG computing resources
Silicon Barrel
HD-MPGD1
HD-MPGD2
HD-TOF-Tracker
HD-dRICH
HD-EMCAL
HD-HCAL
LD-MPGD2
LD-MPGD1
LD-Si-Disks 1–5
LD-pfRICH
LD-EMCAL
LD-HCAL
Beampipe
Enclosure
HD-Si-Disks 1–5

## Slide 5: System Information
Application | Fluent
Settings | 3D, double precision, pressure-based, SST (Shear Stress Transport) k-omega
Version | 25.1.0-10210
Source Revision | 3b709034ad
Build Time | Nov 26, 2024, 13:29:29 EST
CPU | Intel(R) Xeon(R) W-2255
OS | Windows
Table of contents
System Information
Provides details of operating system specifications, computer hardware specifications, Fluent solver method, and turbulence option used in the simulation

## Slide 6
Table of contents
Geometry and Mesh
Geometry and Mesh
Provide mesh metrics e.g. orthogonal quality for each model component—parameters that impact the simulation’s accuracy and stability.
Cells | Faces | Nodes
3585654 | 19456336 | 14074310
The total number of cells, faces between cells, and nodes are generated based on the geometry complexity, desired mesh quality, and computer resources available.
The minimum mesh cell size was set to 2.5 mm, three layers between fluid and solid domains were set, and polyhedral mesh type was selected for the volume mesh.
Mesh Size

## Slide 7: Mesh Quality
Name | Type | Min orthogonal quality | Max aspect ratio
beampipe-air-vol-solid | Poly Cell | 0.29404524 | 21.991253
enclosure-enclosure | Poly Cell | 0.28000452 | 52.157037
ld-hcal | Poly Cell | 0.39569447 | 21.983108
ld-emcal | Poly Cell | 0.39628022 | 22.675015
ld-pfrich | Poly Cell | 0.39160157 | 22.416554
ld-mpgd-2 | Poly Cell | 0.39728688 | 16.532249
ld-mpgd-1 | Poly Cell | 0.39788986 | 15.997825
ld-disk-5 | Poly Cell | 0.39874376 | 17.809741
ld-disk-4 | Poly Cell | 0.3986958 | 17.414631
ld-disk-3 | Poly Cell | 0.39936739 | 17.267653
ld-disk-2 | Poly Cell | 0.39941434 | 17.362587
Table of contents
Geometry and Mesh / Mesh Quality (1 of 2)
Minimum orthogonal quality ranges from 0 (unacceptable) to 1 (excellent). The volume mesh was improved by setting a limit for the minimum orthogonal quality to 0.280 (Good).
The aspect ratio is defined as a measure of the stretching of a cell based on the distance from the mesh cell centroid. Good quality mesh typically has an aspect ratio of ≤ 5 in the main flow region. While ideal aspect ratio is close to 1, higher values, even up to 100 or more, are acceptable.

## Slide 8: Mesh Quality, cont.
ld-disk-1 | Poly Cell | 0.39823703 | 15.807447
silicon-barrel | Poly Cell | 0.28002688 | 53.932512
hd-disk-5 | Poly Cell | 0.39719451 | 17.044787
hd-disk-4 | Poly Cell | 0.39533213 | 17.626022
hd-disk-3 | Poly Cell | 0.39916414 | 17.960018
hd-disk-2 | Poly Cell | 0.39328678 | 17.067598
hd-disk-1 | Poly Cell | 0.39718753 | 16.875494
hd-mpgd-1 | Poly Cell | 0.39908895 | 17.412726
hd-mpgd-2 | Poly Cell | 0.39888267 | 17.542956
hd-tof-tracker | Poly Cell | 0.28265144 | 28.984702
drich | Poly Cell | 0.38914986 | 22.331797
hd-emcal | Poly Cell | 0.39788475 | 21.993974
hd-hcal | Poly Cell | 0.29857456 | 22.129507
Table of contents
Geometry and Mesh / Mesh Quality (2 of 2)

## Slide 9: Orthogonal Quality
Table of contents
Geometry and Mesh / Orthogonal Quality
A histogram provides a visual representation of the distribution of orthogonal quality values across the mesh. The x-axis represents the range of the orthogonal quality values, typically from 0 to 1 and the y-axis represents the count of cells within each quality value.
As shown in the figure below, the well-distributed histogram with a high concentration of bars at the higher end (closer to 1) indicates a good mesh quality for the EIC model.

## Slide 10
Table of contents
Simulation Setup
Simulation Setup
Provides information for:
Physics data, which includes material properties used for each model component, cell zone conditions, and boundary conditions—velocity and temperature, and heat transfer conditions for inner and outer walls of each element of the model.
Solver settings includes the lists of the enabled equations, pseudo-time explicit relaxation factors, and the discretization scheme.

## Slide 11: Models
Model | Settings
Space | 3D
Time | steady state
Viscous | SST k-ω turbulence model
Heat transfer | enabled
Radiation | surface-to-surface
Table of contents
Simulation Setup / Physics / Models
The steady state model assumes that flow conditions and properties remain constant with respect to time, meaning the solution doesn't change over time.
The viscous model allows set parameters for turbulent flow. The Shear Stress Transport (SST) K-ω turbulence model selected is a low-Reynolds-number model, which can handle flows near the wall without needing additional wall functions. This model solves two transport equations, one for turbulent kinetic energy (k) and one for specific dissipation rate of energy (ω).
The surface-to-surface radiation model can account for the radiation exchange in an enclosure of gray-diffuse surfaces. The energy exchange between two surfaces depends in part on their size, separation distance, and orientation.

## Slide 12: Material Properties
Fluid |  |  |  | 
 | air |  |  | 
Density | boussinesq |  |  | 
Cp (specific heat) | 1006.43 J/(kg K) |  |  | 
Thermal conductivity | 0.0242 W/(m K) |  |  | 
Viscosity | 1.7894e-05 kg/(m s) |  |  | 
Thermal expansion coefficient | 0.0034 K^-1 |  |  | 
Solid |  |  |  | 
 | silicon | beryllium | carbon fiber | aluminum
Density | 2330 kg/m^3 | 1850 kg/m^3 | 1750 kg/m^3 | 2719 kg/m^3
Cp (specific heat) | 700 J/(kg K) | 1825 J/(kg K) | 750 J/(kg K) | 871 J/(kg K)
Thermal conductivity | 148 W/(m K) | 190 W/(m K) | 15 W/(m K) | 202.4 W/(m K)
Table of contents
Simulation Setup / Physics / Material Properties (1 of 2)
Bossinesq approximation was set for the air density as it is recommended for natural convection problems involving small temperature changes. It simplifies the density calculations by assuming the density change is directly proportional to the temperature change.

## Slide 13: Cell Zone Conditions
Fluid |  | 
 | beampipe-air-vol-solid | enclosure-enclosure
Material name | air | air
Specify source terms? | no | no
Specify fixed values? | no | no
Frame motion? | no | no
Laminar zone? | no | no
Porous zone? | no | no
3D fan zone? | no | no
Table of contents
Simulation Setup / Physics / Cell Zone Conditions (1 of 2)
Defines the properties and behavior of individual fluid or solid volumes, indicates which element is set as solid or fluid, the material assigned for each element, if the element is in motion or static, and if the element is a heat of source for thermal simulation.

## Slide 14: Cell Zone Conditions, cont.
Solid |  |  |  |  | 
Detector | Material name | Specify source terms? | Specify fixed values? | Frame motion? | Solid motion?
ld-hcal | aluminum | no | no | no | no
ld-emcal | aluminum | no | no | no | no
ld-pfrich | carbon fiber | no | no | no | no
ld-mpgd-2 | carbon fiber | no | no | no | no
ld-mpgd-1 | carbon fiber | no | no | no | no
ld-si-disks 1-5 | carbon fiber | no | no | no | no
silicon barrel | silicon | no | no | no | no
hd-si-disk 1-5 | carbon fiber | no | no | no | no
hd-mpgd-1 | carbon fiber | no | no | no | no
hd-mpgd-2 | carbon fiber | no | no | no | no
hd-tof-tracker | carbon fiber | no | no | no | no
hd-dRICH | carbon fiber | no | no | no | no
hd-emcal | aluminum | no | no | no | no
hd-hcal | aluminum | no | no | no | no
Table of contents
Simulation Setup / Physics / Cell Zone Conditions (2 of 2)

## Slide 15: Boundary Conditions
 | Beampipe Inlet | Beampipe Outlet
Velocity specification method | magnitude, normal to boundary | 
Reference frame | absolute | 
Velocity magnitude [m/s] | 5 | 
Supersonic/initial gauge pressure [Pa] | 0 | 
Temperature [C] | 110 | 
Turbulence specification method | intensity and viscosity ratio | 
Turbulent intensity [%] | 5 | 
Turbulent viscosity ratio | 10 | 
External black body temperature method | boundary temperature | boundary temperature
Internal emissivity | 1 | 1
Participates in view factor calculation? | yes | yes
Flow rate weighting |  | 1
Table of contents
Simulation Setup / Physics / Boundary Conditions (1 of 19)
Provides information about conditions for the beampipe inlet and outlet, such as set velocity, temperature, and pressure, and heat transfer conditions for all walls/surfaces of each model element

## Slide 16: Boundary Conditions, cont.
Beampipe walls | right-inner | left-side-inner | mid-sec-inner | air-sides | right-inner-shadow | left-inner-shadow
Wall thickness [mm] | 1 | 1 | 3 | 1 | 1 | 1
Heat generation rate [W/m^3] | 0 | 0 | 0 | 0 | 0 | 0
Material name | aluminum | aluminum | beryllium | beryllium | aluminum | aluminum
Thermal BC type | coupled | coupled | coupled | coupled | coupled | coupled
Enable shell conduction? | no | no | no | no | no | no
Wall motion | stationary | stationary | stationary | stationary | stationary | stationary
Shear boundary condition | no slip | no slip | no slip | no slip | no slip | no slip
Wall surface roughness | standard | standard | standard | standard | standard | standard
Internal emissivity | 0.15 | 0.15 | 0.18 | 0.18 | 0.15 | 0.15
Wall roughness height [mm] | 0 | 0 | 0 | 0 | 0 | 0
Table of contents
Simulation Setup / Physics / Boundary Conditions (2 of 19)

## Slide 17: Boundary Conditions, cont.
Beampipe walls, cont. | right-inner | left-side-inner | mid-sec-inner | air-sides | right-inner-shadow | left-inner-shadow
Wall roughness constant | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
Radiation BC type | opaque | opaque | opaque | opaque | opaque | opaque
Participates in view factor calculation? | yes | yes | yes | yes | yes | yes
Faces per surface cluster | 1 | 1 | 1 | 1 | 1 | 1
Convective augmentation factor | 1 | 1 | 1 | 1 | 1 | 1
Table of contents
Simulation Setup / Physics / Boundary Conditions (3 of 19)

## Slide 18: Boundary Conditions, cont.
Enclosure walls | outer | right | left
Wall thickness [mm] | 0 | 0 | 0
Heat generation rate [W/m^3] | 0 | 0 | 0
Material name | aluminum | aluminum | aluminum
Thermal BC type | convection | heat flux | heat flux
Heat flux [W/m^2] |  | 0 | 0
Convective heat transfer coefficient [W/(m^2 K)] | 10 |  | 
Free stream temperature [C] | 20 |  | 
Enable shell conduction? | no | no | no
Wall motion | stationary | stationary | stationary
Shear boundary condition | no slip | no slip | no slip
Wall surface roughness | standard | standard | standard
Table of contents
Simulation Setup / Physics / Boundary Conditions (4 of 119)

## Slide 19: Boundary Conditions, cont.
Enclosure walls, cont. | outer | right | left
Internal emissivity | 0.15 | 1 | 1
Wall roughness height [mm] | 0 | 0 | 0
Wall roughness constant | 0.5 | 0.5 | 0.5
Radiation BC type | opaque | opaque | opaque
Participates in view factor calculation? | yes | yes | yes
Faces per surface cluster | 1 | 1 | 1
Convective augmentation factor | 1 | 1 | 1
Table of contents
Simulation Setup / Physics / Boundary Conditions (5 of 19)

## Slide 20: Boundary Conditions, cont.
LD-HCAL walls | side | outer | inner | side-shadow | outer-shadow | inner-shadow
Wall thickness [mm] | 0 | 0 | 0 | 0 | 0 | 0
Heat generation rate [W/m^3] | 0 | 0 | 0 | 0 | 0 | 0
Material name | aluminum | aluminum | aluminum | aluminum | aluminum | aluminum
Thermal BC type | coupled | coupled | coupled | coupled | coupled | coupled
Enable shell conduction? | no | no | no | no | no | no
Wall motion | stationary | stationary | stationary |  |  | 
Shear boundary condition | no slip | no slip | no slip |  |  | 
Wall surface roughness | standard | standard | standard |  |  | 
Internal emissivity | 0.15 | 0.15 | 0.15 |  |  | 
Wall roughness height [mm] | 0 | 0 | 0 |  |  | 
Wall roughness constant | 0.5 | 0.5 | 0.5 |  |  | 
Radiation BC type | opaque | opaque | opaque | opaque | opaque1 | opaque
Participates in view factor calculation? | yes | yes | yes |  |  | 
Faces per surface cluster | 1 | 1 | 1 |  |  | 
Convective augmentation factor | 1 | 1 | 1 | 1 | 1 | 1
Table of contents
Simulation Setup / Physics / Boundary Conditions (6 of 19)

## Slide 21: Boundary Conditions, cont.
Silicon barrel walls | side | outer | inner | side-shadow | outer-shadow | inner-shadow
Wall thickness [mm] | 0 | 0 | 0 | 0 | 0 | 0
Heat generation rate [W/m^3] | 0 | 0 | 0 | 0 | 0 | 0
Material name | silicon | silicon | silicon | silicon | silicon | silicon
Thermal BC type | coupled | coupled | coupled | coupled | coupled | coupled
Enable shell conduction? | no | no | no | no | no | no
Wall motion | stationary | stationary | stationary |  |  | 
Shear boundary condition | no slip | no slip | no slip |  |  | 
Wall surface roughness | standard | standard | standard |  |  | 
Internal emissivity | 0.12 | 0.12 | 0.12 |  |  | 
Wall roughness height [mm] | 0 | 0 | 0 |  |  | 
Wall roughness constant | 0.5 | 0.5 | 0.5 |  |  | 
Radiation BC type | opaque | opaque | opaque | opaque | opaque | opaque
Participates in view factor calculation? | yes | yes | yes |  |  | 
Faces per surface cluster | 1 | 1 | 1 |  |  | 
Convective augmentation factor | 1 | 1 | 1 | 1 | 1 | 1
Table of contents
Simulation Setup / Physics / Boundary Conditions (12 of 19)

## Slide 22: Boundary Conditions, cont.
HD-tof-tracker walls | side | outer | inner | side-shadow | outer-shadow | inner-shadow
Wall thickness [mm] | 0 | 0 | 0 | 0 | 0 | 0
Heat generation rate [W/m^3] | 0 | 0 | 0 | 0 | 0 | 0
Material name | carbon fiber | carbon fiber | carbon fiber | carbon fiber | carbon fiber | carbon fiber
Thermal BC type | coupled | coupled | coupled | coupled | coupled | coupled
Enable shell conduction? | no | no | no | no | no | no
Wall motion | stationary | stationary | stationary |  |  | 
Shear boundary condition | no slip | no slip | no slip |  |  | 
Wall surface roughness | standard | standard | standard |  |  | 
Internal emissivity | 0.85 | 0.85 | 0.85 |  |  | 
Wall roughness height [mm] | 0 | 0 | 0 |  |  | 
Wall roughness constant | 0.5 | 0.5 | 0.5 |  |  | 
Radiation BC type | opaque | opaque | opaque | opaque | opaque | opaque
Participates in view factor calculation? | yes | yes | yes |  |  | 
Faces per surface cluster | 1 | 1 | 1 |  |  | 
Convective augmentation factor | 1 | 1 | 1 | 1 | 1 | 1
Table of contents
Simulation Setup / Physics / Boundary Conditions (16 of 19)

## Slide 23: Boundary Conditions, cont.
HD-EMCAL walls | side | outer | inner | side-shadow | outer-shadow | inner-shadow
Wall thickness [mm] | 0 | 0 | 0 | 0 | 0 | 0
Heat generation rate [W/m^3] | 0 | 0 | 0 | 0 | 0 | 0
Material name | aluminum | aluminum | aluminum | aluminum | aluminum | aluminum
Thermal BC type | coupled | coupled | coupled | coupled | coupled | coupled
Enable shell conduction? | no | no | no | no | no | no
Wall motion | stationary | stationary | stationary |  |  | 
Shear boundary condition | no slip | no slip | no slip |  |  | 
Wall surface roughness | standard | standard | standard |  |  | 
Internal emissivity | 0.15 | 0.15 | 0.15 |  |  | 
Wall roughness height [mm] | 0 | 0 | 0 |  |  | 
Wall roughness constant | 0.5 | 0.5 | 0.5 |  |  | 
Radiation BC type | opaque | opaque | opaque | opaque | opaque | opaque
Participates in view factor calculation? | yes | yes | yes |  |  | 
Faces per surface cluster | 1 | 1 | 1 |  |  | 
Convective augmentation factor | 1 | 1 | 1 | 1 | 1 | 1
Table of contents
Simulation Setup / Physics / Boundary Conditions (18 of 19)

## Slide 24: Reference Values
Area | 1 m^2
Density | 1.225 kg/m^3
Enthalpy | 0 J/kg
Length | 1 mm
Pressure | 0 Pa
Temperature | 288.16 C
Velocity | 1 m/s
Viscosity | 1.7894e-05 kg/(m s)
Ratio of specific heats | 1.4
Near wall distance for heat transfer coefficient | 300
Reference zone | enclosure-enclosure
Table of contents
Simulation Setup / Physics / Reference Values
Provides information on the set reference quantities used for computing normalized flow field variables.

## Slide 25: Solver Settings
Equations | 
Flow | true
Turbulence | true
Energy | true
Numerics | 
Absolute velocity formulation | true
Table of contents
Simulation Setup / Solver Settings (1 of 3)
Indicates the equations, pseudo time explicit relaxation factors, discretization scheme, and solution limits used for the simulation. Pseudo-time explicit relaxation factors are used to control the under-relaxation of the solution, especially in steady state analysis. Factors are implemented through the pseudo-transient method, which treats a steady state solver as a transient solver with an unstable time-step. This method helps improve solution stability and convergence, particularly when dealing with complex flow conditions or poor mesh quality.
Discretization schemes provide information on the numerical methods used to convert the continuous partial differential equations of fluid dynamics into a system of algebraic equations that can be solved numerically. Schemes determine how the derivatives in the used equations are approximated at discrete points in the mesh.

## Slide 26: Solver Settings, cont.
Pseudo time explicit relaxation factors | 
Density | 1
Body forces | 1
Turbulent kinetic energy | 0.75
Specific dissipation rate | 0.75
Turbulent viscosity | 1
Energy | 0.75
Explicit momentum | 0.5
Explicit pressure | 0.5
Pressure-velocity coupling | 
Type | coupled
Pseudo time method (global time step) | true
Table of contents
Simulation Setup / Solver Settings (2 of 3)

## Slide 27: Solver Settings, cont.
Discretization Scheme | 
Pressure | second order
Momentum | second order upwind
Turbulent kinetic energy | second order upwind
Specific dissipation rate | second order upwind
Energy | second order upwind
Solution Limits | 
Minimum absolute pressure [Pa] | 1
Maximum absolute pressure [Pa] | 5e+10
Minimum static temperature [C] | -272.15
Maximum static temperature [C] | 4726.85
Minimum turb. kinetic energy [m^2/s^2] | 1e-14
Minimum spec. dissipation rate [s^-1] | 1e-20
Maximum turb. viscosity ratio | 100000
Table of contents
Simulation Setup / Solver Settings (3 of 3)

## Slide 28: Run Information
Number of machines | 1
Number of cores | 6
Case read | 102.297 seconds
Iteration | 94068.8 seconds
Algebraic MultiGrid | 53464.2 seconds
Virtual current memory | 23.265 GB
Virtual peak memory | 24.4361 GB
Memory per M cell | 6.30427
Table of contents
Run Information
Shows number of computers and cores used in the simulation, the time to read the case and to complete iterations, and the allocated random access memory.

## Slide 29: Solution Status
 | Value | Absolute criteria | Convergence status
Continuity | 0.0008969181 | 0.0001 | Not Converged
x-velocity | 9.351765e-08 | 0.0001 | Converged
y-velocity | 1.210729e-07 | 0.0001 | Converged
z-velocity | 1.320896e-07 | 0.0001 | Converged
Energy | 3.589268e-08 | 1e-06 | Converged
k | 2.523355e-06 | 1e-06 | Not Converged
omega | 1.004515e-05 | 0.001 | Converged
Table of contents
Solution Status
Run Iterations: 7500
Verifies convergence by monitoring parameters such as residuals for the enabled equations.

## Slide 30: Report Definitions
max-temp-enclosure | 104.1543 | C
min-temp-enclosure | 19.7213 | C
max-temp-beampipe | 110 | C
min-temp-beampipe | 94.28207 | C
max-temp-ld-hcal | 43.609 | C
min-temp-ld-hcal | 40.98714 | C
max-temp-ld-hcal-inner-wall | 43.6097 | C
min-temp-ld-hcal-inner-wall | 40.98757 | C
max-temp-ld-hcal-outer-wall | 43.60262 | C
min-temp-ld-hcal-outer-wall | 40.98684 | C
max-temp-ld-emcal | 44.39848 | C
min-temp-ld-emcal | 42.65622 | C
max-temp-ld-emcal-inner-wall | 44.40035 | C
min-temp-ld-emcal-inner-wall | 42.65972 | C
Table of contents
Report Definitions (1 of 11)
Quantify and monitor the maximum and minimum temperatures of each detector

## Slide 31: Report Definitions, cont.
max-temp-ld-mpgd-1 | 38.43433 | C
min-temp-ld-mpgd-1 | 32.58362 | C
max-temp-ld-mpgd-1-inner-wall | 38.4461 | C
min-temp-ld-mpgd-1-inner-wall | 32.59982 | C
max-temp-ld-mpgd-1-outer-wall | 38.3041 | C
min-temp-ld-mpgd-1-outer-wall | 32.58184 | C
max-temp-ld-si-disk-5 | 39.07116 | C
min-temp-ld-si-disk-5 | 31.66182 | C
max-temp-ld-si-disk-5-inner-wall | 39.10369 | C
min-temp-ld-si-disk-5-inner-wall | 31.67608 | C
max-temp-ld-si-disk-5-outer-wall | 38.91839 | C
min-temp-ld-si-disk-5-outer-wall | 31.6607 | C
Table of contents
Report Definitions (3 of 11)

## Slide 32: Report Definitions, cont.
max-temp-silicon-barrel | 58.93353 | C
min-temp-silicon-barrel | 58.09703 | C
max-temp-silicon-barrel-inner-wall | 58.93401 | C
min-temp-silicon-barrel-inner-wall | 58.09625 | C
max-temp-silicon-barrel-outer-wall | 58.92886 | C
min-temp-silicon-barrel-outer-wall | 58.09646 | C
max-temp-hd-si-disk-1 | 41.85189 | C
min-temp-hd-si-disk-1 | 38.1062 | C
max-temp-hd-si-disk-1-inner-wall | 41.86193 | C
min-temp-hd-si-disk-1-inner-wall | 37.914 | C
max-temp-hd-si-disk-1-outer-wall | 41.77343 | C
min-temp-hd-si-disk-1-outer-wall | 37.87319 | C
Table of contents
Report Definitions (6 of 11)

## Slide 33: Report Definitions, cont.
max-temp-hd-si-disk-2 | 41.91953 | C
min-temp-hd-si-disk-2 | 38.34368 | C
max-temp-hd-si-disk-2-inner-wall | 41.92962 | C
min-temp-hd-si-disk-2-inner-wall | 37.83834 | C
max-temp-hd-si-disk-2-outer-wall | 41.84338 | C
min-temp-hd-si-disk-2-outer-wall | 37.79696 | C
max-temp-hd-si-disk-3 | 38.95764 | C
min-temp-hd-si-disk-3 | 38.49385 | C
max-temp-hd-si-disk-3-inner-wall | 38.97012 | C
min-temp-hd-si-disk-3-inner-wall | 34.52242 | C
max-temp-hd-si-disk-3-outer-wall | 38.8623 | C
min-temp-hd-si-disk-3-outer-wall | 34.49313 | C
Table of contents
Report Definitions (7 of 11)

## Slide 34: Report Definitions, cont.
max-temp-hd-emcal | 39.11662 | C
min-temp-hd-emcal | 35.20679 | C
max-temp-hd-emcal-inner-wall | 39.11746 | C
min-temp-hd-emcal-inner-wall | 35.20757 | C
max-temp-hd-emcal-outer-wall | 39.10601 | C
min-temp-hd-emcal-outer-wall | 35.20666 | C
max-temp-hd-hcal | 38.04856 | C
min-temp-hd-hcal | 32.3354 | C
max-temp-hd-hcal-inner-wall | 38.04888 | C
min-temp-hd-hcal-inner-wall | 32.33532 | C
max-temp-hd-hcal-outer-wall | 38.04547 | C
min-temp-hd-hcal-outer-wall | 32.33544 | C
Table of contents
Report Definitions (11 of 11)

## Slide 35: Residuals
Chart: Residuals
Table of contents
Plots / Residuals
The solver’s convergence was determined by monitoring the residual, which when less than 110-3 for governing equations—continuity, momentum, energy, and turbulence and radiation—terminated the simulation.

## Slide 36
Table of contents
Plots / Report Plots
The plot option for the report definitions were enabled for each detector volume to allow an additional point of reference for the monitoring of the convergence in real-time as the solution of the governing equations were iterated.
Report Plots

## Slide 37: min-temp-enclosure-rplot
Chart: min-temp-enclosure-rplot
Table of contents
Plots / Report Plots / min-temp-enclosure-rplot

## Slide 38: max-temp-enclosure-rplot
Chart: max-temp-enclosure-rplot
Table of contents
Plots / Report Plots / max-temp-enclosure-rplot

## Slide 39: min-temp-beampipe-rplot
Chart: min-temp-beampipe-rplot
Table of contents
Plots / Report Plots / min-temp-beampipe-rplot

## Slide 40: max-temp-beampipe-rplot
Chart: max-temp-beampipe-rplot
Table of contents
Plots / Report Plots / max-temp-beampipe-rplot

## Slide 41: min-temp-ld-emcal-rplot
Chart: min-temp-ld-emcal-rplot
Table of contents
Plots / Report Plots / min-temp-ld-emcal-rplot

## Slide 42: max-temp-ld-emcal-rplot
Chart: max-temp-ld-emcal-rplot
Table of contents
Plots / Report Plots / max-temp-ld-emcal-rplot

## Slide 43: min-temp-silicon-barrel-rplot
Chart: min-temp-hd-silicon-rplot
Table of contents
Plots / Report Plots / min-temp-silicon-rplot

## Slide 44: max-temp-silicon-barrel-rplot
Chart: max-temp-hd-silicon-rplot
Table of contents
Plots / Report Plots / max-temp-silicon-rplot

## Slide 45: min-temp-hd-drich-rplot
Chart: min-temp-hd-drich-rplot
Table of contents
Plots / Report Plots / min-temp-hd-drich-rplot

## Slide 46: max-temp-hd-drich-rplot
Chart: max-temp-hd-drich-rplot
Table of contents
Plots / Report Plots / max-temp-hd-drich-rplot

## Slide 47
Table of contents
Contours
The plots show the distribution of temperature, allowing the identification of the high temperature areas and the gradient of the heat transfer between the beampipe air flow and detectors.
Contour Plots

## Slide 48: temperature-outlet
Table of contents
Contours / temperature-outlet

## Slide 49: temperature-inlet
Table of contents
Contours / temperature-inlet

## Slide 50: temperature-mid-sec-ld-hcal
Table of contents
Contours / temperature-mid-sec-ld-hcal

## Slide 51: temperature-mid-sec-ld-emcal
Table of contents
Contours / temperature-mid-sec-ld-emcal

## Slide 52: temperature-mid-sec-pfrich
Table of contents
Contours / temperature-mid-sec-pfrich

## Slide 53: temperature-mid-sec-ld-mpgd-2
Table of contents
Contours / temperature-mid-sec-ld-mpgd-2

## Slide 54: temperature-mid-sec-ld-mpgd-1
Table of contents
Contours / temperature-mid-sec-ld-mpgd-1

## Slide 55: temperature-mid-sec-ld-disk-5
Table of contents
Contours / temperature-mid-sec-ld-disk-5

## Slide 56: temperature-mid-sec-ld-disk-4
Table of contents
Contours / temperature-mid-sec-ld-disk-4

## Slide 57: temperature-mid-sec-ld-disk-3
Table of contents
Contours / temperature-mid-sec-ld-disk-3

## Slide 58: temperature-mid-sec-ld-disk-2
Table of contents
Contours / temperature-mid-sec-ld-disk-2

## Slide 59: temperature-mid-sec-ld-disk-1
Table of contents
Contours / temperature-mid-sec-ld-disk-1

## Slide 60: temperature-mid-sec-silicon-barrel
Table of contents
Contours / temperature-mid-sec-silicon

## Slide 61: temperature-mid-sec-hd-disk-1
Table of contents
Contours / temperature-mid-sec-hd-disk-1

## Slide 62: temperature-mid-sec-hd-disk-2
Table of contents
Contours / temperature-mid-sec-hd-disk-2

## Slide 63: temperature-mid-sec-hd-disk-3
Table of contents
Contours / temperature-mid-sec-hd-disk-3

## Slide 64: temperature-mid-sec-hd-disk-4
Table of contents
Contours / temperature-mid-sec-hd-disk-4

## Slide 65: temperature-mid-sec-hd-disk-5
Table of contents
Contours / temperature-mid-sec-hd-disk-5

## Slide 66: temperature-mid-sec-hd-mpgd-1
Table of contents
Contours / temperature-mid-sec-hd-mpgd-1

## Slide 67: temperature-mid-sec-hd-mpgd-2
Table of contents
Contours / temperature-mid-sec-hd-mpgd-2

## Slide 68: temperature-mid-sec-tof-tracker
Table of contents
Contours / temperature-mid-sec-tof-tracker

## Slide 69: temperature-mid-sec-drich
Table of contents
Contours / temperature-mid-sec-drich

## Slide 70: temperature-mid-sec-hd-emcal
Table of contents
Contours / temperature-mid-sec-hd-emcal

## Slide 71: temperature-mid-sec-hd-hcal
Table of contents
Contours / temperature-mid-sec-hd-hcal

## Slide 72
Table of contents
XY Plots
Show each detector’s mid-section, and the beampipe’s inlet and outlet sections. These plots allow the rough estimation of the detector's diameter.
XY Plots

## Slide 73: temp-vs-pos-inlet-sec
Chart: Static Temperature
| -0.49671199999999999 | -0.45921899999999999 | -0.41450999999999999 | -0.35326600000000002 | -0.32138499999999998 | -0.27898800000000001 | -0.25791999999999998 | -0.22794700000000001 | -0.208425 | -0.195409 | -0.178368 | -0.16933500000000001 | -0.15539 | -0.14727499999999999 | -0.135571 | -0.126198 | -0.117405 | -0.104654 | -0.10073699999999999 | -0.10073699999999999 | -9.8471199999999995E-2 | -9.5787800000000006E-2 | -9.5558500000000005E-2 | -9.2568800000000007E-2 | -8.7357000000000004E-2 | -7.0851800000000006E-2 | -5.5177799999999999E-2 | -3.3021300000000003E-2 | -1.44945E-2 | 1.03391E-2 | 3.0815200000000001E-2 | 5.4309999999999997E-2 | 7.43225E-2 | 8.7636699999999998E-2 | 9.2637399999999995E-2 | 9.5831799999999995E-2 | 9.8527400000000001E-2 | 0.100801 | 0.100801 | 0.10240299999999999 | 0.104376 | 0.117684 | 0.12681899999999999 | 0.13540099999999999 | 0.14750199999999999 | 0.154698 | 0.169099 | 0.17795900000000001 | 0.19409499999999999 | 0.20157600000000001 | 0.205766 | 0.22578200000000001 | 0.25567699999999999 | 0.25626100000000002 | 0.27559800000000001 | 0.32005400000000001 | 0.35230699999999998 | 0.41420899999999999 | 0.46009100000000003 | 0.49663200000000002
inlet-sec | 21.537 | 22.682 | 22.691 | 22.938 | 23.252 | 23.839 | 24.229 | 24.85 | 25.418 | 25.843 | 26.529 | 27.05 | 28.158 | 29.017 | 30.532 | 31.786 | 33.649 | 43.05 | 102.364 | 70.365 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 105.404 | 86.161 | 79.433 | 71.372 | 69.468 | 68.038 | 66.707 | 64.581 | 63.373 | 60.941 | 59.478 | 57.176 | 56.24 | 55.7 | 52.883 | 49.564 | 49.507 | 47.57 | 44.398 | 42.802 | 40.635 | 39.738 | 34.883
Table of contents
XY Plots / temp-vs-pos-inlet-sec

## Slide 74: temp-vs-pos-outlet-sec
Chart: Static Temperature
| -0.49862299999999998 | -0.48271500000000001 | -0.42972199999999999 | -0.40072600000000003 | -0.36374000000000001 | -0.33577699999999999 | -0.31123099999999998 | -0.28915099999999999 | -0.27316299999999999 | -0.247062 | -0.24604899999999999 | -0.22819400000000001 | -0.197661 | -0.15967100000000001 | -0.13881099999999999 | -0.118295 | -0.118295 | -0.111401 | -0.10344299999999999 | -9.4320399999999999E-2 | -8.3499299999999999E-2 | -3.3400399999999997E-2 | 1.6059500000000001E-2 | 5.2953600000000003E-2 | 8.1244700000000003E-2 | 9.3848399999999998E-2 | 0.103287 | 0.11147 | 0.118517 | 0.118517 | 0.13852300000000001 | 0.150059 | 0.160186 | 0.192188 | 0.225439 | 0.25686900000000001 | 0.260822 | 0.28610600000000003 | 0.29898999999999998 | 0.31917699999999999 | 0.32753599999999999 | 0.36171199999999998 | 0.39394299999999999 | 0.427118 | 0.48318 | 0.48342200000000002 | 0.49869799999999997
outlet-sec | 20.973 | 21.632 | 21.829 | 22.111 | 22.708 | 23.399 | 24.195 | 25.063 | 25.792 | 27.283 | 27.338 | 28.295 | 29.651 | 30.927 | 31.811 | 54.871 | 86.215 | 96.631 | 99.571 | 100.644 | 101.303 | 102.392 | 102.612 | 102.509 | 102.19 | 101.649 | 100.835 | 98.563 | 92.31 | 66.399 | 48.316 | 47.305 | 46.259 | 45.474 | 43.468 | 41.157 | 40.74 | 38.03 | 36.635 | 34.807 | 34.498 | 34.247 | 34.778 | 35.33 | 35.209 | 35.165 | 32.262
Table of contents
XY Plots / temp-vs-pos-outlet-sec

## Slide 75: temp-vs-pos-mid-sec-ld-emcal
Chart: Static Temperature
Table of contents
XY Plots / temp-vs-pos-mid-sec-ld-emcal
Detector ⌀ = 0.190 m

## Slide 76: temp-vs-pos-mid-sec-pfrich
Chart: Static Temperature
Table of contents
XY Plots / temp-vs-pos-mid-sec-pfrich
Detector ⌀ = 0.190 m

## Slide 77: temp-vs-pos-mid-sec-ld-mpgd-2
Chart: Static Temperature
Table of contents
XY Plots / temp-vs-pos-mid-sec-ld-mpgd-2
Detector ⌀ = 0.0927 m

## Slide 78: temp-vs-pos-mid-sec-ld-disk-4
Chart: Static Temperature
Table of contents
XY Plots / temp-vs-pos-mid-sec-ld-disk-4
Detector ⌀ = 0.08012 m

## Slide 79: temp-vs-pos-mid-sec-ld-disk-1
Chart: Static Temperature
Table of contents
XY Plots / temp-vs-pos-mid-sec-ld-disk-1
Detector ⌀ = 0.07352 m

## Slide 80: temp-vs-pos-mid-sec-silicon-barrel
Chart: Static Temperature
Table of contents
XY Plots / temp-vs-pos-mid-sec-silicon
Detector ⌀ = 0.072 m

## Slide 81: temp-vs-pos-mid-sec-hd-tof-tracker
Chart: Static Temperature
Table of contents
XY Plots / temp-vs-pos-mid-sec-hd-tof-tracker
Detector ⌀ = 0.21 m

## Slide 82: temp-vs-pos-mid-sec-hd-hcal
Chart: Static Temperature
Table of contents
XY Plots / temp-vs-pos-mid-sec-hd-hcal
Detector ⌀ = 0.55 m

## Slide 83: Conclusions
# | Detector | ID [mm] | OD [mm] | Surface thickness [mm] | Length [mm] | Min temperature [°C] | Max temperature [°C]
1 | LD-HCAL | 248 | 268 | 10 | 450 | 40.99 | 43.61
2 | LD-EMCAL | 190 | 210 | 10 | 600 | 42.66 | 44.40
3 | LD-pfRICH | 190 | 210 | 10 | 491 | 30.37 | 43.18
4 | LD-MPGD-2 | 92.7 | 102.7 | 5 | 25 | 34.08 | 39.60
5 | LD-MPGD-1 | 92.7 | 102.7 | 5 | 25 | 32.58 | 38.43
6 | LD-Si-Disk-5 | 92.7 | 102.7 | 5 | 25 | 31.66 | 39.07
7 | LD-Si-Disk-4 | 80.12 | 90.12 | 5 | 25 | 32.91 | 38.33
8 | LD-Si-Disk-3 | 73.52 | 83.52 | 5 | 25 | 38.49 | 42.76
9 | LD-Si-Disk-2 | 73.52 | 83.52 | 5 | 25 | 38.34 | 42.53
10 | LD-Si-Disk-1 | 73.52 | 83.52 | 5 | 25 | 38.11 | 42.25
11 | Si Barrel | 72 | 82 | 5 | 270 | 58.10 | 58.93
12 | HD-Si-Disk-1 | 73.52 | 83.52 | 5 | 25 | 38.11 | 41.85
13 | HD-Si-Disk-2 | 73.52 | 83.52 | 5 | 25 | 38.34 | 41.92
14 | HD-Si-Disk-3 | 76.84 | 86.84 | 5 | 25 | 38.49 | 38.96
15 | HD-Si-Disk-4 | 108.86 | 118.86 | 5 | 25 | 32.91 | 38.00
16 | HD-Si-Disk-5 | 140.28 | 150.28 | 5 | 25 | 31.66 | 39.76
17 | HD-MPGD-1 | 180 | 190 | 5 | 25 | 27.20 | 39.04
18 | HD-MPGD-2 | 180 | 190 | 5 | 25 | 27.90 | 38.94
19 | HD-TOF-Tracker | 210 | 220 | 5 | 80 | 29.09 | 37.33
20 | HD-dRICH | 440 | 460 | 10 | 1270 | 26.97 | 41.00
21 | HD-EMCAL | 410 | 430 | 10 | 300 | 35.21 | 39.12
22 | HD-HCAL | 550 | 570 | 10 | 1400 | 32.34 | 38.05

## Slide 84: Conclusion
To conclude, the report presents the fluid dynamics and thermal analysis at qualitative and quantitative levels for each model component.
The computed information presented in the report shows the thermal conditions at each detector’s inner wall. The resulting maximum temperature at each detector’s inner wall under the specific set and presented conditions was calculated and displayed.