## Slide 1: TOF requirements, T0 determination, Timing calibrations
Satoshi YANO
Hiroshima University
The ePIC Collaboration Meeting
Electronics and DAQ II: DAQ Integration / ASIC status and plans
07/17/2025

## Slide 2: Message from Jeff
Is there anyone who could give a summary from the TOF side? Specifically, I'd want some idea about:
  The requirement/impact of timing resolution for the physics analysis
  The timing impact of the T0 determination
  Whether it is (or might be) possible to track slow phase drifts of the clock (due to temperature) using calibrations

## Slide 3: Recap of AC-LGAD TOF
The ePIC AC-LGAD TOF system is used for particle identification (PID), tracking, and background rejection in both mid-rapidity (BTOF) and forward-rapidity (FTOF) regions.
A position resolution of ~30 um and a timing resolution of 35 ps for PID and tracking within a space of less than 10 cm in thickness are required
Barrel-TOF (BTOF)
0.64 m
~2.8 m
-1.33<η<1.74
1.84<η<3.61
Forward-TOF (FTOF)
60 cm
10.5 cm

## Slide 4: Recap of AC-LGAD TOF
The ePIC AC-LGAD TOF system is used for particle identification (PID), tracking, and background rejection in both mid-rapidity (BTOF) and forward-rapidity (FTOF) regions.
A position resolution of ~30 um and a timing resolution of 35 ps for PID and tracking within a space of less than 10 cm in thickness are required
Barrel-TOF (BTOF)
0.64 m
~2.8 m
-1.33<η<1.74
1.84<η<3.61
Forward-TOF (FTOF)
60 cm
10.5 cm

## Slide 5: Message from Jeff
Is there anyone who could give a summary from the TOF side? Specifically, I'd want some idea about:
  The requirement/impact of timing resolution for the physics analysis
  The timing impact of the T0 determination
  Whether it is (or might be) possible to track slow phase drifts of the clock (due to temperature) using calibrations

## Slide 6: Impact on the ePIC PID performance
Focus of TOF is below p = 1 GeV/c
Particle-Identification at low momentum region is the primary task
Used in conjunction with Cherenkov light detectors to eliminate PID gaps and to cross-calibrate each other in overlapping regions
K from D
Decay products from D-meson in ep DIS @ √s = 141 GeV
π from D

## Slide 7: Impact on the ePIC PID performance
Focus of TOF is below p = 1 GeV/c
Particle-Identification at low momentum region is the primary task
Used in conjunction with Cherenkov light detectors to eliminate PID gaps and to cross-calibrate each other in overlapping regions
BTOF
K/p 3σ
FTOF
π/K 3σ
BTOF
FTOF
Decay products from D-meson in ep DIS @ √s = 141 GeV
Assuming
BTOF σtot = 35 ps
FTOF σtot = 25 ps
π from D
K from D

## Slide 8: Impact on the ePIC PID performance
Focus of TOF is below p = 1 GeV/c
Particle-Identification at low momentum region is the primary task
Used in conjunction with Cherenkov light detectors to eliminate PID gaps and to cross-calibrate each other in overlapping regions
hpDIRC
BTOF
K/p 3σ
dRICH
FTOF
π/K 3σ
hpDIRC
BTOF
dRICH
FTOF
Decay products from D-meson in ep DIS @ √s = 141 GeV
Assuming
BTOF σtot = 35 ps
FTOF σtot = 25 ps
π from D
K from D

## Slide 9: Sensor Timing Resolution v.s. Overlap with hpDIRC
hpDIRC limit for K/p sep.
hpDIRC limit for π/K sep.
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole!
σsensor> 90 ps doesn’t have overlapping region with hpDIRC in K/p separation any more
y = 0

## Slide 10: Sensor Timing Resolution v.s. Overlap with hpDIRC
hpDIRC limit for K/p sep.
hpDIRC limit for π/K sep.
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole!
σsensor> 90 ps doesn’t have overlapping region with hpDIRC in K/p separation any more
Δp ~ 0.5 GeV/c
Δp ~ 0.45 GeV/c
Current best performance
σsensor ~ 35 ps
y = 0

## Slide 11: Sensor Timing Resolution v.s. Overlap with hpDIRC
hpDIRC limit for K/p sep.
hpDIRC limit for π/K sep.
Δp ~ 0.5 GeV/c
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole!
σsensor> 90 ps doesn’t have overlapping region with hpDIRC in K/p separation any more
Δp ~ 0.45 GeV/c
Current best performance
σsensor ~ 35 ps
y = 0

## Slide 12: Message from Jeff
Is there anyone who could give a summary from the TOF side? Specifically, I'd want some idea about:
  The requirement/impact of timing resolution for the physics analysis
  The timing impact of the T0 determination
  Whether it is (or might be) possible to track slow phase drifts of the clock (due to temperature) using calibrations

## Slide 13: T0 Timing Resolution v.s. PID performance (BTOF case)
y = 0

## Slide 14: T0 Timing Resolution v.s. PID performance (BTOF case)
Reference T0 jitter = 25 ps
y = 0

## Slide 15: T0 Timing Resolution v.s. PID performance (BTOF case)
Reference T0 jitter = 25 ps
+10 ps
y = 0

## Slide 16: T0 Timing Resolution v.s. PID performance (BTOF case)
Reference T0 jitter = 25 ps
+10 ps
+20 ps
y = 0

## Slide 17: T0 Timing Resolution v.s. PID performance (BTOF case)
In σT0 = 25 ps case, the overlap region is shifted by ~0.05 GeV/c for π/K sep. and ~ 0.1 GeV/c for K/p sep. when the additional jitter is 10 ps
Δp ~ 0.1 GeV/c per additional 10ps jitter
for K/p sep.
Reference T0 jitter = 25 ps
+10 ps
+20 ps
Δp ~ 0.05 GeV/c per additional 10ps jitter
for π/p sep.
y = 0

## Slide 18: Message from Jeff
Is there anyone who could give a summary from the TOF side? Specifically, I'd want some idea about:
  The requirement/impact of timing resolution for the physics analysis
  The timing impact of the T0 determination
  Whether it is (or might be) possible to track slow phase drifts of the clock (due to temperature) using calibrations

## Slide 19: T0 Monitoring and Calibration
T0 can be estimated by “Track-Based Average” method
  thit: Measured hit time
  texp: Expected hit time w/ particle assumption (pion mass is assumed)
    Combining hpDIRC PID, the precision can be improved
Precision of the Track-Based T0 depends on # tracks
Hit rate of one sensor is about 1 Hz (BTOF)
  E.g. time interval is set to be 1min, σT0 = 43 ps / √60 ~ 5 ps
    σsensor = 40 ps and σelec. = 15 ps is assumed
  (I think), even in considering various additional effects, the shift can be monitored < 10ps / min
  1 min is enough?

## Slide 20: T0 Monitoring and Calibration
T0 can be estimated by “Track-Based Average” method
  thit: Measured hit time
  texp: Expected hit time w/ particle assumption (pion mass is assumed)
    Combining hpDIRC PID, the precision can be improved
Precision of the Track-Based T0 depends on # tracks
Hit
rate of one sensor is about 1 Hz (BTOF)
  E.g. time interval is set to be 1min, σT0 = 43 ps / √60 ~ 5 ps
    σsensor = 40 ps and σelec. = 15 ps is assumed
  (I think), even in considering various additional effects, the shift can be monitored < 10ps / min
  1 min is enough?

## Slide 21: T0 Monitoring and Calibration
T0 can be estimated by “Track-Based Average” method
  thit: Measured hit time
  texp: Expected hit time w/ particle assumption (pion mass is assumed)
    Combining hpDIRC PID, the precision can be improved
Precision of the Track-Based T0 depends on # tracks
Hit rate of one sensor is about 1 Hz (BTOF)
  E.g. time interval is set to be 1min, σT0 = 43 ps / √60 ~ 5 ps
    σsensor = 40 ps and σelec. = 15 ps is assumed
  (I think), even in considering various additional effects, the shift can be monitored < 10ps / min
  1 min is enough?

## Slide 22: Summary
TOF is one of the important PID detector, especially in low-momentum region
T0 is one of the main source of the timing jitter
  Under realistic assumption (σT0 =20-25 ps), there is already no PIC acceptance hole
Additional T0 jitter effect is expected to worse PID coverage momentum range by 0.05 GeV/c and 0.1 GeV/c per 10ps for π/K and K/p separation, respectively
The T0 shift is possibly monitored by “Track-Based Average” method
  The shift to each sensor may be able to be monitored by 10 ps precision each 1 min

## Slide 23: Summary
TOF is one of the important PID detector, especially in low-momentum region
T0 is one of the main source of the timing jitter
  Under realistic assumption (σT0 =20-25 ps), there is already no PID acceptance hole
Additional T0 jitter effect is expected to worse PID coverage momentum range by 0.05 GeV/c and 0.1 GeV/c per 10ps for π/K and K/p separation, respectively
The T0 shift is possibly monitored by “Track-Based Average” method
  The shift to each sensor may be able to be monitored by 10 ps precision each 1 min

## Slide 24: Summary
TOF is one of the important PID detector, especially in low-momentum region
T0 is one of the main source of the timing jitter
  Under realistic assumption (σT0 =20-25 ps), there is already no PID acceptance hole
Additional T0 jitter effect is expected to worse PID coverage momentum range by 0.05 GeV/c and 0.1 GeV/c per 10ps for π/K and K/p separation, respectively
The T0 shift is possibly monitored by “Track-Based Average” method
  The shift to each sensor may be able to be monitored by 10 ps precision each 1 min

## Slide 25: Summary
TOF is one of the important PID detector, especially in low-momentum region
T0 is one of the main source of the timing jitter
  Under realistic assumption (σT0 =20-25 ps), there is already no PID acceptance hole
Additional T0 jitter effect is expected to worse PID coverage momentum range by 0.05 GeV/c and 0.1 GeV/c per 10ps for π/K and K/p separation, respectively
The T0 shift is possibly monitored by “Track-Based Average” method
  The shift to each sensor may be able to be monitored by 10 ps precision each 1 min