## Slide 1: ePIC DAQ Plans and picoDAQ Overview
EIC User Group and ePIC Joint Collaboration Meeting
July 14th – 18th, 2025
Jefferson Lab, Newport News, VA
David Abbott (Jefferson Lab)
L3 Project Manager for ePIC DAQ/Computing

## Slide 2: Breakout Overview
Joint session discussions this morning
  ePIC DAQ plans (picoDAQ) and RDO development status
  Software interfaces for test benches and beams.
ePIC DAQ Status
  picoDAQ plans
  ePIC sub-detectors – upcoming testing
GTU Status
RDO Overviews
  ALINX AXAU15 RDO/DAM Development Board
  dRICH RDO
  Calorimeter test stand
  SVT readout development

## Slide 3: ePIC DAQ Schedule
A functional DAQ will be necessary for small scale detector testing as well as commissioning and pre-ops.
Computing resources are staged to make purchases when the hardware is needed, taking advantage of price savings and performance improvements in time.
Hardware and software development early in the construction phase will involve a series of releases with increasing functionality.
Detector Install: FY29Q2 - FY31Q2
Cosmics: FY31Q3
Early CD-4: FY32Q4
DAQ Releases:
PicoDAQ FY26Q1
  Readout test setups
MicroDAQ: FY26Q4
  Readout detector data in test stand using engineering articles
MiniDAQ: FY28Q1
  Readout detector data using full hardware and timing chain
Full DAQ-v1: FY29Q2
  Full functionality DAQ ready for full system integration & testing
Production DAQ: FY31Q3
Ready for cosmics
MiniDAQ
Production
DAQ
PicoDAQ
MicroDAQ
PDR2
Full DAQ-V1
Non-LLP pre-baseline schedule is in progress
PDR1
PDR3

## Slide 4: ePIC Readout Chain
Global Timing
Unit (GTU)
- Interfaces to Collider
- Run Control & DAM
- Config & Control
- Clock & Timing
On Detector
SMT BGA
Adapter
Detector Specific
Sensor
Detector Specific
Front End
Board
(FEB)
Detector Specific
Readout
Board
(RDO)
Few Variants
Data Aggregation Module (DAM)
Common
Echelon 0
Computing
Common
To Echelon 1
(ethernet)
PCIe/
Ethernet
RDO/DAM
Protocol
(fiber-pair)
ASIC Protocols
(I2C, lpGBT)
Copper/Fiber
ASICs
ASICs
RDO
DAM
VTRX+/SFP+
lpGBT
VTRX+/SFP+
dRICH, TimePix, AstroPix, Calorimeters
pfRICH, hpDIRC, TOF
On Detector RDO
(98.5 or 39.4 MHz)
Off Detector (Platform)
FEB
ASICs
39.4 MHz
39.4 MHz
DAQ Room
DAM
RDO
lpGBT
VTRX+
DAM
RDO/
Aggregator
SVT/MAPS

## Slide 5: ePIC DAQ Support
While many detector groups may have test stands that they are using for development work, it is important at this stage to begin to have common solutions available for all ePIC sub-systems (even if they choose not to use them).
In near term, as we are developing engineering articles for all the DAQ components (FEB,RDO,DAM,GTU), we want to have two “releases” of firmware/software that will support a subset of hardware that is generally available – both commercially and from new and existing hardware designs.
PicoDAQ
  Focused around RDO/ASIC configuration and readout.
  This is for simple test systems supporting a single RDO (FPGA) connected to one or multiple FEBs (ASICS/Digitizers).
  Ethernet-based configuration, control and readout support from a Linux PC or server.
MicroDAQ
  Build on PicoDAQ by adding DAM and GTU hardware support
  Implementation of GTU<->DAM<->RDO clock distribution and communication protocol.
  Support via DAM for time frame building of data from multiple RDOs.
  PCIe and Ethernet readout options from the DAM.

## Slide 6: GTU Updates
GTU specifications and schematic design has been under development this year.
Thanks to William Gu for all his work on this. He will provide an overview and status in this session.
The current timeline is to produce an engineering article by the end of 2025 (or early 2026).
For early detector test setups we still need to provide some GTU functionality, in particular the appropriate clocks (98.5 MHz and 39.4 MHz).
In additional to the final DAM design, we are supporting GTU functionality for some commercial hardware as well.

## Slide 7: FELIX Updates – FLX-155
FELIX hardware for future ATLAS experiments at HL-LHC is being developed at BNL (Omega Group)
  ePIC is collaborating with Omega to use this design as our DAM board.
Initial engineering articles were tested in early 2025. Updated PCB design sent out for fabrication/population
  Final design board will be tested this Fall (2025).
We expect to produce at least 4 boards for ePIC use after testing. Availability anticipated in Jan/Feb 2026
RDO
GTU interface
Versal Ultrascale+ FPGA
Detector
Front-End Link eXchange
100Gb
Ethernet
Linux OS, Clock Distribution
Stream Frame Builder, Optional fixed latency processing
(output via Ethernet and/or PCIe)
Up to 48 fiber links
RDO
RDO
RDO

## Slide 8: Mini-DAM/GTU Support
Inexpensive FPGA development board can be used as an RDO interface to ASIC FEBs via the FMC connector.
With the addition of an FMC adaptor board developed at JLAB it can be used as a “mini” DAM with readout/control support for up to 5 RDO boards.
In addition, a clock chip on the adapter card will provide GTU services for distribution of 98.5 MHz or 39.4MHz clocks
Alinx AXAU15
(Artix Ultrascale+ FPGA)
~$800
FMC DAM adapter board (JLAB Design)

## Slide 9: JLab DAQ Support for ePIC
At JLab all 4 experimental halls use common hardware and software designs and applications to implement their DAQ systems (CODA).
  Our long-term goal is to integrate ePIC DAQ developments into our existing designs.
We also work with researchers wanting to bring in new equipment to try and integrate with existing systems. This is not always easy.
There are a number of groups now working on ePIC related sub-detectors whom we need to support at some level.

## Slide 10
HRPPD Readout Test Stand
CAEN DT5742B digitizer
CAEN V1742 Digitizer with CODA DAQ and electronics
CAEN N1470 HV source for HRPPD
Light source pulsed 405nm laser
Calibrated Hamamatsu S2281 photodiode
XYZ motion stage Velmex
CAEN DT5742B Digitizer
Electronics Rack
Waveform from CAEN *742 digitizer
CAEN 1742 Digitizer​

## Slide 11: ZDC testing – CAEN Commercial System
Janus is open-source software developed by CAEN for the control and readout of FERS‐5200 boards

## Slide 12: TimePix – Readout testing
SPIDR4 Control board using a Zync 7000 series SoC
Petalinux OS, Developed at NIKEF

## Slide 13
Lumi Pair Spectrometer DAQ/Readout Overview
Stephen JD Kay, Nicholas Zachariou, University of York
Pair Spectrometer
  Two WSciFi calorimeters
  Max #readout channels - 3360
  By grouping SiPMs in first 4 + last 6 layers, can reduce significantly
    3360 -> 2100
Expected rates - At peak lumi setting, 0.1 pair production event per 10ns
  Expect ~80 SiPMs to fire from an event
  ~50 NPE per SiPM
    Expected signal
Readout, no final decision but don’t want to reinvent the wheel
  HGCROC
Some initial beam tests of modules
  Would love to use real readout system
  Caen desktop digitisers so far -> Very limited (~2 seconds of data!)

## Slide 14: JLAB Front-End Readout Electronics
Artix FPGA card with 1Gb Ethernet
1Gb
Ethernet
Clock/Sync
(RJ45)
Artix 7 FPGA
(firmware TDC)
Petiroc
ASICs
Used with the RICH Detector in Hall B and the DIRC detector in Hall D
ALERT experiment in
Hall B (TOF detector).
MAROC3 ASIC Daughter Card
Petiroc ASIC Daughter Card
VMM3 ASICs
KINTEX
FPGA
At JLAB we have developed a common firmware and software framework for simple readout of these types of electronics.

## Slide 15: Front-End readout support at JLab
TCP Socket based slow control protocol from a Linux-based PC using a 1/10Gb ethernet port
  32bit registers map to ASIC configuration bus.
FPGA based block RAM used to aggregate data and build frames/events
  Up to 32 input streams to create one ~1GB/s output stream
Low cost commercial TCP/IP block supporting 1 or 10Gb ethernet links (Client and Server)
  Low resource utilization
  License will allow JLAB to distribute downloadable firmware using this IP for ePIC associated projects
We plan to continue and expand support for this firmware/software for both existing and future projects.
ASIC
PC
ASIC
ASIC
FPGA
Network
IP
Slow Control
Bridge
TCP/UDP
Client/Server
Frame
Builder
Linux OS
c library
Stream 0
Stream 1
Stream N
Framebuilder
TCP Even Builder socket
0
0
0
1
1
1
2
2
2
0
1
2
0
1
2
0
1
2

## Slide 16: Thank you! Questions?

## Slide 17
Backup

## Slide 18: EIC Streaming DAQ/Computing Architecture
Bunch Crossing
10.2 ns/98.5 MHz
Interaction Rate
~ 2 us/500 kHz
Low occupancy
(for Physics signal)

## Slide 19: Summary of Channel Counts and Data Flow
FEB
RDO
Readout Computer
Detector
DAM
PCI/Eth
Fiber
Copper
Aggregate | 2.0 Tb/sec
Noise | 1.6 Tb /sec
Signal from Physics + Background | 400 Gb / sec
Aggregate | 2.0 Tb/sec
Per RDO (Avg) | 0.7 Gb/sec
Eth
Aggregate | 115 Gb/sec
Collision Signal | 62 Gb/sec
Synchrotron Rad | 6 Gb/sec*
Electron Beam | 4.5 Gb/sec
Hadron Beam | 1.0 Gb/sec
Noise | 41 Gb/sec
Summary of Data Flow
Scale of the system:
Electronics
  ~ 24 detectors
  ~ 5 Readout Technologies
  ~ 3000 RDOs (on detector/in racks)
  ~ 100 DAM boards (DAQ room)
  GTU (with interface boards)
Maximum Data Volume
  ~ 2 Tb/sec digitized
  ~ 115 Gb/sec recorded
Online Computing
  ~200 nodes (DAQ Room/SDCC)
Synchrotron radiation caveats:
Rates are based upon hit rate for all ePIC detectors. In fact, data volumes depend upon specific detector hit (64 bits/hit assumed)
Highest Synchrotron radiation / electron beam gas will correspond to lower values for collision signal
Plan to analyze by component soon
*

## Slide 20
TCP/IP IP Blocks for FPGA
10G TCP/IP Client
https://comblock.com/download/com5503soft.pdf
https://www.comblock.com/com5502soft.html
10G TCP/IP Server
Low cost 10Gbps TCP/IP IP blocks from COMBLOCK (also 1Gbps version are available)
Very flexible license
Low resource utilization
TCP <-> Peripheral bus bridge used, but this bridge can be replaced by many other bus types if needed without changing the register map of the front-end unit
JLAB can distribute downloadable firmware using this IP for ePIC associated projects

## Slide 21: Timing Resolution with Reconstructed Clock

## Slide 22: Timing Resolution with Reconstructed Clock