## Slide 1: Overview Barrel Time-of-Flight
Satoshi YANO
Hiroshima University
The ePIC Collaboration Meeting AC-LGAD detector workfest
07/16/2025

## Slide 2: Recap of Barrel-TOF
The ePIC AC-LGAD TOF is PID, tracking and background rejection detector for mid-rapidity (BTOF: -1.33<η<1.74)
Cylindrical shape is composed of 144 tilted staves (288 half-staves)
Strip-type AC-LGAD sensor is used to meet the requirement of ~35 ps and ~30 um timing and spatial resolution respectively
Barrel-TOF (BTOF)
0.64 m
~2.8 m
-1.33<η<1.74

## Slide 3: Recap of Barrel-TOF
The ePIC AC-LGAD TOF is PID, tracking and background rejection detector for mid-rapidity (BTOF: -1.33<η<1.74)
Cylindrical shape is composed of 144 tilted staves (288 half-staves)
Strip-type AC-LGAD sensor is used to meet the requirement of ~35 ps and ~30 um timing and spatial resolution respectively
Barrel-TOF (BTOF)
0.64 m
~2.8 m
-1.33<η<1.74
144 x Staves

## Slide 4: Recap of Barrel-TOF
The ePIC AC-LGAD TOF is PID, tracking and background rejection detector for mid-rapidity (BTOF: -1.33<η<1.74)
Cylindrical shape is composed of 144 tilted staves (288 half-staves)
Strip-type AC-LGAD sensor is used to meet the requirement of ~35 ps and ~30 um timing and spatial resolution respectively
Barrel-TOF (BTOF)
0.64 m
~2.8 m
-1.33<η<1.74
144 x Staves

## Slide 5: Impact on the ePIC PID performance
Focus of TOF is below p = 1 GeV/c
Particle-Identification at low momentum region is the primary task
Used in conjunction with Cherenkov light detectors to eliminate PID gaps and to cross-calibrate each other in overlapping regions
K from D
Decay products from D-meson in ep DIS @ √s = 141 GeV
π from D

## Slide 6: Impact on the ePIC PID performance
Focus of TOF is below p = 1 GeV/c
Particle-Identification at low momentum region is the primary task
Used in conjunction with Cherenkov light detectors to eliminate PID gaps and to cross-calibrate each other in overlapping regions
BTOF
K/p 3σ
FTOF
π/K 3σ
BTOF
FTOF
Decay products from D-meson in ep DIS @ √s = 141 GeV
Assuming
BTOF σtot = 35 ps
FTOF σtot = 25 ps
π from D
K from D

## Slide 7: Impact on the ePIC PID performance
Focus of TOF is below p = 1 GeV/c
Particle-Identification at low momentum region is the primary task
Used in conjunction with Cherenkov light detectors to eliminate PID gaps and to cross-calibrate each other in overlapping regions
hpDIRC
BTOF
K/p 3σ
dRICH
FTOF
π/K 3σ
hpDIRC
BTOF
dRICH
FTOF
Decay products from D-meson in ep DIS @ √s = 141 GeV
Assuming
BTOF σtot = 35 ps
FTOF σtot = 25 ps
π from D
K from D

## Slide 8: Sensor Timing Resolution v.s. Overlap with hpDIRC
hpDIRC limit for K/p sep.
hpDIRC limit for π/K sep.
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole!
σsensor> 90 ps doesn’t have overlapping region with hpDIRC in K/p separation any more

## Slide 9: Sensor Timing Resolution v.s. Overlap with hpDIRC
hpDIRC limit for K/p sep.
hpDIRC limit for π/K sep.
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole!
σsensor> 90 ps doesn’t have overlapping region with hpDIRC in K/p separation any more
Δp ~ 0.5 GeV/c
Δp ~ 0.45 GeV/c
Current best performance
σsensor ~ 35 ps

## Slide 10: Sensor Timing Resolution v.s. Overlap with hpDIRC
hpDIRC limit for K/p sep.
hpDIRC limit for π/K sep.
Δp ~ 0.5 GeV/c
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole!
σsensor> 90 ps doesn’t have overlapping region with hpDIRC in K/p separation any more
Δp ~ 0.45 GeV/c
Current best performance
σsensor ~ 35 ps

## Slide 11: Data Transmission
Front-side
Back-side
8 x 2 x 288 =4608
Half-Stave = 8 x Modules = ~ 1320 [mm]
Module (Stavelet) ~ 160 [mm]
3 x 8 x 2 x 288
=13824
2 x 8 x 2 x 288
=4608
21 [mm]
Service Hybrid
33 [mm]
lpGBT
VTRx
x4
FPC
Interposer
Sensor
CFDROC
(ASIC)
X/X0 < 3% (including support structure)
DCDC
Backend
32 (front-side) + 32 (back-side) = 64 CFDROCs
600 [mm]

## Slide 12: Stave Assembling Steps (Opt1)
Sensor + ASIC
Interposer
FPC
Glue dispenser
Wire bonding
Module-to-Module bonding machine
Support structure
Module Assembly Site
Final Construction Site
Glue dispenser

## Slide 13: Detector Assembling Workflow
Mechanical QA
Purdue/Academia Sinica
BTOF QA
BNL
Install to ePIC
BNL
Stave QA
Purdue/BNL
RB QA
Rice
PB QA
Rice
RB Assembling
Company E
PB Assembling
Company E
SH QA
Rice
SH Assembling
Rice
BTOF construction
BNL
Stave assembling
Purdue/BNL
ASIC Production
TSMC
ASIC QA
Institute A
ASIC QA
Institute B
Interposer
Production
Company C
Sensor QA/QC
Hiroshima
Module assembling
Hiroshima
Module QA
Hiroshima
Sensor QA/QC
RIKEN
Sensor Production
HAMAMATSU
Module assembling
UCSC
Module QA
UCSC
Sensor QA/QC
UCSC
Module assembling
RIKEN
Module QA
RIKEN
FPC Production
Company D
Module
Check
Purdue /BNL
FPC QA
Hiroshima
FPC QA
RIKEN
FPC QA
UCSC
Interposer QA
Hiroshima
Interposer QA
RIKEN
Interposer QA
UCSC
Mechanical
Production
Purdue/Academia Sinica

## Slide 14: Assembly Site in Japan
Hiroshima University and RIKEN will be one of the main assembly site
The site, 100 m2 Class 10,000 (partially Class 1,000), are under construction
  Construction will be completed at the end of JFY25 (March 2026).

## Slide 15: Assembly Site in Japan
Hiroshima University and RIKEN will be one of the main assembly site
The site, 100 m2 Class 10,000 (partially Class 1,000), are under construction
  Construction will be completed at the end of JFY25 (March 2026).

## Slide 16: Assembly Site in Japan
Hiroshima University and RIKEN will be one of the main assembly site
The site, 100 m2 Class 10,000 (partially Class 1,000), are under construction
  Construction will be completed at the end of JFY25 (March 2026).
Autumn 2024

## Slide 17: Assembly Site in Japan
Hiroshima University and RIKEN will be one of the main assembly site
The site, 100 m2 Class 10,000 (partially Class 1,000), are under construction
  Construction will be completed at the end of JFY25 (March 2026).
Reference object
Autumn 2024

## Slide 18: Assembly Site in Japan
Hiroshima University and RIKEN will be one of the main assembly site
The site, 100 m2 Class 10,000 (partially Class 1,000), are under construction
  Construction will be completed at the end of JFY25 (March 2026).
Autumn 2024
Summer 2025
8 months later
Reference object

## Slide 19: Assembly Site in Japan
Hiroshima University and RIKEN will be one of the main assembly site
The site, 100 m2 Class 10,000 (partially Class 1,000), are under construction
  Construction will be completed at the end of JFY25 (March 2026).
Autumn 2024
Summer 2025
8 months later
Reference object

## Slide 20: What should be discussed with the other working groups
Impact on other detectors and entire ePIC system
  Acceptable maximum material budget for tracking and PID
  Required spatial resolution for tracking
Best design for the integration, services and maintenance keeping best performance
Service Hybrid (SH) design and location
  Currently, the design of FTOF is mainly ongoing
  The space available for the BTOF is limited due to material budget constraints and service requirements, so deeper exploration is required.
Today

## Slide 21: What should be discussed with the other working groups
Impact on other detectors and entire ePIC system
  Acceptable maximum material budget for tracking and PID
  Required spatial resolution for tracking
Best design for the integration, services and maintenance keeping best performance
Service Hybrid (SH) design and location
  Currently, the design of FTOF is mainly ongoing
  The space available for the BTOF is limited due to material budget constraints and service requirements, so deeper exploration is required.
Today
Beyond today

## Slide 22: Backup

## Slide 23: Stave Assembling Process (Opt2)
Sensor + ASIC (packaged)
Interposer
FPC
Glue dispenser
Wire bonding
Support structure
FPC
Glue dispenser
Wire bonding
Assembling sites
BNL/Purdue