## Slide 1: Status report ToF Simulations and Software Kentaro Kawade Shinshu Univ. on behalf of the ePIC ToF simulation team

## Slide 2: ToF Simulation Working Group
Coordinators
  Kentaro Kawade, Tommy Tsang Chun Yuen
Holding biweekly meeting since June 2024
Current Activities
  Tommy (KSU)
    Digitization for BToF
    Implement new ToF geometry/design
  Honey Khindri (IIT Madras)
    Digitization for EToF
  Kyohei Ono
    Impact of ToF material budgets on hpDIRC resolution
  Kentaro Kawade
    Evaluate PID performance
https://indico.bnl.gov/category/569

## Slide 3: ToF Digitization Tommy and Honey
ToF (AC-LGAD) brief software status on PID session

## Slide 4: BToF; Digitization work-flow design
Start
Geant4 hit
Charge sharing
Edep & time in cells
Pulse Generation
Pulse Combiner
ADC and TDC
in sensor
Pulse Discretization
Pulse Digitization
Calibration
Hit Association
Clustering
Tracking
Tracking
Already pushed to main branch
Trying to push in [PR]
Coupling of clusters and tracking is a next step

## Slide 5: Calibration, clustering and Hit association
Calibration of TDC to time is just a linear transformation
  Same for ADC
  No time walk (slewing) correction
Clustering is just weighted average of neighbors
  Group connected neighbors together
    Hits are neighbors if Δt < 1ns
  Weighted by Edep
  Time of a cluster = time of the earliest hit
  No Edge correction
Association of reconstructed hit with true hits
  They come from the same sensor
  Time difference between the two hits < 1 ns
  If there are multiple hits within 1 ns  choose the one with the smallest t difference
Cluster 1
Cluster 2
Cluster 3
Time axis not shown

## Slide 6: Clustering performance
Checking digitized ADC and TDC
  Time walk as expected
    Need to introduce time walk correction or CFD for BToF
  Need to introduce noise on the pulse
Clustering worked fine
  better ADC linearity
  better phi resolution thanks to the charge sharing

## Slide 7: EToF; Current digitization work-flow design
Ongoing development based on BToF WF
Energy distribution of a single Hit in EToF
  Distributed as expected
  Tentative: 2D gaussian 1 mm width

## Slide 8: Geometry updates in EPIC simulation

## Slide 9: update: BTOF geometry
Before: Sensor on one side  New: Sensors on both sides
Cooling tubes in carbon form
Updated to match proposed drawing [Link]
Updated on May 2025

## Slide 10: update: ETOF geometry
Issue: ACTS is unable to use tracking information on the back side of ETOF [Report]
  Error with ETOF geometry implementation
Fixed in [PR]
Cover on the left removed to show sensors

## Slide 11: update: strip size
Realistic BTOF grid size: 0.5 cm * 0.5 mm
Realistic ETOF grid size: 0.5 mm * 0.5 mm
However, position better than 0.5 mm because of charge sharing (not yet implemented).
Reduced BTOF grid size to 0.5 cm * 0.1 mm
Reduced ETOF grid size to 0.1 mm * 0.1 mm
Grid size

## Slide 12: Plans: Geometry and digitization
Time walk/edge correction
Use CFD instead of EICROC for BTOF
  EICROC uses constant threshold, not constant fraction
Add noise to pulses
Add cooling tubes to ETOF
Realistic charge sharing parameters
  Communicate with sensor R&D experts

## Slide 13: Material effect Study Kyohei

## Slide 14: Motivation: Material budget
Estimate the impact of BTOF material budgets on the outer hpDIRC angular resolution
  To optimize the BTOF design and performance
  Crucial inputs for sensors, structures and readout PCBs to relax the tight requirement (1% X0)
hpDIRC is a Cherenkov particle identification detector
  → Angular resolution at the surface is important
    Target@6 GeV/c: Δθ = 0.5 [mrad]
  Material budget of BTOF  Affects on angular resolution due to multiple scattering effects Determine the upper limit of the BToF material budget
TOF (64cm) Outer MPGD (72.5cm) DIRC (75.5cm)
hpDIRC: high performance Detection of Internally Reflected Cherenkov light

## Slide 15: Simulation setup: Angle & Material Study
Added sensitive layer at the hpDIRC surface
  To take truth hit position at the surface
Different BToF Support structure materials
  Carbon foam (default)：0.09 g/cm3 (0.12% X/X0)
  Carbon fiber : 1.5 g/cm3 (2.64% X/X0)
  Aluminum：2.65 g/cm3 (6.52% X/X0)
Single particle full Detector simulation in DD4hep
  Particle:
  Fixed Momentum:
  Direction
    :
    :
EICrecon to perform tracking and calculate angular resolution
  Take angular resolution using the “Residual method”
Dummy sensitive layer
Original sensor position
BTOF Support structure

## Slide 16: Calculate Angular Resolution -Residual method
Reconstruct tracks using all tracker hits with a Kalman filter
Propagate the fitted tracks to the hpDIRC surface  Use the intersection as a reconstructed hit position
Take difference of propagated track angles and truth hit angles
  Resolution is given by Gaussian sigma Ex)
@6GeV
epic 25.06.0
EICrecon 1.26.0

## Slide 17: Angular Resolution vs. angle
Best resolution achieved at θ ≈ 90° (as expected)
  But; Still does not match the requirement “0.5 mrad @ 6 GeV”
Detector Requirements 0.5mrad @ 6GeV
epic 25.06.0
EICrecon 1.26.0
epic 25.06.0
EICrecon 1.26.0

## Slide 18: Angular Resolution for different Materials
Slight performance degradation observed with increasing material budget
  Carbon foam keep the resolution close to requirement
  But, not very sensitive to material budget  Can ToF be more dense?
epic 25.06.0
EICrecon 1.26.0
epic 25.06.0
EICrecon 1.26.0
Detector Requirements 0.5mrad @ 6GeV

## Slide 19: Sensor Position Study Kyohei

## Slide 20: Sensor Position Study: Motivation
Barrel TOF layout:
  Si sensor  ASIC  Si  ASIC  ...
  Both sided structure
The total material amount varies depending on the sensor position
  Inner sensor hit: Sensor → Support structure → ASIC
  Outer sensor hit: ASIC → Support structure → Sensor
Insensitive to scattering?

## Slide 21: Simulation setup: Sensor Position Study
Particle gun：
Events：10,000
Particle direction：
    ① Inner sensor only hits: ,
    ② Outer sensor only hits: ,
    ③ Both sensors hits: ,
Fixed Momentum：
Recent simulation versions
  epic version：25.06.0
  EICrecon version: 1.26.0
Take angular resolution with Residual method

## Slide 22: Sanity Check: BTOF Sensor Hit Distribution
Looks OK for X-Y hit distribution
Note: Maps integrate over Z-axis
Inner Only | Outer Only | Both side

## Slide 23: , by Sensor Position @ 6GeV
The inner sensor has better angular resolution than the outer sensor

## Slide 24: Angular Resolution vs Momentum by Sensor Position
Angular resolution varies significantly with hit location.
→ Certain structural layouts may achieve even better resolution than current designs.
Inner: 0.56 mrad
Outer: 0.72 mrad
Both: 0.63 mrad
Inner: 0.53 mrad
Outer: 0.68 mrad
Both: 0.59 mrad

## Slide 25: Angular Resolution vs. Momentum by Sensor Position
Position dependent angular resolution gap remains even in the no material baseline.
→ Difference is not driven by support structure material.
The cause of the effect of the position is still under investigation.

## Slide 26: Tentative summary
This study is ongoing to determine the upper limit of the material budget for BTOF and to optimize the detector design.
  Angle & Material Study
    Best θ and φ resolution at θ≈90°, but slightly less than the detector requirement of 0.5 mrad at 6 GeV
    The TOF support material of the barrel can also be a decisive factor.
  → Lighter options (carbon foam) keep hpDIRC resolution close to spec, but heavier options can cause PID performance to decline
  Sensor position study
    Angular resolution varies significantly with hit location.
  → Certain structural layouts may achieve even better resolution than current designs.
    Origin of the position effect is still under investigation.

## Slide 27: TOF PID performance in recent ToF software and geometry Kentaro Kawade & Kyohei Ono
ToF digitization is fully ready yet, we are using artificial smearing for hit timing

## Slide 28: Intro: PID
Generators
  Pythia NCDIS
    Nevents: 200k
    Energy: 18x275 GeV
  Particle Gun: pi/K/proton
    Nevents: 100k for each
    Eta&Phi: Flat
  epic ver 25.04.1
Reconstruction framework
  EIC Recon Version 1.24.2
Own developed offline analysis code
PID performance when considering finite timing resolution will be shown
This report focus on this only
ePIC PID requirement

## Slide 29: PID performance evaluation: Gaussian fit
Obtain each mass peak and its width
  inclusive 3 gaussian fitting
Introduce Figure of Merit (FoM), to assess the PID performance quantitatively
  μ: mass2 peak position
  σ: gaussian width
pion Kaon Proton

## Slide 30: Results: 0. No smearing
FoM
3σ separation
  pi/K Enough GeV
  K/p Enough GeV

## Slide 31: Results: 1. 33 ps smearing
FoM
3σ separation
  pi/K 1.4 GeV
  K/p 2.3 GeV

## Slide 32: Results: 2. 44 ps smearing
FoM
3σ separation
  pi/K 1.2 GeV
  K/p 2.1 GeV
This (44ps total timing resolution) is a realistic option

## Slide 33: Results: 3. 66 ps smearing
FoM
3σ separation
  pi/K 1.0 GeV
  K/p 1.6 GeV

## Slide 34: 3σ separation power vs eta
Perform same analysis differentially

## Slide 35: PID: Summary
PID performance study was performed based on single particle gun generator
  Generate uniform pion/kaon/proton
Checked impact from finite timing and tracking pathlength resolution
  Timing resolution is crucial for PID performance
    Ex) 44ps timing resolution
    3σ pi/K separation up to 1.2 GeV
    3σ K/p separation up to 2.1 GeV
Todo
  Study with PYTHIA eP collision
    Basically consistent, no different beyond stat error
  Perform same analysis for the EToF region (MC is ready)
  Signal + Background sample

## Slide 36: Summary and prospects
Digitization
  Many progress on BToF/EToF digitization but there are still a lot of Todo items
    Time walk/edge correction & Introduce CFD for BTOF
    Add noise to pulses and etc.
Impact of BTOF material budgets on the outer hpDIRC angular resolution
  Closed to the 0.5 mrad requirement for tracking
  However, not very sensitive to the BToF material budget
  How tracking resolution affects the overall PID performance at the hpDIRC?  Need input from hpDIRC
PID performance
  Estimating PID performance with recent software & geometry
  Looks fine for BToF, need to do for EToF as well
  Plan; PID performance with signal + background samples