## Slide 1: Experimental Nuclear Physics Division Support Group Report
Fast Electronics & Data Acquisition
‘FEDAQ’

## Slide 2: Status Report Overview
  Activity list in Hall B
  DAQ Readout Boards
  Trigger – (No report from me today)
  Discussion & Summary

## Slide 3
Mark Taylor
Armen Stepanyan
FEDAQ
Hall B Activities
FPGA power mezzanine
VMM power mezzanine
Base board
VMM
VMM
To GEM
FPGA
VTRx
(rad hard)
MGT power mezzanine
50 mm x 215 mm
128 channels
Original FastBus crates/modules removed and excessed
Over a thousand RG58 coaxial connectors re-terminated with Lemo plugs after removal of old circuit boards used with the 1872 FastBus ADC
New VXS crates have been received and tested.
  Installation in the hall by next week 17-Nov
New Trigger Fiber Optic cable has been ordered and patch panels received -> Complete
  Fiber patch cables need to be ordered
New single mode network fiber optic cable is installed New DAQ switch installed and cabled to the counting house.
Hall B Deck 2 North rack layout documentation started
6 of 7 VXS crates installed in equipment racks in Hall B, Deck 2 North area

## Slide 4
Mark Taylor
Armen Stepanyan
Jim Sheperd [Temp]
FEDAQ
Hall B Activities
VMM power mezzanine
Base board
VMM
VMM
To GEM
FPGA
VTRx
(rad hard)
MGT power mezzanine
50 mm x 215 mm
128 channels
Hall B – Space Frame – Deck 2 North – Rack layout
Network Gear and Trigger Fiber Panels in L2-1
VXS Crates
DAQ Modules
Cables from
HCAL in the floor
CAEN HV equipment
2025 March 3

## Slide 5
Mark Taylor
Armen Stepanyan
Jim Sheperd [Temp]
FEDAQ
Hall B Activities
VMM power mezzanine
Base board
VMM
VMM
To GEM
FPGA
VTRx
(rad hard)
MGT power mezzanine
50 mm x 215 mm
128 channels
Hall B – Space Frame – Deck 2 North – Rack layout
Network Gear and Trigger Fiber Panels in L2-1
VXS Crates – 6 of 7 installed
Note 3 crates are mounted from other side of racks
CAEN HV equipment
2025 March 3

## Slide 6
Mark Taylor
Armen Stepanyan
Jim Sheperd [Temp]
FEDAQ
Hall B Activities—Shown at last collaboration meeting
VMM power mezzanine
Base board
VMM
VMM
To GEM
FPGA
VTRx
(rad hard)
MGT power mezzanine
50 mm x 215 mm
128 channels
Hall B – Space Frame – Deck 2 North – Rack Photos
Will these cables be used?
RG213? RG6?
Large Coax cable
6 VXS Crates & DAQ Modules
Will reside here
CAEN HV equipment
What is this equipment used for?
Will need to identify and document system function.

## Slide 7
Mark Taylor
Armen Stepanyan
FEDAQ
Hall B Activities
VMM power mezzanine
Base board
VMM
VMM
To GEM
FPGA
VTRx
(rad hard)
MGT power mezzanine
50 mm x 215 mm
128 channels
Hall B – Space Frame – Deck 2 North – DEFINE Equipment EquipmentRack layout
Need to document this equipment!
What devices are connected to this equipment?
Cabling? Voltage/Current needs? Hazards?
Operating Procedures?
Required for ERR Preparations

## Slide 8: VXS Crate Configuration
Typical VXS Crate Setup: FADCs, VTP, SD, TI, CPU:
VTP receives integrated pulses from all FADC channels in crate to create trigger. Optical connections used to share information with other crates.
Common configuration used at Jlab
  21 Slot VXS crate
  Up to 16 FADCs (256 channels/crate)
  230 FADC250-v3 boards have been tested.
    28 will be delivered to the MOLLER DAQ group
    Balance will be installed in Hall B
  CPU for readout/config/monitor
    NEW Abaco SBC have been received
    Plan to install in Hall B before March lockup
  TI and SD synchronize & distribute clocks, triggers, sync to front-end
  VTP used to create trigger from FADC

## Slide 9
Mark Taylor
Armen Stepanyan
FEDAQ
Hall B Activities
VMM power mezzanine
Base board
VMM
VMM
To GEM
FPGA
VTRx
(rad hard)
MGT power mezzanine
50 mm x 215 mm
128 channels
Hall B – Space Frame – Deck 2 North – CAEN HV Status
Mark has tested all 7 mainframes and 2 have issues.
  Local control connection
There are a few spare power supply modules for these CAEN models so we can replace bad units and test again.
HV ‘Dummy’ load board fabricated and will be used to test each of the HV module’s outputs
Will verify and check the AC power connections
Is there a spare CAEN mainframe for backup during the experiment period?
2025 March 3

## Slide 10: FADC250-v3 Board Status
FADC250_V3
Production boards have been tested!!
There are firmware activities to continue for
Testing with the VXS Trigger Processor[VTP]
CODA Driver verification activities continue
Streaming ReadOut [SRO] test verification is
planned as well.
Optical Port – NOT populated
Used in Stand-Alone mode only
Xilinx Kintex Ultrascale FPGA
Single FPGA solution!
Significantly lower power than previous version
Reduced part count and same price as 2012
FEDAQ
H. Dong
E. Jastrzembski
J. Wilson
Ben Raydo

## Slide 11: FADC250-v3 Board Modernization
FADC250_V3
Acceptance testing of the new modules is extensive
Resolution at 4.88mV; Full scale range is 2V; 12bit; 250Msps
VME/VME2eSST
Gigabit serial data transfer to VTP – Will experiment need Streaming Redout Option?
VME Eprom programming
SDRAM testing
Low level and Full Crate Acceptance Test [FCAT] software is complete
FEDAQ
H. Dong
W. Gunning
E. Jastrzembski
J. Wilson
Ben Raydo

## Slide 12
  Old equipment removal performed safely and without issues
  Original coaxial cable cards re-terminated with Lemos
  Hall activities remain but we are making progress
  All DAQ modules are on site and tested
  New VME Cpu are on site
  Network and Trigger fiber cables installed
    Goal is to cable these to the new crates and run tests
  Topics not covered:
    Trigger setup for HyCAL and other detectors
    GEM DAQ configuration and integration with new VXS readout
    What are your questions?
Summary

## Slide 13: Backup slides
They said we were going “wireless”,,,

## Slide 14
Mark Taylor
Armen Stepanyan
Jim Sheperd [Temp]
FEDAQ
Hall B Activities
FPGA power mezzanine
VMM power mezzanine
Base board
VMM
VMM
To GEM
FPGA
VTRx
(rad hard)
MGT power mezzanine
50 mm x 215 mm
128 channels
25 New Abaco VME64x CPU modules ordered
  2eSST firmware verified to work with JLAB DAQ modules
New VTP boards received and tested
New Trigger Interface boards received and tested
New Signal Distribution [SD] boards received and tested
New Trigger Fiber Optic cable has been ordered and patch panels received
New Trigger fiber will have to be tested to Pie Tower and Trigger Supervisor
  Configure 7 new VXS crates and test with CLAS12 DAQ
  Plan to install new CPU, SD, TI, VTP before March lock up

## Slide 15
C. Dickover
B. Raydo
CEA Saclay** INFN*
More Examples of VXS Readout/Control of ASIC
2.5Gbps line rate 16bit bus @ 125MHz for transmit and receive
RICH 25,000 pixels
2.5Gbps line rate 16bit bus @ 125MHz for transmit and receive
SBS GEM
+40K pads
2.5Gbps line rate 16bit bus @ 125MHz for transmit and receive
MicroMegas
+20K strips
Forward Tracker
+3300 uMegas Strips
VME64x Readout Bandwidth [~200MBs]
OK Because Detector occupancy Is low (~1%)
Thomas Jefferson National Accelerator Facility
FPGA FEC**
DREAM
FPGA MPD*
APV25

## Slide 16
Thomas Jefferson National Accelerator Facility
This Design will carry JLAB DAQ for another decade!!
Amazing Electronic Device!

## Slide 17
Fast Electronics Streaming ReadOut Mode
FEDAQ
Streaming Read-Out – Experience
  Augment existing pipelined hardware developed for the 12GeV experiment program. ( Flash ADC – 12bit/250Msps, High speed Gigabit backplanes)
  Demonstrated high speed serial transmission that eliminates VME 200MByte/sec limitation
    VXS uses multiple Giga-bit serial links on back-plane for data transfer
    VXS Serial back-plane limit is 8GByte/sec
    VXS Trigger_Processor[VTP] data transfer limit presently: ~2GByte/sec
  VXS Trigger Processor with fADC250 boards on CLAS12 sub-detector used successfully during beam operations. [Forward Tagger]
    16 fADC250 Modules ReadOut with serial mode to VTP
    150MBytes peak data rates from Forward Tagger operated with beam
    VTP uses 10GbitEthernet links to DAq network system

## Slide 18
Streaming Without ‘Crates’
Readout/Control of ASIC <-->Network
FEDAQ Group
JLAB FPGA Readout/Control Board
192 Channel Interface
Algorithms
  1ns TDC
  Scaler
Fixed Latency up to 8us
Optical Ethernet – Use Commercial 1Gbe
  Finisar Transceiver capable of 10Gbps
  Artix could run @3.125Gpbs
Mates to ASIC
+5VDC @1A
Xilinx Artix7
INDRA Test Lab in CEBAF Center
Readout R&D lab for future 12GeV experiments
  - TDIS
  - SoLID
  - Moeller
Development of new Software for managing streaming data storage
Developing Software Framework for processing tasks. i.e.) Calibration, monitoring, reconstruction.
Use new COTS {Aritsta} network gear that includes high level FPGA for control of data stream
Development of High Level Synthesis code for creating ‘virtual triggers’ from streaming data
FPGA ReadOut & Control[ROC]
Develop interfaces with new ASIC:
Used MAROC3 for CLAS12 RICH and GlueX DIRC detectors
Petiroc 2A -> 32 Channel SiPM with Q and T conversion {10 bit ADC; 18ps timing[Prototype in development]
Innovation in Nuclear Data Readout and Analysis
Aritsta Network Switch
Uses Xilinx FPGA
Fiber Optic