## Slide 1
P. Varghese, M. Guran, L. Reyes, S. Raman, FNAL
14 October 2025
LLRF System Analysis for the
Fermilab PIP-II LINAC
PIP-II is a partnership of:
US-DOE
India-DAE
Italy-INFN
UK-STFC-UKRI
France-CEA, CNRS/IN2P3
Poland-WUST, WUT, TUL

## Slide 2: Outline
PIP2-LINAC Accelerator Components
LLRF System – SEL Architecture
3. Calibrations and SEL Operational Modes
Physics Requirements – LLRF Specifications
Analysis of Feedback Loops and Stability
Beam Loading in PIP-II cavities
7. Steps towards improving performance

## Slide 3: Fermilab Accelerator Complex

## Slide 4: Fermilab Accelerator Complex

## Slide 5: PIP2 4-Cavity RF Station

## Slide 6: PIP2 LLRF Systems
 | Station1 | Station2 | Station3 | Station4 | Station 5 | Station6 | Station7 | Station8 | Station9 | Station10 | Station11 | Total
 | RFQ, B1-4 | HWR | SSR1-1,2 | SSR2-1,2,3 | SSR2-4,5 | SSR2-6,7 | LB650-1,2,3 | LB650-4,5,6 | LB650-7,8,9 | HB650-1,2 | HB650-3,4 | 
Number of cavities | 6 | 8 | 16 | 15 | 10 | 10 | 12 | 12 | 12 | 12 | 12 | 125
RF Freq (MHz) | 162.5 | 162.5 | 325 | 325 | 325 | 325 | 650 | 650 | 650 | 650 | 650 | 
S3 – SSR1-1,SSR1-2
S4-S11 – SSR2 (7),
LB650 (9), HB650 (4)

## Slide 7: SEL Principle
Positive feedback configuration requires limiters
Loop phase offset is 2nπ of oscillation frequency
Cavity stored energy and field magnitude depends on the real or inphase(I) component of forward power
Detuning due to microphonics and other disturbances are compensated by the quadrature(Q) component
In GDR mode (SELAP) both positive(low gain) and negative(high gain) feedback loops are active
Key Features

## Slide 8: SEL System Architecture

## Slide 9: SEL System Calibrations
SSA Calibration
Gradient Calibration
Transmitted Power
Stored Energy from Reverse
Power during cavity decay

## Slide 10: Computing SEL Mode Limits
Real Power
Imag Power

## Slide 11: Computing SEL Mode Limits
SSA Calibration
Forward Power

## Slide 12: Gain Tuning Procedure LCLS-II
Increase system gain and check if SEL limits are exceeded
in the amplitude or phase feedback loops.
If one of the limits is crossed reduce closed loop bandwidth (system gain)
Till the outputs are within the SEL limits

## Slide 13: Stability Analysis with Bode Plot

## Slide 14: PIP-II Loop Delay Components
Assumed loop delay = 1 us
Delay | RFQ | Buncher | HWR | SSR1 | SSR2 | LB650 | HB650
Total | 985 | 1200 | 920 | 2720 | 2720 | 2770 | 2720
LLRF Controller Delay | 500 | 500 | 500 | 2100 | 2100 | 2100 | 2100
LLRF-Amplifier Drive (cable) | 50 | 150 | 20 | 70 | 70 | 70 | 70
Amplifier | 200 | 100 | 100 | 200 | 200 | 200 | 200
HPRF Distribution | 150 | 200 | 200 | 200 | 200 | 250 | 200
RF Fanback to LLRF (cable) | 85 | 250 | 100 | 150 | 150 | 150 | 150
Cavity half bandwidth (Hz) | 5542 | 8125 | 35 | 53.8 | 32.2 | 31.4 | 32.76
Gain (Max with 45 deg phase margin) | 23 | 16 | 3846 | 881 | 1462 | 1479 | 1430

## Slide 15: Disturbance Rejection and Regulation Requirements
PIP-II Specifications
Energy Stability(Linac) < 0.01%
Amplitude Regulation(individual cavity) < 0.06 rms %
Phase Regulation < 0.06 rms deg
Maximum detuning < 20 Hz

## Slide 16: Disturbance Rejection and Regulation – Amplitude Loop
When above limits are used
Stability analysis gives a max gain for SSR1 cavities of 880
Provided the box limits are increased

## Slide 17: Disturbance Rejection and Regulation – Phase Loop
For example, if
Stability analysis gives a max gain for SSR1 cavities of 880
Provided the box limits are increased

## Slide 18: PIP-II Cavity/Amplifier Parameters

## Slide 19: Beam Loading in PIP-II Cavities
PIP-II Beam Current = 2000 μA
LCLS-II Beam Current = 100 μA /300 μA
JLAB Beam Current = 400 μA
Cavity Description | Cavity Voltage (MV) | Forward Power – No beam (kW) | Forward Power – With Beam (kW) |  | Amplifier Max Power(kW)
HWR_6 | 2.008 | 2.64 | 4.45 | 1.3 | 7
SSR1_8 | 2.050 | 1.98 | 4.13 | 1.44 | 7
SSR2_5_4 | 4.993 | 6.40 | 11.92 | 1.36 | 20
LB650_5_3 | 11.88 | 15.93 | 28.97 | 1.35 | 40
HB650_4_2 | 19.953 | 24.28 | 40.71 | 1.29 | 70
Cavity Description | Cavity Voltage (MV) | Forward Power – No beam (kW) | Forward Power – With Beam (kW) |  | Amplifier Max Power(kW)
HWR_6 | 2.008 | 2.64 | 4.45 | 1.3 | 7
SSR1_8 | 2.050 | 1.98 | 4.13 | 1.44 | 7
SSR2_5_4 | 4.993 | 6.40 | 11.92 | 1.36 | 20
LB650_5_3 | 11.88 | 15.93 | 28.97 | 1.35 | 40
HB650_4_2 | 19.953 | 24.28 | 40.71 | 1.29 | 70
Feedback limits currently allow for 1.15 increase in power ratio
Feedforward beam loading compensation is needed

## Slide 20: Adding Gated Feedforward for Beam Loading
FF_I
FF_Q
+
+

## Slide 21: Adding Gated Feedforward for Beam Loading

## Slide 22: Beam Loading in SSR1 Cavity

## Slide 23: Beam Loading in SSR1 Cavity

## Slide 24: Steps Towards Performance I
  Add feedforward(FF) beam loading compensation(BLC)
  Gating of FF BLC with beam arrival trigger is required – PIP-II beam Duty cycle is only 1%
  DAC drive limits need to be adjusted for each cavity type due to differing beam/no beam power ratios
  Loop delays of ~ 3 μs can be improved with firmware changes
  Amplifier non-linearity should be handled correctly as a variety of amplifier sizes and vendors are being used
  LCLS-II and PIP-II linacs are using the same codebase – both projects will benefit from the improvements

## Slide 25
  The SEL Implementation for PIP-II was described
  Stabilty Analysis was used to determine theoretical feedback gain limits
  The beam loading for PIP-II cavities was compared with the output saturation limits currently being used
  The need for gated feed forward beam loading compensation was demonstrated
  Steps for improving performance were discussed

## Slide 26
Thank You!

## Slide 27
Backup Slides

## Slide 28: Beam Loading Power Calculation

## Slide 29: HWR Control Performance
Cavity 6
Cavity 7
Cavity 8
Detuning
Histograms
Cavity 4
Cavity 5
PIP-II Specifications
Energy Stability(Linac) < 0.01%
Amplitude Regulation(individual cavity) < 0.06 rms %
Phase Regulation < 0.06 rms deg
Maximum detuning < 20 Hz

## Slide 30: SSR1 Cryomodule Testing
Cavity1
Cavity2
Cavity5
Cavity3
Cavity4
Cavity6
Cavity7
Cavity8
Microphonics Detuning
Piezo Transfer Function – C1