## Slide 1: DESY. Update on LLRF systems
Low Level Radio Frequency Workshop
Newport News, VA, USA
13-16 oct. 2025
Julien Branlard, for the LLRF team

## Slide 2: DESY campus = construction site
CAST
Center for Accelerator Science and Technology (new control room)
Sept.2025
Artist’s view
DESYUM
New visitor center
(opening 2025)
Sept.2025
Artist’s view

## Slide 3: DESY campus = construction site
Innovation Factory
(Deep tech, startup, research and technology transfer)
Artist’s view
Sept.2025
Innovation Factory 2
(opening 2027)
Artist’s view
Sept.2025

## Slide 4: DESY campus = construction site

## Slide 5: FLASH
2021 - 2022 shutdown (10 months)
  ACC23 = 2 new cryomodules with cavities running on average at 28 – 29 MV/m
  ACC45 optimized waveguide distribution
  New energy 1.35 GeV
  New main oscillator
2024 – 2025 shutdown (14 months)
  photon beam line upgrade
    variable gap + apple-X undulators (FLASH1 beamline)
    new injector laser + provide external seeding
  LLRF
    modernizing legacy monitoring system (new racks, VME  MTCA)
    improving RF reference distribution to bring benefit of new MO to end users
Successive upgrades, back in operation since August 2025
MO designed in collaboration with ISE, Poland licensed to KVG
Integrated jitter:
< 12 fs [10 Hz to 100 Hz]
< 1.8 fs [100 Hz to 1 kHz]
< 0.8 fs [1 kHz to 1 MHz]
Oct. 2024

## Slide 6: EuXFEL
beam regions
Recent developments, currently shutdown (1st warmup since 2017 !), restart January 2026
new RF gun
new MO
Integrated jitter:
< 12 fs [10 Hz to 100 Hz]
< 2.1 fs [100 Hz to 1 kHz]
< 1.1 fs [1 kHz to 1 MHz]
benefit 1-to-1 from FLASH MO development
adapt LLRF to support any arbitrary setpoint waveform
energy savings
adapt LLRF to compensate for HPRF non-linearities
adapt LLRF for 2 input ports and probe pick-up
> 1 MW savings (Mio €)
Gun5 installation at XFEL (Sept. 2025)

## Slide 7: PETRA IV
PETRA III upgrade (construction phase 2029 – 2032)
Courtesy H. Reichert

## Slide 8: PETRA IV
PETRA III upgrade (construction phase 2029 – 2032)
Courtesy H. Reichert

## Slide 9: PETRA IV
PETRA IV upgrade
  Upgrade LLRF (MTCA.4-based)
    24 cavities at 500 MHz each 80 kW SSA
    24 cavities at 1.5 GHz each 10 kW SSA
PETRA III upgrade (construction phase 2029 – 2032)
Preparation
Test stand 500 MHz HOM-damped cavity installed and in operation at PETRA III with demons- -trator LLRF system
Hiring process
6 groups of 4+4 single cavity controls
MTCA.4 implementation
Courtesy N.O. Froehlich

## Slide 10: R&D
Scope include CW and Long Pulse operation, referred to as High Duty Cycle (HDC)
  distributed gradients ranges and Qext
  worse case: Ecav = 18-20 MV/m, Qext = 6e7
  expected microphonics ~ 3 Hz (rms)
LLRF control
  preferred approach would be 1 SSPA / cavity
BUT
  we might have to settle for vector sum control (8-16 cavities)
 Currently following both approaches
  investigating common-mode RF and individual piezo control (resonant filling)
Preparation for the EuXFEL CW upgrade
See Bozo Richter’s poster Wed. afternoon “Resonant filling for long pulse operation of EuXFEL using iterative-based FF”
GDR
Qext = 1.5 – 2.1e7
Pout = 1.7 – 2.2 kW
Ecav = 9 – 10.5 MV/m
Observer-based detuning computation
Piezo adaptive FF
RF FB
preliminary results
piezo adaptive FF
Courtesy B. Richter

## Slide 11: R&D
Courtesy B. Boghrati
image: https://www.sckcen.be/en
SIS8310 (Struck)  next generation, high-precision ADC
  Phase Noise: 0.52 fs [ 100 Hz – 100 kHz] Ampl. Noise: 5.1e-7 [ 100 Hz – 100 kHz]
  Prototyping phase
  Production planned for 2026
  RFSoC
    3rd gen. Zynq UltraScale+ (ZU47DR)
    8x 14-bit ADCs at 5 GSPS
    8x 14-bit DACs at 10 GBPS
    PCIe gen 4 (front and rear)
    First production batch Spring 2026
Applications
Beam diagnostics and fast orbit feedback for PETRA IV
LLRF for MYRRHA (accelerator-driven nuclear reactor in Belgium)
New MTCA developments for LLRF
Courtesy U. Mavric
evaluation phase
evaluation phase

## Slide 12: R&D
Carrier Suppression Interferometer
Demonstrated in the lab 60 dB noise floor improvement
Used in the LLRF detection chain
  out-of-loop phase -160 to –180 dBc/Hz
  100 as integrated jitter [10 Hz – 1 MHz]
Integrate CSI (carrier suppression interferometer) to LLRF control
L. Springer, et al. “Phase Noise Measurements for L-Band Applications at Attosecond Resolution” in IEEE Transactions on Instrumentation and Measurement, vol. 71, pp. 1-7, 2022, Art no. 8003307, doi: 10.1109/TIM.2022.3170975
F. Ludwig, et al. “RF controls based on carrier suppression detection with attosecond resolution”, Phys. Rev. Accel. Beams 28, 072803 – Published 31 July, 2025
Courtesy M. Hoffmann

## Slide 13: Summary : Projects Roadmap
2025 2026 2027 2028 2029 2030 2031 2032 2033 2034 2035 2036
FLASH
PETRA IV
~HDC R&D
iSAS
shutdown
operation
2020+
TDR
construction
operation
+LINAC II
+DESY IV
preparation
…?
XFEL
HDC
Construction
XFEL
operation
LIMP
operation
FOS
CDR
approval
(HDC upgrade)
deliverables
innovate for sustainable accelerator system European-funded project focused on efficiency and sustainability of accelerator systems

## Slide 14: References
1.3 GHz master oscillator, developed by DESY / ISE, licensed to KVG GmbH
https://kvg-gmbh.de/product/main-oscillator/
J. Branlard et al. “RF-based energy savings at the FLASH and European XFEL linacs”, in Proc. LINAC'24, Chicago, IL, USA, Aug. 2024, pp. 591-595. doi:10.18429/JACoW-LINAC2024-THZA003
L. Springer, et al. “Phase Noise Measurements for L-Band Applications at Attosecond Resolution” in IEEE Transactions on Instrumentation and Measurement, vol. 71, pp. 1-7, 2022, Art no. 8003307, doi: 10.1109/TIM.2022.3170975
F. Ludwig, et al. “RF controls based on carrier suppression detection with attosecond resolution”, Phys. Rev. Accel. Beams 28, 072803 – Published 31 July, 2025

## Slide 15
THANK YOU FOR YOUR ATTENTION !
MSK : group outing Sept. 2025
Contact
Deutsches
Elektronen-Synchrotron
www.desy.de
Julien Branlard
MSK
julien.branlard@desy.de
+49 (0)40 8998 1599

## Slide 16: BACKUP SLIDES

## Slide 17: R&D
uLOG LO + REFER distribution board (uLOG)
DESY licensed production to company KVG GmbH
  Series production at 1.3 GHz and 1.5 GHz
  Production test stand to test each subcomponents

## Slide 18: R&D
TCK7  FMC2ZUP
SIS8300  SIS3rd generation ADC
uLOG  uLOG next generation
  DESY licensed production to company KVG GmbH
  Production of 10x 1.3 GHz and 3x 1.5 GHz modules (HZB)
  Development of test stand to test each subcomponents
New MTCA developments for LLRF
Courtesy Uros Mavric
TCK7
ZUP + 2x FMC

## Slide 19: R&D
Two CW-capable tests stands
  Test of 3.9 GHz in CW at XATB1 (SSA)
  Test of 1.3 GHz in CW/LP at CMTB (IOT)
Development of a waveguide Q-tuner : goal is to extend QL tuning range (up to 1e8) w/o changing cryomodules
Continuous wave (CW) and Long Pulse (LP) R&D at XFEL
Dynamic heat load measurement as a function of duty cycle
CW test with 3.9 GHz module in XATB1
CW tests with 1.3 GHz module in CMTB

## Slide 20
R&D for the HDC upgrade
Understanding efficiency optimization and maximum beam energy vs cryo capacity
Extending external coupler (Qext) range
Current max Qext = 1e7
Possible HDC Qext = 5e7
Waveguide Q-tuner offers a factor 10 increase in Qext
0 10 40 60 80 100
Motor position (%)
14
12
10
8
6
4
2
0
Qext scale (a.u.)
Establishing the maximum dynamic heat load
Assessing limit with heaters, with CW RF, at the cavity level, at cryomodule level
unstable operation
20W
10W
3020W
40W
50W
60W
70W
80W
90W
Time
meas.
simul.
Major impact on efficiency of the accelerator
Major impact on the maximum beam energy

## Slide 21
R&D for the HDC upgrade
RF source options and thermal impact on input couplers
Investigating RF source options
Consider max power, efficiency, foot print, noise performance, cooling, etc..
4 kW SSA in AMTF
40 kW IOT in CMTB
Assessing coupler heating
Assessing limit of coupler heating when operating in CW
Pin = 3 kW
XM46.1

## Slide 22: R&D
Continuous wave (CW) and Long Pulse (LP) R&D at XFEL
XFEL : can we increase the current 1.3 msec pulse to 2, 3 ms without changing the hardware ?
  Pulse stretching (affects read / write tables)
  Affects diagnostics (detuning, performance computation etc…)
  Tests at XFEL
Sept 2021 : longer beam time by shortening fill time and lowering QL (4.6e6  2.5e6)
A13 665  1000 usec flat top
March 2022 : longer beam time by using extended modulator pulse
A10 665  970 usec flat top
QL = 4.6e6
Tfill = 750 usec
QL = 2.5e6
Tfill = 400 usec
Tbeam = 650 usec
Tbeam = 1000 usec

## Slide 23: R&D
MAGO revival (Microwave Apparatus for Gravitational waves Observation)
  Pick up MAGO project (from early 2000) driven by CERN at the time
  Use binary cell SRF cavity as possible detector for gravitational waves
  LLRF in SEL combined with CSI to improve SNR
LISA (Laser Interferometer Space Antenna)
  Development of detector electronics (non-LLRF)
Gravitational waves
MAGO cavity at DESY
CSI setup
Image ESA
Courtesy Louise Springer