## Slide 1
High-Precision LLRF System
for the Upgrade of SXFEL
Chengcheng Xiao, Yiming Xu, Chenyu Wei, Wencheng Fang
Microwave Group
Shanghai Advanced Research Institute. CAS
Oct.13 2025, Newport News

## Slide 2: OUTLINE
Introduction of SXFEL
Hardware Design
Frimware Design
Experiments performed at SXFEL

## Slide 3: SSRF CAMPUS

## Slide 4: SXFEL LINAC
LINAC in SXFEL is composed of five S-band accelerating units, two S-band deflecting cavities, twelve C-band accelerating units, one X-band accelerating unit, one C-band deflecting cavity, and two X-band deflecting cavities. At the end of the linear accelerator, the beam reaches a final energy of 1.5 GeV
Layout of SXFEL LINAC
Accelerating Gradient | 
S band/ C band/ X band | 20MV/m 37MV/m 10MV/m
Voltage of Deflecting Cavity | 
S band/ C band/ X band | 2MV 10MV 20MV
Microwave stability | 
S band C band X band | 0.09º(rms)，0.04%(rms) 0.18º(rms)，0.04%(rms) 0.36º(rms)，0.04%(rms)
Pulse width | 0.1-5 uS
Repetition Rate | 1-50 Hz
Accelerating structure parameters

## Slide 5: LLRF Subsystem
VM-modulated signal generated by the LLRF is first amplified by the solid-state power amplifier , then the output signal is amplified by a 50 MW klystron, subsequently boosted by the pulse compressor, and ultimately delivered to the accelerating structure
LLRF / SSA/ MODULATOR/ KLYSTRON
Microwave Subsystem

## Slide 6: LLRF Subsystem
LO/CLK Generator
Solid State Amplifier
Function Description | Generation of Clock and LO signals
Reference Frequency | 2856 MHz/5712 MHz
LO | 2829.556 MHz/5685.556MHz
CLK | 105.77 MHz
LO Added Phase Jitter | ＜15 fs
CLK Phase Jitter | ＜100fs
Function Description | Provides driving power for the klystron
Working Frequency | 2856MHz /5712MHz
MAX power | 62 dBm/55 dBm
Stability | AMP 0.03%，PHA 0.03O /AMP 0.03%，PHA 0.06O

## Slide 7: Hardware Design
8 RF down-conversion channels
Vector Modulator that drives DAC-generated I/Q signals with a reference source
The design achieves short-term amplitude stability better than 0.015%, while maintaining phase jitter below 25 fs (rms) within the 10 Hz–10 MHz offset range
8 Channels
AC
VM
Reference
（VM）
IF
LO
IN
IP
QN
QP
LTC5562
SMA
Frequency Mixer/ Vector Modulator

## Slide 8: Hardware Design
Independent down-conversion modules and vector modulation (VM) modules
Metallic shielding is employed to secure inter-channel isolation exceeding 70 dB
Multi-stage low-pass filters are employed to suppress harmonic components
Rogers dielectric materials are utilized to support efficient and stable high-frequency signal transmission
Stabilized power supply modules are integrated to eliminate ripple-induced disturbances
Frequency Mixer/ Vector Modulator

## Slide 9: Hardware Design
DSP Board Design

## Slide 10: Hardware Design
16 Layers
Based on Zynq MPsoc
8-channel 310 MSPS 16bit ADCs
4-channel 500 MSPS 16bit DACs
8-channel DC ADC sampling
Seperate CLK distribution for ADC and DAC
FMC interface
SSD/micro SD
DSP board

## Slide 11: Hardware Design
Cooling Matters!
FPGA
Power Management
Ethernet
ADCs
...

## Slide 12: Hardware Design
DSP Board
Frequency Mixer/ Vector Modulator
WR Mezzanine Card

## Slide 13: Firmware Design
SystemGenerator aided function design
SysGen automatically generates Verilog code according to schemtic
Running at 100-MHz CLK, same with the ADCs & DACs
Packaged module simplifies the design, so more attention is paid on the function and timing rather than data type
4 times pipeline IQ demodulator
Output I/Q component at 100 MHz

## Slide 14: Firmware Design
16-bit AD/DA leads to 16-order real-time pipeline CORDIC
Output 15-bit amplitude and 17-bit phase at 100 MHz
Output is used by algorithms directly

## Slide 15: Firmware Design
Multiple operation mode
Sel register controls the mode, which can be set online by Linux
Enhance flexibility and universality
Amp.
Bus
0
Sel
A-PID
A-set
Phase
Bus
0
Sel
P-PID
P-set
Freq.
Bus
0
Sel
F-PLL
Σ
+
CORDIC
Phase
Amp.
I
Q
DA1
DA2
+
+
+
+
I-offset
Q-offset
+
+
+
+
1
2
3
1
2
3
1
2
3
Mode | Function
0 | Turn off
1 | Continuous-wave PID control
2 | Continuous-wave PLL control
3 | Pulse-wave (repetition rate: 1~1000 Hz; Duty range: 0.01~100%)
4 | Feedforward table output of any waveform
… | To be continue
Modules of all modes are connected to 3 buses

## Slide 16: Firmware Design
CORDIC output from PL is buffered in RAM pending retrieval by PS
A Finite State Machine (FSM) manages a counter and a RAM to facilitate waveform recording
Resolution Switch module uses an integer value to control data recording rates. It generates a single-clock-wide pulse (logic high) every clock cycles and remains at logic low otherwise
Cover a wide range of time scales
Observable time window can be adjusted from 20 µs to 80 ms, with a corresponding time resolution ranging from 10 ns to 40 µs
Multi-resolution waveform recorder
State transition diagram of the FSM

## Slide 17: Experiments performed at SXFEL
Absolute time stamp is incorporated on a pulse-by-pulse basis, enabling seamless interfacing with the WR pulse, bunch ID, and timing information supplied by the control system
Time-stamp column replacement is applied to the PVs, thereby facilitating pulse-by-pulse diagnostics for beam commissioning personnel
WR Mezzanine Card Test
EPICS PV Edit
Pulse /Bunch ID in Vivado

## Slide 18: Experiments performed at SXFEL
VM signal stability test(C band)
PYDM interface
Experimental results demonstrate that the VM output achieves amplitude stability better than 0.015% (RMS) and phase stability better than 0.015 degrees (RMS) under 5712 MHz
At the input of the accelerating structure, the measured amplitude stability is better than 0.03% (RMS), while the phase stability is better than 0.03 degrees (RMS)

## Slide 19: Experiments performed at SXFEL
C band LLRF in SXFEL
S band LLRF in SSRF LINAC
S band LLRF in RF-Gun Test Stand

## Slide 20: Summary
New S/C band LLRF system was developed for SXFEL/SSRF facility and is working well
  White Rabbit Compatible
  High-performance, high-sampling-rate ADCs and DACs
  Comprehensive range of interfaces
  PS-PL instead of CPU-FPGA
X band LLRF system is under developing
Intra-pulse MPC control is under developing
Ongoing efforts are focused on exploring how AI can be integrated to enhance system’s capabilities

## Slide 21: Thank you for your attention!