## Slide 1: Advanced LLRF Automation and Diagnostic Strategies for Horizontal Testing of HIAF SRF Cavities
Feng QIU, Yuan HE, Lijuan YANG, Zheng GAO, Jiayi PENG, Tiancai JIANG (IMP)
Rihua ZENG (Dongjiang Lab)
The Low Level Radio Frequency Workshop 2025 (LLRF2025)

## Slide 2
RF Parameter Characterization
Summary
Introduction
01
02
04
CONTENTS
Automation, Diagostic & Opt.
03

## Slide 3: Introduction
CiADS&HIAF (Hui zhou)
  HIAF: High Intensity heavy-ion Accelerator Facility
  CiADS: China Initiative Accelerator Driven System
Architectural Rendering
HIAF (High Intensity heavy-ion Accl. Facility)
HIAF and CiADS
Taipingling Nuclear Power Plant
2 km
Aerial View
iLINAC
IMP (Lan zhou)
Two new large-scale facilities were built in Hiuzhou, Guang Dong Province

## Slide 4
Motivation and facility layout
Isotope Terminal
Radioactive Beam Line
External Target Terminal
T1
BRing
iLinac
SECR
HFRS
SRing
High-Energy Density Terminal
T2
Hyper nuclear Research Facility
Properties of Nuclear Matter
High-Energy Irradiation - Single Particle
T3
T4
T5
High-Precision Toroidal Spectrometer
Electron-Ion Recombination Spectrometer
T6
Project Engineering Objectives
Expanding the Landscape of New Nuclides
Weakly Bound Nuclear Structure and Reaction Mechanisms
Precise Measurement of Nuclear Masses
Ions targets：
5-250 MeV/u CW heavy ions beam
35 MeV/u-5.7GeV/u pulse beam
HIAF Facility

## Slide 5: HIAF-iLINAC
17MeV/u
(238U35+)
SECR
0.8MeV/u
β =0.04
β =0.19
β = 0.076
f = 81.25 MHz
β = 0.15
f = 162.5 MHz
LEBT
RFQ
QWR007
HWR015
MEBT
SSA
ions | Q/A | intensity | Energy (MeV/u) | Operation mode
238U35+ | 1/7 | 1.0 emA | 17 | Pulse
78Kr19+ | 1/4.1 | 1.0 emA | 27 | 
18O6+ | 1/3 | 1.0 emA | 33 | 
H2+ | 1/2 | 0.6 emA | 48 | 
48Ca-70Zn | - | 10 pμA | 4-8 | CW
Xe-U | - | 10 pμA | 5-22 | 
iLINAC layout and parameters
iLinac Design Specification：Continuous wave (CW) and pulsed beam
Component Structure : Room temperature front end and Superconduct linac
...
...

## Slide 6: SRF Cavities
 | QWR007 | HWR015
CM Quantity | 6 | 11
CM Length [mm] | 5073 | 5836
CM Width [mm] | 2000 | 2000
CM Height [mm] | 3800 | 3800
Cavity Quantity | 5 | 6
Solenoid Quantity | 5 | 2
BPM Quantity | 4 | 1
SECR
0.8MeV/u
LEBT
RFQ
QWR007
HWR015
MEBT
5.3MeV/u
17MeV/u
SOL
QWR
SOL
QWR
SOL
QWR
SOL
QWR
SOL
QWR
SOL
HWR
HWR
HWR
SOL
HWR
HWR
HWR
CM-QWR007 (x6)
CM-HWR015 (x11)
QWR007 (x6): 30 cavs
HWR015 (x11): 66 cavs.
Helium gas storage station
Cold box
~100 m
  HIAF SRF linac employs 17 cryomodules with 96 SRF cavities

## Slide 7
Low Level RF
  Hardware:
  ADC (×8): ADS42Ib69, 16-bits, 250 MHz
  DAC (×2): AD9747, 16-bits, 250 MHz
  FPGA: XCZU19EG
  ARM: 19eg
  Motor Tuner
  Algorithm:
  A/P ctrl.
  Individual ctrl.

## Slide 8
RF Parameter Characterization
Summary
Introduction
01
02
04
CONTENTS
Automation, Diagostic & Opt.
03

## Slide 9
Calibration of QL under impedance mismatch
Error ↓ from ±30 % to ±2 %
Consistent with network-analyzer scan
Imp. mismatch
Before cali：Err~±30%
After cali.：Err~±2%
RF off
Detuning-dependent
Field decay
J. Y. Ma,… F. Qiu* et al., Measurement of the cavity‑loaded Q factor in SRF systems with mismatched source impedance, Nucl. Sci. and Tech. 34:12, 2023
J. Y. Ma,… F. Qiu* et al., Application of a new cavity-loaded factor calibration algorithm on the Test Stand 2 facility at the European, Radiation Detection Technology and Methods, 8:4, 2024
3dB half-bandwidth (f0.5,scan)
The residual Vf after RF off
Scan
Decay
Measurement of QL

## Slide 10
  Rise and decay-based QL measurement agree well
  During quench, decay-based QL drops rapidly (f0.5 ↑), while rise-based remains stable → providing a possibility for quench detection
Decay-based
Rise-based
Rise-based
Decay-based
Rise-based
Decay-based
Measurement of QL (cont’d)
Quench onset field

## Slide 11
Static LFD coefficients
A. Bellandi et al., IEEE Transactions on Nuclear Science, vol. 68, no. 4, pp. 385-393
  Procedure for static LFD measurement:
  Measure dynamic frequency detuning during RF pulse.
  Extract steady-state detuning at flat-top and record the corresponding .
  Perform a linear fit of versus ; the slope gives the static LFD coefficient.
For nearly 80% of the cavities, lies in 0.1–0.2, with just one cavity above 0.6
-0.66

## Slide 12
Dynamic LFD Model
F. Qiu*, Z. L. Zhu, J. Y. Ma et al., An approach to characterize Lorentz force transfer function for superconducting cavities，Nucl. Instrum. Methods Phys. Res. A 1012 (2021) 165633
：Epeak
：
LFD Model
KLFD
KLFD
Grey-box Model
greyest
  Grey-box identification yields the cavity mech. mode from Epeak and ΔfLFD, revealing 4 dominant modes
  coincides with the
  static Lorentz detuning coefficient
Static LFD coefficient
Notes: By applying grey-box system identification using and the measured Lorentz-force detuning, the transfer function of the cavity mechanical modes can be obtained, allowing estimation of the dominant modes.
The low-frequency limit of the identified mechanical transfer function () agrees well with the static Lorentz-force detuning coefficient.

## Slide 13
Pressure sensitivity
  Cavity pressure sensitivity coefficient (df/dp) is determined from helium-pressure induced detuning, with detuning extracted from the decay-phase slope of RF pulses
For ~80% of the cavities, the pressure sensitivity () lies in the 3–7 Hz/mbar range.

## Slide 14
Peak gradient
CM4
CM5
  The average Epeak​ in closed-loop operation is ~33 MV/m, exceeding the design value of 28 MV/m
  Most cavities show field-emission onset above 20 MV/m
Radiation Dose [μSv]
104
100
102
Radiation Dose [μSv]
104
100
102
Peak gradient [MV/m]
Peak gradient [MV/m]

## Slide 15
  Automated batch measurements of cavity parameters: ,(decay-based, rise-based and frequency scan) static LFD coefficient (KLFD), and pressure sensitivity (df/fp)
Cavity Loaded Q
Static LFD Coefficient
Measurement Automation

## Slide 16
RF Parameter Characterization
Summary
Introduction
01
02
04
CONTENTS
Automation, Diagostic & Opt.
03

## Slide 17
  Automated RF conditioning enables adaptive power ramp-up with real-time interlock and vacuum protection, achieving safe, efficient, and unattended cavity processing.
  Key steps: initialization → power ramp-up → interlock/vacuum control → auto recovery → data logging.
Automated RF Conditioning

## Slide 18
Automated RF Loading
  The RF control system automatically loads and initializes all superconducting cavities in pulse mode.
  Each cryomodule is sequentially powered and monitored through the automated startup interface.

## Slide 19
Expert experience-based Feature-Extraction
Feedline mismatch
Sawtooth type
Sawtooth type
Flatroof
Multipacting
  Features are extracted from RF conditioning data.
  Machine learning automatically identifies abnormal events — feed-line faults and multipacting.
Sawtooth type
Flatroof
Normal
ML-based Abnomal Recognition

## Slide 20
Bayesian Opt. for Pulsed RF Ctrl.
  Bayesian optimization is used to tune six coupled parameters in pulsed SRF operation, including PI gains (A/P loop), feed-forward amplitude (Fₐ), and feedback activation time (TFB).
  This approach minimizes RMS fluctuations at loop closure and enhances amplitude–phase stability during the beam flat-top.
Metrics:

## Slide 21
RF stabilities
  Bayesian optimization significantly improves both intra-pulse and pulse-to-pulse RF stability
  Amplitude and phase stabilities during the flat-top are reduced to 0.02 % and 0.02 deg, while long-term pulse-to-pulse stability remian below 0.001 % and 0.003 deg
Before Opt.
After Opt.
Pulse-to-Pulse
0.02%
0.02 deg
Notes: %

## Slide 22
RF Parameter Characterization
Summary
Introduction
01
02
04
CONTENTS
Automation, Diagostic & Opt.
03

## Slide 23: Summary
  An integrated LLRF automation framework was developed, enabling automatic measurement of key cavity parameters — loaded Q, Lorentz-force detuning coefficient, and pressure sensitivity
  Real-time batch operation was achieved for automated RF conditioning and pulse-mode loading across multiple superconducting cavities
  Machine-learning-based intelligent diagnosis automatically identifies abnormal RF conditioning events, such as multipacting and feedline mismatches
  Bayesian optimization of loop parameters in pulsed operation improves amplitude and phase stability by nearly one order of magnitude

## Slide 24
Thanks for your attention

## Slide 25
Back-up Slides