## Slide 1
Advanced Photon Source Upgrade Digital LLRF Systems Summary
T. Berenc, M. Borland, J. Calvey, T. Madden, O. Mohsen, A. Nassiri, Y. Yang (ANL)
J. Breeding (Cutting Edge Communications, LLC)

## Slide 2
Intent
Booster
PAR
Linac
Storage
Ring
To share a few LLRF topics and experience that may be of interest, even if not necessarily novel.
Outline
APS-U Storage Ring Systems
  Specifications and Simulations
  RF Noise Suppression System
  Bunch Lengthening Cavity
Injectors
  Particle Accumulator Ring

## Slide 3
APS-U RF Overview
1.1km 6GeV 4th generation synchrotron light source
  original 7GeV ring completely dismantled
main RF systems reused with modifications
  12 cavities now instead of 16
  klystron 60Hz harmonic noise suppression
superconducting Bunch Lengthening cavity
  improves lifetime and emittance
Injectors kept intact with some upgrades
  increased beam-loading, 2nC → 20nC
  digital LLRF in Particle Accumulator Ring
new ring-to-ring Timing & Synchronization[1,2]
Booster
PAR
Linac
Storage
Ring
[1] U. Wienands et. al. IPAC 2018, MEPAF007
[2] U. Wienands et. al., LLRF 2024 Topical Workshop

## Slide 4
Storage Ring - Specifications
Minimize re-design of existing main (352MHz, h=1296) RF systems
new 4th harmonic (1408MHz) passive superconducting Bunch Lengthening System (BLS)
  QL = ~7e6, (R/Q)a = 104 Ohm, BW3dB = ~ 200 Hz, single-cavity V=~1MV
  detuning (~ +10kHz) contributes to growth of longitudinal oscillations
4
(Mike Kelly, et. al.)
Bunch Lengthening Cavity
Main RF System (352MHz)
[3] M. Kelly et. al. IPAC 2024, MEPS10
[4] J. Fuerst et. al., MEDSI 2025, WEOC04

## Slide 5
Storage Ring - Specifications
Beam Stability Specifications
    beam orbit stability
      horizontal: 1.25µm, 0.25µrad
      vertical: 0.4µm, 0.17µrad
    beam energy noise: <1.3e-4 (10% of energy spread)
RF Specifications were guided by existing performance → required improvements
  Are the existing noise levels tolerable?
    with regards to beam stability
    with regards to effects on longitudinal feedback system
  Is the beam-cavity interaction stable under new conditions?
    including the bunch lengthening cavity
5
[5] APS-U Functional Requirements Document (FReD)

## Slide 6
Storage Ring - Specifications
Are the existing noise levels tolerable?
Is the beam-cavity interaction stable under new conditions?
6
[6] M. Borland, ANL/APS LS-287 (2000) latest at v2025.2
[7] https://ops.aps.anl.gov/manuals/elegant_latest/elegant.pdf
[8] T. Berenc, M.Borland, IPAC2015, MOPMA006
developed a model for RF feedback to include in elegant[6-7] particle tracking simulations [8]
  included ability to inject noise
RF system time-domain noise measurements used in simulations
  no surprise: our 1MW klystrons are the dominant source of RF noise
  for stability specs: factor of 3 improvement → 0.075% rms, 0.1deg rms [1kHz BW]
  to prevent longitudinal feedback system saturation: goal of factor of 10 improvement
Collaborate with Physicists early in the system design process

## Slide 7
Storage Ring - Simulations
7
[9] Berenc et. al. - LLRF 2017
RF feedback integrated into elegant RFMODE element
feedback in amp/phase or I/Q, individual custom filters
parametric and additive noise for generator and receiver
can model feed-forward using generator I/Q noise inputs

## Slide 8
RFNS OFF vs. RFNS ON
We gratefully acknowledge the computing resources provided on Improv, a high-performance computing cluster operated by the Laboratory Computing Resource Center at Argonne National Laboratory.
10,000 particles per bunch,
216 bunches (2.16M particles)
100,000 turns
~6 hours on 128 cores (AMD EPYC 7713 64C 2GHz processors)
Simulations

## Slide 9
RFNS OFF vs. RFNS ON
Simulations

## Slide 10
RFNS OFF vs. RFNS ON
Modes 1-107
Mode 0
Mode 0
Modes 1-107
Simulations – Longitudinal Coupled Bunch Modes
We learned:
for a Passive Bunch Lengthening Cavity
Mode0 synchrotron tune is still dictated by the Main RF voltage
Robinson instability still dictated by Main RF conditions (i.e., generator)
Higher order coupled bunch modes see a synchrotron tune shift from the flattened potential well created by the Mode0 induced voltage
[10] R. Lindberg, M. Borland, private communication

## Slide 11
RF Noise Suppression – targeted 60Hz harmonics
Some constraints
existing systems are purely analog-based
the way the 1MW klystron-based systems are regulated
  fixed RF drive (saturation), global amp. control is limited, ~100Hz BW mod-anode feedback
  phase loops straight forward: inner loop around klystron, outer-loop around cavities
Approach: minimize RF noise at the source, don’t let it get into the cavities in the first place
11
[11] T. Berenc et. al., LLRF 2024 Topical Workshop

## Slide 12
RF Noise Suppression – some results
Specifications
0.075% rms, 0.1deg rms [1kHz BW]
future RFNS improvements
presently adding harmonics
will explore wideband changes

## Slide 13
RF Noise Suppression – some results
Beam Jitter
horizontal rms motion
at dispersive P3 BPMs
energy noise spec: <1.3e-4
horizontal rms motion
near IDs (P0 BPMs)
beam orbit stability spec
horizontal: 1.25µm, 0.25µrad
vertical: 0.4µm, 0.17µrad
Girders have a 30Hz vibration that is being addressed.
measured vertical: ~1um
future RFNS improvements
presently adding harmonics
will explore wideband changes
Solid State in the future
Klystrons will be replaced with Solid-State Amplifiers. Phase noise is nearly 20dB less over 1kHz bandwidth

## Slide 14
Bunch Lengthening System
Bunch Lengthening Cavity is a passive cavity (i.e., purely beam-driven)
Positive detuning (i.e., fres > frf), beam drives cavity at nearly +90deg impedance angle
QL and ∆f adjust both the magnitude and phase of Vcav
We have adjustable couplers, but we do not adjust them
∆f is adjusted via a pneumatic tuner
  we regulate the tuner pressure
  tuning is held fixed to achieve desired Vcav at operational beam current
Quench detection is simply based upon the difference between expected and actual |Vcav|
use BPM sum signal and field probe, assume steady-state
scaling factor k represents impedance magnitude
works for all beam currents (i.e., when filling the ring)
also detects over-voltage (e.g., mis-tuning)

## Slide 15
Bunch Lengthening System - Quench
Passive cavity
  have to use beam for conditioning
  cavity protection must dump beam
Quench detect circuit
  uses low-pass filter on
    this prevents spurious trips (e.g., during swap-out)
  includes adjustable delay to allow multiple breakdowns before dumping beam
Detuning, ∆f, can be determined by looking at magnitude oscillations at beam injections, or dø/dt at beam dump
Quench during BLS commissioning
Cavity Voltage and Beam
Quench Detect ∆V
|Vcav| ringing @injection
ø Rotation during dump

## Slide 16
Bunch Lengthening System
Turning back on after maintenance shutdown
sudden initial transient followed by oscillatory response
bump in Helium pressure was seen
Oscillations at ∆f , similar response to stepped drive
  Beam rides through it, can’t respond at ∆f = ~20kHz
beam is nearly a perfect current source
  not a generator which becomes mismatched
Is this multipacting driven with an ideal current source?
Recent Event not yet understood
Cavity Voltage and Beam
Phase
Zoom: Vcav and Beam

## Slide 17
Particle Accumulator Ring
PAR 9.78 MHz (h=1)
PAR 117 MHz (h=12)
digital LLRF started with these systems.
  successful collaboration with SNS and John E. Breeding
  tight integration w/ Data Acquisition [12]
same codebase used for BLS, RFNS
Fundamental & Harmonic in Operations
  Ferrite tuners on both
  Harmonic used for bunch compression
Extensive effort for transfer to operations
  spreadsheets of all PVs + fields
  alarm levels, and alarm handlers
  Turn-on and alarm response instructions
[12] T. Madden, Wednesday poster session

## Slide 18
Future Directions
RFNS – additional 60Hz harmonics
PAR – fast voltage modulations for beam manipulations
Booster – digital LLRF and transient beam-loading compensation
Storage Ring – LLRF for Solid-State Systems
Linac Photo-Cathode Drive Laser – timing & synchronization
Thanks for Listening