## Slide 1: Anomaly Detection in the CERN Proton Synchrotron RF Systems Using Machine Learning
Presenter: Joel Wulff
Date of presentation: 15/10/2025
Low Level rf conference 2025, Newport News, VA, USA
Acknowledgements: A. Lasheen, H. Damerau, B. Woolley, F. Velotti, M. Algelly, P. Ellison, PS-OP, SY-RF experts and piquet

## Slide 2: Introduction - The CERN PS
The CERN accelerator complex
A network of accelerators and experiments
The Proton Synchrotron: one of the earliest accelerators in the chain

## Slide 3: Introduction - The CERN PS
The CERN accelerator complex
A network of accelerators and experiments
The Proton Synchrotron: one of the earliest accelerators in the chain
Serves as both pre-injector to the LHC, and delivery accelerator to a large range of proton/ion experiments (with varied beam requirements).
Requires flexibility and extreme reliability
→Possible only with through excellent use and maintenance of its many RF systems!
You are here!
Circumference ~ 1 Newport News lake
PS

## Slide 4: Introduction - PS RF systems
Figure from H. Damerau
Wide range of:
  RF frequency: from 2.8-200 MHz
  Hardware/ages
  → Complicated to monitor, maintain, and diagnose…
Many potential sources of faults (meaning downtime)
External
E.g, B-train missing, Beam based, electrical glitch
Low-level RF
E.g, Feedback loop, Frontend computer faults, missing signals
High-level RF
E.g, Gap relay failures / early closures, Cavity tuning errors, amplifiers
To understand/prevent failure modes, need to understand root-causes.
→ Requires good diagnostics!

## Slide 5: Past experience
Constant efforts needed to keep the PS running at high availability (98%+ for RF)
Real time fault analysis often inefficient
  Lack of tools for operators/RF experts to guide diagnostics, difficult to overview the whole accelerator and easy to feel overwhelmed.
  Multiple calls when issues occur: to Low/High-level on-call personnel, equipment experts → High engagement of personnel!
How can we guide the investigation process, to know where to start, to become more efficient and proactive?
5
Postmortem diagnostics and review become tedious and time-consuming
  Information distributed, few links between tools
  → Extensive investigation by experts often necessary for finding root cause

## Slide 6: Towards proactive diagnostics
We need a solution/tool that is:
Capable of constantly monitoring systems → Warn early (ideally before fault?)
Generic→ a “recipe” that can scale to more than one type of equipment
Can correlate/monitor many systems → enable root-cause analysis
Idea: Exploit the large amount logged, measured signals and known settings to monitor the state of our systems, and provide a warning when things look not “normal”
Anomaly Detection

## Slide 7: Reconstruction based Anomaly Detection (AD): Auto Encoders
Basic idea: use in-distribution data (non-anomalous) to train an ML model
Normal signal
Anomalous signal
(Recon.) Normal signal
Train
Test
(Recon.) Anomalous signal
Learn to recon. well!
Recons. poorly…
Backpropagation of unsupervised reconstruction loss.
Similar methods explored for other systems at CERN: M. Algelly et. al. for KFA71 kicker

## Slide 8: Reconstruction based AD: Auto Encoders → PS RF 10 MHz cavities
Main RF system of the PS: 10 units (+1 spare)
Both programmed and measured voltages available
loss = Mean Square Error residual between inputs/outputs.
anomaly score calculated for each timestep using residuals.
An anomaly threshold can be set (based on training data and testing on known anomalies).
Timesteps with anomaly score above thresh. are flagged.
Autoencoder
+ Beam intensity!
Recon. loss
Notes: Explain why 10MHz is the obvious choice for pilot: 10 units, statistics, program and measured setting, main RF system

## Slide 9: Collecting a dataset
Unsupervised logged data: no labels available for anomalous vs. non-anomalous samples…
Beam normally delivered well,
→ Assume anomaly rate << normal rate
→ Clean dataset of “obvious” anomalies
Max difference programmed vs. measured voltage
N.B.: x-axis labels refer to different settings of the accelerator.
Total data:
From 3 weeks of PS Complex run (Sep. 2024)
→ ~260k PS cycles (after filtering of non-active and test cycles, missing historical settings…)
~13k suspected anomalous samples reserved for testing (filtered using max diff. prog. vs meas.)
Train/val. split 80/20 chronologically (all val. data acquired after training data)

## Slide 10: Training/Test results
Both training and validation sets have low anomaly scores! 😃
Most suspected anomalies reconstruct poorly 😃
Clear distinction between most known anomalies and training!
Demonstrate and test in operation
With threshold, can separate data into normal/anomalous.
Cluster data as anomaly/normal based on anomaly score (here max., but could also use mean, etc.).

## Slide 11: Demonstrated in operation - Real time anomaly detection
Deployed live monitoring through web-based interfaces*
  Shared with experts: very positive feedback!
  Data logged → track statistical trends → forecasting?
Trained on data from Sep. 2024
→Deployed on real-time data July 2025
Models remain valid: reconstruct “normal” events well
→ Already exploited in operation
Caught real anomalies
  Oscillation damping failure
  Early gap closure
→Corrected by expert!
Normal
Anomalous
See example in backup slides*

## Slide 12: After 10 MHz pilot: what’s next?
Reconstruction-based A.D. successfully deployed for 10 MHz cavity voltages
  First version of a “recipe” for anomaly detection on PS RF signals
  → can it be applied to more RF subsystems?
Apply to global beam loop signals!
Notes: Simplify: Good results on 10 MHz, → expand to more subsystems of RF system

## Slide 13: Applying the recipe: Global beam loops (LLRF)
Many signals with potential for analysis
  Inputs for global beam loops such as the phase loop, radial loop, extraction resynchronization, frev
For this presentation focus on phase loop signal!
  More challenging than voltages: less clear/no setting, normal and anomalous signals can be difficult to distinguish
Notes: Before: single RF approach: move to include global beam control loops in anomaly detection scheme

## Slide 14: Constructing the phase loop dataset
Same approach as for rf voltages:
Collect unsupervised dataset:
Phase program (closest to setting)
Notes: Single plot, same approach as RF voltages. Apply “blindly” to pdisc

## Slide 15: Constructing the phase loop dataset
Same approach as for rf voltages
Collect unsupervised dataset:
Phase program (closest to setting)
Data cleaning less straightforward…
Signal and setting differ significantly: max difference checks not enough…
Measured phase
Model input: Measured signal and matched (inverted and scaled) phase program
Notes: Single plot, same approach as RF voltages. Apply “blindly” to pdisc

## Slide 16: Constructing the phase loop dataset
Same approach as for rf voltages:
Collect unsupervised dataset:
Phase program (closest to setting)
Check for discontinuities at injection, transition, excessive noise after open loop handover → avoiding anomalies in training set.
Only train on data of interest: ~from injection to extraction
More complex workflow →initial focus limited to single beam type: Multi-Turn Extraction (MTE) + smaller dataset (~6k)
Data cleaning less straightforward…
Signal and setting differ significantly: max difference checks not enough…
Specialized checks required (with specific beam information, timings, etc.)
Measured phase
Model input: Measured signal and matched (inverted and scaled) phase program
Injection
Transition crossing
Open loop handover
Extraction
Notes: Single plot, same approach as RF voltages. Apply “blindly” to pdisc

## Slide 17: Autoencoder approach: Phase loop test results
Re-used model architecture from cavity voltages*
Reconstructs normal samples well, (some) anomalies poorly!
1d-convolutional neural network, see backup slides*
Struggles to differentiate certain anomalies
Overlap between normal samples, and injection phase offset samples…
Could complementary methods allow differentiating these anomalies?
threshold
With thresholding can detect “easier” anomalies, e.g., “no beam”.
Still useful to track large changes!

## Slide 18: Complementing the autoencoder: Statistical models
Idea: Can a purely statistical model distinguish between the known classes?
Within valid regions (e.g., beam injection/extraction):
Model timesteps of signal as Gaussian: Calculating the 𝜇 and 𝜎 from the training set → Statistical expectation for value of signal at each timestep
Calculate Z-score* of test-points as anomaly indicator:
distance from mean in 𝜎*
Phase loop measurement model for MTE beam

## Slide 19: Statistical model: results for MTE
Model differentiates normal from known anomalies!
Anomalous point (A.P.) here ±4𝜎 from mean, cycle is anomalous if >5% A.P. Perfect distinction of known anomalies*,
Offset!
→ Including injection phase:
Data split | Normal | No beam | injection phase
Nbr. datapoints | 284 | 1843 | 1216
Nbr. Anomalies | 0 | 1843 | 1216
Accuracy | 100% | 100% | 100%
*with limited dataset and anomaly checks

## Slide 20: Summary
  Anomaly detection auto-encoders demonstrated and working for PS RF 10 MHz cavities at CERN.
    Live web-based monitoring available and shared with equipment experts.
    Further exploration planned towards preventative maintenance strategies,
→ can broken hardware be spotted in degraded performance before failure?
  Naive extension to more RF subsystems effective for “obvious” anomalies.
    More subtle anomaly types remain challenging…
→ Statistical methods provide complementary approach.
  Data collection and cleaning crucial for success
    If clear settings/references are available → relatively simple!
    For other cases (such as beam loops): requires focused effort and beam knowledge.
Future work: Deploy anomaly detection models for as many RF signals as possible.
→ Correlate anomalies with: eachother, faults/hardware repairs, and beam degradations,
→ Working towards true end goal: automatically identify root-causes!
Notes: Try to relate to generic conclusions, connect with
Focus on quick conclusions: Working solution for 10 MHz cavity voltage: Effective anomaly detection for multiple voltage programs and beam types with single model
Naive extension to subsystems effective for large anomalies → Further refinement needed for specific types, statistical methods provide complementary approach
Generally, most cumbersome part of workflow is data collection and cleaning: If both settings and measurement are easily available → good performance is likely!
Towards the future: Streamline data collection, training, and deployment workflow → Deploy anomaly detectors for as many RF signals as possible
Exploit data for end-goal: correlating co-anomalies, and classifying root-causes.

## Slide 21
Thank you for listening! Questions?

## Slide 22: Reconstruction based AD: Auto Encoders → Architecture
Conv1D
ReLU
Conv1D (stride = 2)
ReLU
Conv1D
ReLU
n x 32
32 x 16
16 x 8
Conv1D
ReLU
ConvTranspose1D (stride = 2)
ReLU
Conv1D
ReLU
8 x 16
16 x 32
32 x n
Feature extraction
Downsampling
Feature extraction
Feature processing
Upsampling
Reconstruction
Fully convolutional (1D conv.)
  Handles varying cycle length natively
  Correlates time-aligned signals easily
Modifiable to only reconstruct partial inputs X
More sophisticated options to be explored:
  e.g., VAE, CVAE, Transformer based.

## Slide 23: Live monitoring panel: Main overview
Selectable beam user (selector)
Cavity specific panel links/status
Live signal monitoring panel link (see anomaly score, cavity voltage, LLRF)
Anomaly threshold per cavity
Max anomaly score per cavity

## Slide 24: Example of filtered sample (MTE beam)
Offset at injection
Noisy signal after beam control handover

## Slide 25: Statistical models for other beam types
Statistical models are bespoke for each beam type, however…
  With data-cleaning workflows, can be (semi)-automatically generated:
→ Demonstrated by creating models for more beam types, e.g.: Time-of-Flight (TOF) experiment, and Antiproton-Decelerator (AD)
Statistical model: TOF
Statistical model: AD

## Slide 26: Extra plots: SFTPRO1 (MTE) anomalous samples
No beam
Injection phase

## Slide 27: Extra plots: EAST1, normal and anomalous sample
Normal
Transition spread

## Slide 28: Example of settings correction: C10-51 on SFTPRO1
C10-51 was consistently anomalous on monitoring
2. Most events came from SFTPRO1/LHCPILOT/LHCIND1 (checked through NXCALS, could be done on monitoring)
3. Check of anomaly score and signals
Early voltage drop
→ Gap relay closing early
→ HLRF expert informed and fix issue

## Slide 29: Current WRAP (live monitoring) panels
Monitoring cavity anomalies (accessible only through CERN tunnel)
Main overview panel: https://wrap.cern.ch/app/196304
  Shows all users and all cavities by default
Per cavity/selector overview: https://wrap.cern.ch/app/196944
  Shows all operational USERS for a certain cavity. Can specify cavity by clicking on the device
  MD USERS version: https://wrap.cern.ch/app/197536
Per cavity/USER live RF signals dashboard: https://wrap.cern.ch/app/197085
  Shows live RF signals for a certain USER/Cavity. Both USER and cavity can be configured in the panel by clicking and choosing, or changing in the link.

## Slide 30: Training/Test results for 10MHz: Overlap at low a.s.
Fast voltage change not reconstructed well: suspected model limitation or lack of representation in training set…
Test set examples with max anomaly score >0.005:
Generally real, minor anomalies
→ Should remain anomalies
Initial anomaly threshold set to 0.005, but adjustable per cycle if needed.
→ Re-evaluate on more data
EAST_15GeV_24
Train set examples with max anomaly score >0.005:
98+% from single LSA cycle: EAST_15GeV_24
→ Outlier, to be investigated further

## Slide 31: Training/Test results: Rediscovers anomalies
Detected anomalies: 10 MHz RF cavities
Several interesting cases re-discovered by autoencoder:
From Test set
From Training set
→ Should be excluded in future trainings
From Test set

## Slide 32: Extra: Max anomaly score histograms for train/test/val
Validation set
Good reconstruction
Majority of poor recon. come frome single cycle: EAST_15GeV_24
Training set
Suspected anomalies (test)