## Slide 2: Piezo compensation algorithm for SC cavities at ESS
LLRF25 workshop
PRESENTED BY ANDERS SVENSON

## Slide 3: Outline
ESS overview – Linac
Motivation – ESS case
ESS cold cavities – Spoke and elliptical (MB/HB) cavities
Power overhead
Piezo compensation system – Hardware overview
Algorithms overview
  Offline char
  Online
Results
Summary and future work

## Slide 4: ESS overview
Timeline:
  DTL4 Beam: April, 2023
  Beam on Dump (BOD), 870 MeV: May, 2025
  Beam on Target (BOT), 870 MeV: March, 2026

## Slide 5: Motivation
ESS case
  High gradient
  Pulsed cavities (ESS pulse length 3ms)
  Super-fluid helium
  Lorentz force detuning (LFD) is the dominant source of cavity detuning.
Without compensation cavities can dynamically detune by several bandwidths.
Maintaining the accelerating gradient under these conditions would require considerable excess RF power.
Beam
LFD
RFDS + LLRF
FB loop overpower 1 BW = 2x power

## Slide 6: Cavities and excess power
Cavity parameters:
Without LFD compensation
Chart: Power increase - nominal QL
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600
Spoke | 0 | 0.0032245 | 0.012898 | 0.02902 | 0.051591 | 0.080611 | 0.11608 | 0.158 | 0.20637 | 0.26118 | 0.32245 | 0.39016 | 0.46432
MB | 0 | 0.011336 | 0.045344 | 0.10202 | 0.18138 | 0.2834 | 0.4081 | 0.55546 | 0.7255 | 0.91821 | 1.1336 | 1.3717 | 1.6324
HB | 0 | 0.0087786 | 0.035114 | 0.079007 | 0.14046 | 0.21946 | 0.31603 | 0.43015 | 0.56183 | 0.71107 | 0.87786 | 1.0622 | 1.2641
Cavity | Nominal Eacc [MV/m] | QL [x10^5] | KLFD [Hz/(MV/m)2] | Detuning [Hz] | F1/2 [Hz]
Spoke | 9.0 | 2.0 (1.5 to 2.3) | -4.4 to -5.1 | -356 to -413 | 880
Medium Beta | 16.7 | 7.5 (6.0 to 8.5) | -2.0 | -569 | 470
High Beta | 19.9 | 6.6 (5.8 to 7.3) | -1 | -396 | 530

## Slide 7: Cold Tuner System
Driver specification and Hardware
  2 channel piezo driver for single cavity
  Same HW for all SC cavities
  External power supply to cover 0 to 180V output range
Spoke
Elliptical
Parameter | Value | Comments
Form factor | MTCA.4 | Not fully compliant to MTCA.4 as RTM takes 2 slots
Number of channels | 2 bipolar | Actuator/sensor mode
Piezo capacitance | 1 uF to 5 uF | At cryo temperature
Repetition rate | ≤14 Hz | Pulse duration max 3.5 ms
Power supply voltage | ±100 V | External supply
Max dissipated power | 30 W per channel | 
Amplifier 3dB bandwidth | DC – 1 kHz | 
Actuator voltage range | Elliptical: 0 to +180 V Spoke: -47 to + 180 V | 1 MSa/s, 16-bits
Sensor mode | 1 MSa/s, 16-bits | Input impedance: 10 kΩ
Protection | Current, Voltage, Thermal | DAC level limits in EEPROM
Developed by DMCS:

## Slide 8: Cavity dynamics and detuning
Overview
Dynamics of cavity voltage:
  Lorentz force detuning, mode k:
Time varying total detuning:
Compensation:
Algorithm with transfer function H:

## Slide 9: Piezo algorithm
Offline characterisation
Done once of a cavity to determine w1/2 , C1 and L
Cables and equipment change amplitude and phase
Applying standard least square:
Iterative Learning Control (ILC):
L transfer function for channel A:

## Slide 10: Characterisation 1(2)
Offline part
  Applying Piezo pulses at low gradient
  RF pulse width is limited to ~3.2 ms and by applying the actuator pulse in advance, observation time can be increased.
  The resulting detuning is combined
  Low pass filtering applied to remove high frequency content.
Pulse 1
Pulse 2
Detuning
Detuning – filtered
Detuning 2
Detuning 2 filtered

## Slide 11: Characterisation 2(2)
Offline part
  Inverse transfer function
    where σ ensures small uncertainties in H give large incorrections in gains of L
  In time domain:
  The non-causal L(t) needs to be time shifted

## Slide 12: Online part
For every pulse a new detuning needs to be calculated
To reduce noise dV/dt is calculated with linear regression over a sliding window.
Vreg is used to reduce noise sensitivity at low gradients
The algorithm acts on the difference of intended and estimated detunig, e(t)
Q(q) implemented as zero phase low pass filter
The online part runs at 50 kSa/s as detuning changes slowly

## Slide 13: Chirp
Alternative characterisation method
An alternative to impulse response
Chirp from 25 Hz to 600 Hz
In pulses of 2.5 ms
Gives a different shape of L
Not yet fully tested in online part

## Slide 14: Mechanical modes
  With long Piezo sensor acquisition time mechanical modes was observed
4 MV/m and 12 MV/m
4 MV/m
12 MV/m

## Slide 15: Results
”Normal” cavity
HB cavity at 20MV/m
Cavity tuning sensitivity: 2-3 Hz/V
Setpoint: 100 Hz
Piezo voltages:
L functions:

## Slide 16: Results
”Stiff” cavity
HB cavity at 20 MV/m
Cavity tuning sensitivity only 0.23 Hz/V
Setpoint: 20 Hz
Piezo voltage:
L functions:

## Slide 17: Performance with and without Piezo
Piezo OFF
Cavity detuning at high field (LFD) requires > 50% extra power at pulse end!
FB loop overpower 1 BW = 2x power
Piezo ON
Flat pulse with FB

## Slide 18: Summary and outlook
Only few cavity tested so far but results looks promising.
More testing needed to optimise performance
Further Improvements:
  Detuning calculation is quite computational heavy and noisy
    Reduce sample rate and add filtering
  Allow longer observation time for transfer function
    Trigger limitation
  Evaluate characterisation with chirp method

## Slide 19: Contributors
Contributors at Lund University:
          Bo Bernhardsson, Prof. Department of automatic control
          Anders J. Johansson, Associate Professor at EIT
  Contributors and DMCS in Lodz:
          Wojciech Cichalewski, PhD and team lead
  Contributors at ESS:
          Mateusz Nabywaniec, IOC implementation
          Cecilia Maiano, Teststand coordination
          And many more

## Slide 20: Thank you!