## Slide 1: Reverse phase operation for CERN's FCC-ee 400 MHz RF system: Increasing flexibility brings challenges for cavity control
Ivan Karpov and Franck Peauger for FCC SRF WP1 with input from:
Xavier Buffat, Yann Dutheil, Giorgia Favia, Jiquan Guo (JLAB), Mauro Migliorati (INFN), Katsunobu Oide, Luca Sabato, Roxana Soos, Jorg Wenninger, Frank Zimmermann, Mikhail Zobov (INFN)
LLRF 2025, 13.11.2025

## Slide 2: Future Circular e+e- collider (FCC-ee)
Courtesy A. Navascues Cornago
An e+e- collider as the 1st stage of the integrated FCC program
New 90.7 km tunnel to be later reused for a hadron collider
Double-ring collider (separate beam pipes for electrons and positrons)
Collider runs at constant energy
Regular top-up injection from a full-energy booster synchrotron, located in the same tunnel
SC RF systems in two straight sections

## Slide 3: Challenging requirements for FCC-ee RF system
Beam current and energy loss for 50 MW synchrotron radiation (SR) budget
Low energy operating points:
High beam current and weak SR
Low RF voltage
Beam instabilities
Significant power losses due to high-order modes (HOM)
High energy points:
Low beam current and strong SR
High RF voltage to be reached with a small footprint
Instabilities suppressed by SR
Small power losses due to low beam current
A few one- or two-cell cavities at low RF frequency (400 MHz)
Many multi-cell cavities at higher RF frequency (800 MHz)
RF system choice is driven by minimization of hardware modification between operating points

## Slide 4: Collider RF system layout
400 MHz 2-cell cryomodule (CM) (FCCACSGA0002)
800 MHz 6-cell CM (FCCACSGA0003)
F. Cottenot, M. Timmins, and V. Parma
33 400 MHz CMs
33 400 MHz CMs
33 400 MHz CMs
33 400 MHz CMs
33 400 MHz CMs
33 400 MHz CMs
102 800 MHz CMs
Common RF for 2 beams
&
Beam 1
Beam 2

## Slide 5: Reverse phase operation
Reverse phase operation (RPO) mode:
Proposed to increasing RF cavity voltage (Y. Morita et al., SRF, 2009)
Experimentally verified with high beam loading in KEKB (Y. Morita et al., IPAC, 2010)
Baseline solution for EIC ESR (e.g., J. Guo et al., IPAC, 2022)
 | Total voltage (GV) | Cavity voltage (MV) | Quality factor
Z | 0.088 | 0.67 | 
WW | 1.05 | 7.95 | 
 | Total voltage (GV) | Cavity voltage (MV) | Quality factor
Z | 0.088 | 0.67 | 
WW | 1.05 | 7.95 | 
Optimal quality factor, , and detuning minimize RF power
Enormous change is required switching from Z to WW
A sketch of RPO mode for 12 RF cavities
With RPO at Z, can be kept constant for Z, WW, and ZH operating points (no hardware changes)
Flexibility of the running sequence

## Slide 6: Reverse phase operation
A sketch of RPO mode for 12 RF cavities
Focusing cavities
Defocusing cavities
Reverse phase operation (RPO) mode:
Proposed to increasing RF cavity voltage (Y. Morita et al., SRF, 2009)
Experimentally verified with high beam loading in KEKB (Y. Morita et al., IPAC, 2010)
Baseline solution for EIC ESR (e.g., J. Guo et al., IPAC, 2022)
 | Total voltage (GV) | Cavity voltage (MV) | Quality factor
Z | 0.088 | 0.67 | 
WW | 1.05 | 7.95 | 
 | Total voltage (GV) | Cavity voltage (MV) | Quality factor
Z | 0.088 | 0.67 | 
WW | 1.05 | 7.95 | 
Optimal quality factor, , and detuning minimize RF power
Enormous change is required switching from Z to WW
With RPO at Z, can be kept constant for Z, WW, and ZH operating points (no hardware changes)
Flexibility of the running sequence

## Slide 7: Static beam loading compensation with RPO
To minimize RF power requirements optimal quality factor and optimal detuning must be used
Total RF voltage can be changed in discrete steps of (e.g., A. Blednykh et al, 2022)
Opposite detuning for two groups:
,
Risk of longitudinal coupled-bunch instabilities (LCBI) in certain scenarios
Strong transient beam loading due to gaps in the filling schemes
Cavity impedance at fundamental,

## Slide 8: Transient beam loading with RPO
Gaps in beam filling scheme will result in modulation RF parameters
Original filling scheme with proposed 88 MV RF voltage results in ~50 % modulation of the effective RF voltage
Voltage amplitude and phase transients from small-signal model (F. Pedersen, 1992)
 |  | (MV) | (MV) | 
71 | 61 | 89 | 7.95 | 9.21e5
71 | 61 | 89 | 7.95 | 9.21e5

## Slide 9: Bunch-by-bunch spread of beam parameters
Large synchrotron tune and bunch length spread can significantly degrade beam stability (e.g., due to X-Z instability, K. Ohmi, 2016)
Peak-to-peak variation -21/+10 %
Peak-to-peak variation -9/+27 %

## Slide 10: Possible mitigations
where peak-to-peak beam phase spread
Synchrotron tune spread according small-signal model
Higher RF voltage and shorter gaps reduce spread
Evaluation of option with = 200 MV and original showed unacceptable reduction of lifetime to about 20 s compared to 1320 s given by radiative Bhabha scattering (K. Oide, 09.10.2024)
A new filling scheme with shorter gaps is necessary for reduction of the spread
5%
spread for 1.2 µs gap length
Relative contributions to spread
30%

## Slide 11: Results for smaller gaps between trains
With a new filling scheme (40 trains of 280 bunches), RF voltage spread was significantly reduced
Working point can be found for all bunches at nominal intensity, but not during non-uniform bootstrap injection needed for e-cloud mitigation (X. Buffat et al, 24.04.2025, also R. Soos et al, FCC week, 2025)
Injection and extraction systems were adapted to decrease the rise time below 600-ns (G. Favia, FCC week, 2025)
FCC Feasibility study final report, 2025

## Slide 12: Possible scenarios of coupled bunch instabilities
Standard mode – all RF lines (cavities, LLRF, HLRF) are ON
Degraded mode – trip of one or more RF lines
Reaching integrated luminosity goals requires at least 3-4% redundancy of the RF system (preserve beam with up to 5 RF lines down)
For ZH and a 10% redundancy is assumed based on LEP experience
Integrated luminosity vs RF system redundancy scaled from LHC data
J. Heron, FCC Week, 2024

## Slide 13: Mitigation measures
RF feedback suppresses instability due to fundamental cavity impedance
Longitudinal damper can mitigate instability of low-order coupled bunch modes (max growth rate < 0.5 , e.g., D. Teytelman, FCC week, 2019)
RF cavity
Load
Circulator
Generator
–
+
Cavity voltage
Forward wave
Reflected wave
Error signal
Delay
RF feedback
Phase pickup
Longitudinal damper
Reference signal
Beam
Tuner
+
+
Simplified block diagram of FCC RF system similar to LHC (P. Baudrenghien et al, 2006)

## Slide 14: Analytical results for dipole mode
Growth rate of mode (J. L. Laclare, 1985)
Instability growth rates
Long. damper rate
SR damping rate
Total effective impedance with direct RF feedback (DFB)
loop delay = ns, digital gain = 10
LCBI can be suppressed with DFB in standard mode
Longitudinal damper should be sufficient to damp instability in degraded mode with one RF line being down

## Slide 15: Dynamic beam-cavity interaction model
Coupled differential equations (e.g., J. Tückmantel, 2011) are solved for four groups:
Focusing ( cavities)
Defocusing ( cavities)
Tripped focusing ( cavities)
Tripped defocusing ( cavities)
Combined with longitudinal equations of motion for one particle per bunch
Longitudinal damper IIR filter similar to one implemented in the CERN SPS (P. Baudrenghien, EDMS, 2023 inspired by D. Teytelman, PhD thesis, 2003)
Synchrotron frequency spread
RF power transients (1/10 of ring)

## Slide 16: Trip of focusing cavity: first 100 turns
Short RF voltage transients ~6%
Fast adjustment of reference voltage is required to limit the initial bunch oscillation amplitude <10% of rms bunch length
~ 48 ps
Trip
Reaction time
Controlled voltage increase

## Slide 17: Trip of focusing cavity: longer tracking
Short RF voltage transients ~6%
Fast adjustment of reference voltage is required to limit the initial bunch oscillation amplitude <10% of rms bunch length
Without longitudinal damper beam becomes unstable
~ 48 ps

## Slide 18: Trip of focusing cavity: longitudinal damper ON
Longitudinal damper preserves beam stability
Ramping up the gain 0.1 0.5 within ~250 turns is required to keep RF power transients below ~500 kW
RF line recovery scenario needs to be analyzed
~ 48 ps

## Slide 19: Summary
The FCC-ee baseline RF system allows switching between for Z, WW, and ZH operating points without hardware modifications.
This requires Reverse Phase Operation (RPO) at Z operating point and common RF system for two beams at ZH operating point
Flexibility of operation sequence poses additional challenges:
Strong transient beam loading leads to significant modulation of RF and beam parameters.
Required 4% redundancy to achieve integrated luminosity goals cannot be demonstrated with dynamic beam-cavity interaction model. RF power margins could be sufficient to preserve the beam only in the case of a single RF line trip.
Thank you for your attention!

## Slide 20: Backup slides

## Slide 21: Trip of focusing and defocusing cavities
Short RF voltage transients ~6%
Peak power of other cavities is modulated at synchrotron frequency (avg. <45%, peak <80%)
Initial bunch oscillation amplitude is <8% of rms bunch length
Not enough power margin to handle simultaneous trip of two cavities
~ 48 ps
Trip
Reaction time
Controlled voltage increase

## Slide 22: Example for Z mode
Longitudinal damper OFF
Longitudinal damper ON, gain ramp 0.1-> 0.5 (within ~250 turns)

## Slide 23: Example for Z mode
Longitudinal damper OFF
Longitudinal damper ON, gain ramp 0.1-> 0.5 (within ~250 turns)

## Slide 24: Higher total RF voltage
Moving from 89 to 195 MV reduces RF power transient:
Is there a room for this in LCC optics?
Can we profit from relaxed bunch charge for non-uniform filling schemes?
~ 48 ps
Trip
Reaction time
Controlled voltage increase

## Slide 25: Instability growth rates
Calculations for loop delay of ns, DFB gain 10, OTFB gain 20:
LCBI can be suppressed already with DFB, while OTFB gives additional stability margin
SR limit
132 2-cell cavities with RPO

## Slide 26: HOM-driven coupled-bunch instabilities
Longitudinal plane:
No trapped HOMs
impedance is well below the SR threshold
Updated 2-cell design with suppressed of 0-mode at MHz by 2 orders of magnitude (S. Gorgi Zadeh, 15.08.2024)
Only twice below SR damping limit for (might be larger due to limited bandwidth of circulator)
We gain a factor of 20 with 10 kHz frequency spread from cavity to cavity
Transverse plane:
Instabilities growth rates (min. rise time > 100 turns) are within capabilities of transverse feedback system (W. Hofle, 2024)
SR damping
SR damping

## Slide 27: Simplified beam-cavity interaction model
Coupled differential equations are solved for four groups:
Focusing ( cavities)
Defocusing ( cavities)
Tripped focusing ( cavities)
Tripped defocusing ( cavities)
Combined with longitudinal equations of motion for one particle per bunch
Longitudinal damper is not implemented yet
RF cavity
Load
Circulator
Generator
–
+
Cavity voltage
Forward wave
Reflected wave
Error signal
Delay
Direct RF feedback
Phase pickup
Longitudinal damper
Reference signal
Beam
Tuner
+
+

## Slide 28: Alternative filling schemes
Hybrid filling schemes with 5-ns spacing micro-trains can suppress e-cloud limitations (L. Sabato, presentation yesterday)
Negligible impact on the RF voltage spread (15.3 % 16.8 %)

## Slide 29: RF baseline evolution for collider
FCC Conceptual design report (2018)
Z
WW
ZH
Common RF for 2 beams
F. Peauger, FCC Week 2022 & FCC FS MTR (2024)
FCC FS Final Report (2025)
+
×104
×104
×272
×272
×372
Operational margins
Less HOM power for WW with 2-cell cavities
Same RF for WW & ZH
+
Common RF for 2 beams
×112
×264
×264
×264
×488
×264
×264
×264
×264
×408
+
Common RF for 2 beams
Same RF for Z, WW & ZH
One power source per cavity
6-cell for for cost reduction
Reverse Phase Operation (RPO) mode for Z is required to unify Z-WW-ZH RF system

## Slide 30: Trip of focusing cavity
Short RF voltage transients ~6%
Peak power of other cavities is modulated at synchrotron frequency (avg. <15%, peak <32%)
Initial bunch oscillation amplitude is <10% of rms bunch length
Beam is unstable without longitudinal damper due to uncompensated impedance
~ 48 ps

## Slide 31: Trip of defocusing cavity
Similar results to the case of focusing cavity trip
Simultaneous trip of two cavities of any type leads to significant RF power overshoot
~ 48 ps

## Slide 32: Trip of 3 single-cell cavities (4% redundancy)
Smaller relative transient compared RPO scheme
Absolute peak power modulation exceeds 1 MW level
~ 48 ps

## Slide 33: Reverse phase operation
Reverse phase operation (RPO) mode allows for increasing RF cavity voltage having optimal static beam loading compensation (Y. Morita et al., SRF, 2009)
Experimentally verified with high beam loading in KEKB (Y. Morita et al., IPAC, 2010)
Baseline solution for EIC ESR (e.g., J. Guo et al., IPAC, 2022)
Phasors
RF waves
*Electron convention for synchronous phase:

## Slide 34: RF baseline evolution
FCC Conceptual design report (2018)
Z
WW
ZH
Separate RF systems
Common RF system
Separate RF systems
Common RF system
F. Peauger, FCC Week 2022 &
FCC FS Mid-Term Report (2024)
FCC FS Final Report (2025)
Separate RF systems
Common RF system

## Slide 35: SPS Longitudinal damper model
RF seminar of I. Stachon

## Slide 36: SPS Longitudinal damper model
RF seminar of I. Stachon
Details are in the EDMS document prepared by P. Baudrenghien

## Slide 37: Higher-order mode power
Unavoidable 15 kW increase in HOM power compared to single-cell design for option 1 and potentially up to 10 kW deposited in resonance mode (S. Gorgi Zadeh, 23.01.2024)
Verification of possible reduction of the tapering angle at the extremities of the cavity string is ongoing (K. Canderan, 29.10.2024)
K. Oide, 06.11.2024
2 coaxial HOM couplers
Option 2:
2.3 kW
4.2 kW
6.8 kW
4.3 kW
5.9 kW
5.1 kW
6.5 kW
5.5 kW
6.1 kW
4.8 kW
6.4 kW
6.4 kW
Option 1:
1.9 kW
3.7 kW
6.1 kW
3.7 kW
5.3 kW
4.5 kW
5.8 kW
4.9 kW
5.5 kW
4.2 kW
5.7 kW
5.3 kW
Option | (MV) | (mm)
1 | 103.00 | 14.6
2 | 117.86 | 13.7
Option |  | 
1 | 103.00 | 14.6
2 | 117.86 | 13.7
Tapers contribution to the HOM power
HOM power equation
In absence of resonant modes

## Slide 38: Baseline collider RF system configuration
Proposed solution:
Installation of 2-cell cavities with individual RF power sources (~0.5 MW level) from the beginning
Reverse phase operation (RPO) mode for Z, normal mode for W and H (combined RF system for 2 beams)
Applicability of RPO for FCC-ee needs to be confirmed
Courtesy of O. Brunner
Extra year of operation?
66
MTR recommendation:
Study options to avoid the 1-cell/2-cell RF cavity reconfiguration between Z and H/WW running to simplify the SRF system implementation and improve flexibility in the physics programme.

## Slide 39: Beam loading model: main equation
Generator current
Generator power
Fixed parameters are , , , , , while , , and can be adjusted
See, e.g., J. Tückmantel, CERN Report No. CERN-ATS-Note-2011- 002 TECH, 2011

## Slide 40: Derivations for arbitrary cavity phase (1/2)
Complex quantities: , , and
Generator current
, ,
Then splitting in real and imaginary parts:
0

## Slide 41: Derivations for arbitrary cavity phase (2/2)
= 0 for
Minimized for
Setting recovers classical equations for optimal parameters
Adjusting , can be modified to meet certain constraints
The minimum power

## Slide 42: RF power requirements
Starting with energy gain per turn
No RF power overshoot is needed for RPO if optimal detuning and optimal quality factor are used
Constraints:
- The same for all cavities to avoid a movable fundamental power coupler design
- The same to have the identical power sources and uniform power distribution (role of variations is under study)
Cavity voltage must be the same for all cavities: =

## Slide 43: Reverse phasing mode equations
Preservation of energy gain
Preservation of synchrotron tune
See, also A. Blednykh et al, EIC-ADD-TN-33, 2022
The aim is to keep , , and for Z, W, and ZH modes
Cavity voltage can be change in discrete steps of
Cavity voltage
Optimal detuning
Phases

## Slide 44: Critical impact of spread
A coherent beam-beam instability, X-Z instability (K. Ohmi, 2016)
Threshold
Working point chosen between resonances and
Higher
  stronger low order resonance but more space available between them
Bunches are ~50% shorter (assuming the same )
  stronger beamstrahlung ( increase is smaller)
  stronger impact of longitudinal impedance?
M. Migliorati, 2024

## Slide 45: Parameter sensitivity of RPO
Small, but visible impact of parameter spread on global parameters (e.g., )

## Slide 46: Steady-state beam loading
Increasing (43.890.6 Ohm) and reducing :
Large range for adjustment (a factor of ~75-600) starting from : possible FPC solutions under study (S. Gorgi Zadeh and E. Montesinos, CERN SRF, 2024; see also slides of F. Gerigk, FCC week 2024)
Incresed detuning enhances instability due to fundamental mode
Can the total voltage be increased for Z mode?
RF power for SRF cavities with circulators is minimized for optimal parameters:
Optimal detuning
Optimal quality factor
Optimal parameters for different scenarios

## Slide 47: New adjustable power coupler concept
Z
W
t
This length can be increased by λ/2 (374 mm) and get similar results
,
,
4,
,
,
,
,
,
  Two windows (LINAC4-like) are placed outside the cryomodule  integration challenge after cryostating
  A more robust and easier-to-cool down window design  easier to cover all four working points
  Providing ~1 MW in CW operation with variable coupling for Z, W, H, ttbar.
  HOM power see: F. Peauger & I. Karpov
  Prototyping starting.
normalized to 1J stored energy
W
Z