## Slide 1: A Universal Cavity Controller for testing SRF cavities at CERN
D. Barrientos, L. Balocchi, K. Brunner, K. Geis, A. Macpherson, L. Millar, N. Stapley, T. Wlostowski
14/10/2025

## Slide 2: Motivation
Development and validation of SRF Cavities
  Purpose: Measurement of high quality factor SRF cavities (Q0 in 108 - 1011 range)
    CERN has a variety of cavities with frequencies ranging from 101 -1300 MHz
    LLRF framework must be adaptable to any given cavity type and specific R&D needs
Cavity validation
LLRF example system
Cryomodule validation
Images courtesy of HL-LHC WP4 – Crab Cavities

## Slide 3: Motivation
Development and validation of SRF Cavities
  Context: LLRF must follow cavity testing as they progress through their preparation cycle
    RF measurement from bare cavities to beam-ready cryomodules
Cavity validation
LLRF example system
Cryomodule validation
Images courtesy of HL-LHC WP4 – Crab Cavities

## Slide 4: Motivation
Development and validation of SRF Cavities
  Requirement: Common architecture to ensure coherence across measurement campaigns
    Measurements include both pulsed and continuous powering operational modes
    Self-Excited Loop and Generator Driven modes required
Cavity validation
LLRF example system
Cryomodule validation
Images courtesy of HL-LHC WP4 – Crab Cavities

## Slide 5: System architecture

## Slide 6: System architecture
LLRF cavity controller standardization

## Slide 7: Hardware
16-bit IQ DAC +
Vector modulator
(BW = 25 MHz)
4 input channels
14-bit ADCs
(BW = 25 MHz)
LO distribution
(200 MHz – 1.5 GHz)
Artix-7 FPGA
16 MB SSRAM
2x SFPs
(up to 2.5 Gbps)
PCI Express
VME A24/D16
Clock,
triggers…

## Slide 8: Software
CERN standard setup
Reusing control applications layer
Easy integration into CERN controls system
Encapsulation of hardware related operations in low-level library
Code generation for driver and FPGA registers layers

## Slide 9: Reksio (& cheby)
Create memory map with a graphical tool. Verify correctness
Use code generators for HDL and C++ driver wrapper, FESA class skeleton
Quick development/testing using Python
Open-source tools
T. Gingold, B. Bielawski - FPGA Developers’ Forum 2025, CERN

## Slide 10: UCC architecture
Hardware independent architecture
Reusability
Standard blocks and processes

## Slide 11: UCC architecture

## Slide 12: UCC architecture

## Slide 13: UCC architecture

## Slide 14: UCC architecture

## Slide 15: UCC architecture

## Slide 16: Ease development
Example:
  Generate IF data with different attenuation, phase offset, frequency.
  Model demodulation, low-pass-filter, CORDIC
  Check magnitude, phase, frequency

## Slide 17: UCC architecture

## Slide 18: UCC architecture

## Slide 19: UCC architecture
T. Wlostowski et al. – ICALEPCS 2015, Melbourne, Australia

## Slide 20: UCC architecture
Hardware independent architecture
Reusability
Standard blocks and processes
System/user parts
MCU
IP cores + shared libraries
Continuous Integration

## Slide 21: Continuous Integration (CI)
Simulation, implementation, generation
CI4FPGA service at CERN
  Scalable VM-based k8s clusters
  Easy-to-use Docker images
  Comprehensive documentation
C. Gentsos - FPGA Developers’ Forum 2025, CERN

## Slide 22: Cavity tests
Mobile development setup
Tests setup installation
Gradual deployment into all SRF test systems

## Slide 23: Cavity tests
Courtesy of HL_LHC WP4 - Crab Cavities
Recent 400 MHz Crab cavity
performance validation campaign
Courtesy of HL-LHC WP4 – Crab Cavities
RFL
FWD
TRN
Self-Excited Loop: Typical pulse measurement

## Slide 24: Future challenges: Axion detection
Heterodyne approach:
  Drive a high-Q cavity at a frequency, ωpump.
  Axion interacts with cavity field and transfers energy to a second mode at ωsignal.
  Monitor ωsig, the axion mass is given by the frequency difference (Δω= ωpump - ωsignal).
  Mass range can be scanned by varying Δω  tuning system.
Initial tests in Q1 2026
L. Millar et al. – 22nd International Conference on RF Superconductivity (SRF2025), Tokyo, Japan