## Slide 1: Upgrade of the Barrier Bucket LLRF system for High-Intensity, Low-Loss Multi-Turn Extraction at the CERN PS
T. Gavric, B. Woolley, H. Damerau, Y. Brischetto, M. Vadai
15th October 2025

## Slide 2: Overview
Introduction to CERN PS
Introduction and motivation behind MTE
Previous work
Synchronization scheme
New features
Exotic bunch shapes
Future work
10/15/2025

## Slide 3: CERN Proton Synchrotron (CPS or PS)
Oldest operating machine
First multiplexed injector in the complex
Responsible for most RF gymnastics
Accelerates through relativistic transition

## Slide 4: Introduction and motivation behind MTE
Mitigate PS extraction losses during 5 turn extraction of coasting beam
Pulsed RF: barrier-bucket for longitudinal kicker gap
Less losses with
  PS-SPS transfer of fixed-target beam (SFTPRO)
  All high-intensity fast- extracted beams without dummy septum
M. Vadai, Barrier-bucket multi-turn extraction reducing losses at PS-SPS transfer, https://indico.cern.ch/event/1254574/
2023: First full year of operation → major success

## Slide 5: Previous work
Barrier-bucket MTE scheme significantly reduces beam loss in PS extraction region
Non-PPM (non-multiplexed) barrier waveform
  Lacked flexibility
2 consolidation boards
  h16 measurement
  h1 measurement
10/15/2025

## Slide 6: Synchronization scheme
Conventional synchronization not possible
  RF voltage of the wide-band cavity generating the BB would be too low for a conventional synchronization
Synchronization concept in use:
  Synchronizing in h16 using feed-forward cogging with the main 10 MHz RF system
  Lower accuracy than typical closed loop synchronization, but sufficient for barrier buckets
  Synchronization in h1: phase measurement and communicating phase information within the cycle to set the correct barrier position for extraction
10/15/2025
Notes: 590-600 Loops off,ℎ16 phasemeasurement 600 ℎ1 phase measurement 600-620 Cogging 620-650 Radial steering to central orbit 650-770 Constant offset for MTE 770-800 Radial steering to extraction orbit 800-815 Hand-over ℎ16 to barrier bucket 800-815 Debunching 835 Extraction

## Slide 7: H16 synchronization
Synchronization to the nearest bucket
Measure h = 16 phase of bunches in PS with respect to SPS
Frequency bump to correct beam phase → cogging
Part of the new PS beam control firmware
10/15/2025
Notes: 590-600 Loops off,ℎ16 phasemeasurement 600 ℎ1 phase measurement 600-620 Cogging 620-650 Radial steering to central orbit 650-770 Constant offset for MTE 770-800 Radial steering to extraction orbit 800-815 Hand-over ℎ16 to barrier bucket 800-815 Debunching 835 Extraction

## Slide 8: Change in h1 measurement
h=1 controller measures the phase w.r.t. SPS and sends it real-time via C programs on front-ends to the barrier bucket drive
h=1
controller
SPS h=1 RF
PS h=1 RF
Network
BB
drive
φh1 mod h16
To wideband
cavity
New Finemet cavity controller
Non-standardized hardware removed
Enables remote intervention
10/15/2025
Notes: - Hardware only used for synchronization.
- Hand-made electronics, conforms to no rack standard.
- Power and comms: FEC via USB.

## Slide 9: New features (1)
Full control of RF drive voltage
  PPM/Multiplexed
  Arbitrary waveform
  15-bit waveform memory
Acquisition of gap voltage
  Single turn
  Hard trigger (from General machine timing through backplane)
  OR Software trigger
Arbitrary gain function of the waveform
  FGC: Internal function generator – new preferred option
  CVORB – external function generator – separate HW
Chart: 
10/15/2025

## Slide 10: New features (2)
New extraction synchro for PS: h1 measurement w.r.t. SPS derived h1
  Updates BB azimuth during the cycle (C620 ms)
  SPS h1 phase measurement performed on the cavity controller using beam synchronous NCO
Added internal acquisition channels:
  10kHz sample rate during whole cycle
  Voltage output gain function
  h1 phase measurement – between SPS derived h1 and PS h1
Accordion sweep of the waveform
  Time in which sweep happens can be set
    Used for smooth batch compression – interesting for possible ion chain upgrade
10/15/2025

## Slide 11: Exotic bunch shapes
New Finemet controller → Full control of RF voltage function during a turn
DAC bins
Drive function (1 turn)
Clock samples (h256)
Finemet cavity gap voltage
Future applications of PS wide-band cavity
Transient beam loading compensation

## Slide 12: Future work
Deploy new firmware during commissioning period
Test BB IP as a part of new digital PS beam control
Additional updates to enable further beam manipulations
Deserializer
Sushi
train
(QSFP)
H
armonic
selection
Phase loop
harmonic (F)
Selected H
dPhase
Phase
error
Stable phase (F)
HPF
Cutoff
frequency (R)
PI
controller
Kp, Ki Phase
loop (F)
Noise
window
detection
Phase loop
WR Core
SFP
Btrain
to Frev
Frev
+
GFSTRIM
CORDIC
and
Memap
IQ Memap
Beam and cav phase offset (F)
Sum masking (F)
H
a & Hb
dPhase
WR
Core
Btrain
Receiver
F function
Phase
offsets
and
harmonic
selection
Synchro phase offset,
harmonic (R)
Coarse synchro phase
Fine synchro phase
PI controller
Kp, Ki (F)
PI controller
Kp, Ki (F)
Synchro
loop
correction
Threshold
detection
Synchro
loop
Harmonic
selection
Rpos
Hb
Rpos
Ha
R loop harmonic (F)
PI Controller
Kp, Ki, R steering (F)
Transition
Radial loop
Barrier
Bucket
Selector (T)
SFP
FMC
23
-
bit
parallel
Function
generator
F
function
,
playback
K
phase, radial, synchro
dR
prog
H
phase, radial
?
stable
GFSTRIM
Timing
Barrier Bucket
AVC
inhibit
?
loop
st
art/stop
R loop
st
art/stop
S loop
st
art/stop
Computation
(cordic)
Computation
(cordic)
Rpos
IQ
Hb
Rpos
IQ
Ha
F measured
F sim
F playback
H
1
-
Ref
H84
-
Ref
H9
-
Ref
H8
-
Ref
MemMap
B
polinomial
Cutoff F
HPF
?
offset
synchro
H
synchro
?
transition
Sum masking
Enable
Corrections
Transition
start
Start (T)
Threshold
start
Start (T)
Block diagram of the new PS beam control firmware
Credits to Francisco Javier Diaz Ferreira
10/15/2025

## Slide 13: Acknowledgements
CERN SY-RF-LL
B. Woolley
CERN SY-RF-CS (LLRF Software)
Y. Brischetto
CERN SY-RF-BR (Beams & RF studies)
H. Damerau
10/15/2025

## Slide 14: Questions ?
10/15/2025
T. Gavric | Upgrade of the Barrier Bucket LLRF system for High-Intensity, Low-Loss Multi-Turn Extraction at the CERN PS