## Slide 1: Radio Frequency Astronomy
Matthew A. Morgan

## Slide 2: Outline
The National Radio Astronomy Observatory
Astronomical Interferometry
Components and Instrumentation
Technical Focus: Reflectionless Filters

## Slide 3: The National Radio Astronomy Observatory

## Slide 4: The National Radio Astronomy Observatory
Builds and operates state-of-the-art radio telescope facilities for use by the international scientific community.
Is funded by the National Science Foundation.
Is operated by cooperative agreement with Associated Universities, Inc.

## Slide 5: The Jansky Very Large Array (VLA)
27 antennas
25m diameter
1.0 GHz to 50 GHz
Notes: Number of antennas 28 (27 active and 1 spare)
Dish size 25 meters
Weight 230 tons
Latitude 34°04'43.497" North
Longitude 107°37'03.819" West
Dish Surface Aluminum panels accurate up to .5 mm
BUS Steel
Frequencies From 1.0 GHz to 50 GHz
Resolution 0.2 arcseconds to 0.04 arcseconds
Reconfigurable Array North arm is 11 miles long, two other arms are 13 miles long
A configuration size 22.62 miles across
B configuration size 7.08 miles across
C configuration size 2.11 miles across
D configuration size 0.64 miles across

## Slide 6: The Very Long Baseline Array (VLBA)
10 antennas
25m diameter
300 MHz to 96 GHz
8611 km maximum baseline
Notes: Number of Dishes 10
Dish Sizes 25 meters (82 feet)
Antenna Weight ~ 218 tons
Total Collecting Area 19,635 square meters
Receiver Frequencies 0.3 GHz – 96 GHz (90 cm – 3 mm)
Resolution 0.17 – 22 milliarcseconds
Array Size Maximum baseline of 8,611 km (5,350 mi)

## Slide 7: The Robert C. Byrd Green Bank Telescope (GBT)
1 antenna
100m diameter (2.3 acres)
100 MHz to 116 GHz
Notes: The surface of the GBT is perfectly smooth to a noise level of 260 microns (5 human hairs)
The pointing accuracy of the GBT is 2 arc seconds, able to resolve a quarter at 3 miles
The GBT weighs almost 17 million pounds and stands over 485 feet above ground level
The GBT’s collecting area is 2.34 acres and its diameter is 300 feet

## Slide 8: The Atacama Large Millimeter Array (ALMA)
66 antennas
7m and 12m diameter
35 GHz to 950 GHz
25 μm surface accuracy
16,500 ft. altitude
Notes: Number of antennas 66
Dish sizes Fifty-four 12 meter and twelve 7 meter
Antenna weight ~100 tons
Total collecting area of array 71,000 square feet or 6600 square meters
Number of antenna pads 192
Receiver frequencies From 35 GHz to 950 GHz
Resolution 12.5 arcseconds to 0.009 arcseconds
Reconfigurable array Minimum of 160 m, maximum of 16 km
Partners United States, Chile, Japan, Europe, Taiwan and Canada
Average annual rainfall 2.3in or 58mm
Average daily temperature at site 34°F or 1.1°C
Elevation 16,500 ft or 5000 m

## Slide 9: Radar with the GBT and VLBA
Initial proof-of-concept tests
700W, 13.9 GHz transmitter on GBT
Return signal received by VLBA.
Apollo 15 landing site shown.
~1.25m resolution.
The finest-resolution images ever taken of the moon from the (Earth) ground.
image credit: Raytheon
Notes: A recent article in the Microwave Journal reported on radar experiments done using the GBT and VLBA that successfully produced high resolution images of the Moon, and detected a Near-Earth Asteroid making a close flyby of Earth, more than 5 times farther away than the Moon – using less power than a microwave oven. In these tests, as a proof of concept, the GBT transmitted a 650-watt radar signal at 13.9 GHz that was received by VLBA antennas, producing radar images of the Moon’s surface with unprecedented detail.

## Slide 10: Radar with the GBT and VLBA
Tycho crater shown at 9m resolution.
Planned upgrade: 500 kW
Uses:
  Planetary defense (NEOs)
  Space situational awareness
  Geology and planetary science (asteroids, comets, planets, and moons)
image credit: Raytheon
Notes: Demonstrated compelling radar results using a pilot system with potential for:
  Meter-scale imaging of the Moon from the ground
    Geology and dynamics
  Detecting, tracking, and characterizing space debris in cislunar space
    Safety and security
  Detecting, tracking, and characterizing NEOs for planetary defense
    Impact hazard assessment and mitigation planning
  Studying solid bodies across the Solar System for planetary science
    Physical and dynamical characterization

## Slide 11: Next-Generation Very Large Array (ngVLA)
263 antennas
6m and 18m diameter
1.2 GHz – 116 GHz
8860 km maximum baseline

## Slide 12: The Central Development Laboratory (CDL)
Notes: Approx. 50 engineers, scientists, machinists, and technicians
38,000 sq. ft. lab and office space

## Slide 13: Astronomical Interferometry

## Slide 14: Wavefront Synchronization
Precision timing
  femtoseconds of delay
  Hydrogen masers
  Round-trip phase monitoring corrected by fiber-stretchers or numerical calibration
Mathematical solution determines telescope positions to sub-wavelength accuracy.
θ
θ
D
D sin θ

## Slide 15: Interferometry and Fourier Transforms
cross-correlations...
...and auto-correlation.
Fourier Plane

## Slide 16: Interferometry and Fourier Transforms
Earth rotation
Fourier Transform
Fourier Plane
(Hercules A)

## Slide 17: Resolution and Sensitivity
An interferometric array has the same resolution as a single dish with diameter equal to the maximum baseline.
Sensitivity, on the other hand, is determined by collecting area.

## Slide 18: Geodesy
The very precise determination of telescope positions from interferometric calibration additionally supports geodetic measurements
  Earth Orientation Parameters (EOP)
  Celestial Reference Frame (CRF)
  Terrestrial Reference Frame (TRF)
  Movements of the Earth’s crust
θ
θ
D
D sin θ

## Slide 19: Components and Instrumentation

## Slide 20: Cryogenic Low-Noise Amplifiers
InP HEMT
Cooled typically to 15K.
Noise temperature 5 times the quantum limit () up to 100 GHz
  that is, 5-photon detection threshold
  Noise figure as low as ~0.04 dB
Much better dynamic range than cryogenic amplifiers typical of quantum computing.
Notes: Best result is about 2-3K at <10 GHz (about 0.04 dB NF)
P1dB on the order of -15 dBm

## Slide 21: Superconducting Mixers
Based on superconducting-insulating-superconducting (SIS) tunnel junction.
  Nb/Al-AlN/Nb
Approx. 1 μm junction size.
Near quantum-limited performance, 100 GHz to 1 THz.
Balanced and sideband-separating configurations.
Notes: Mixer is near quantum-limited (maybe 1.5 hv/k), but receiver noise also must include IF cryo amplifier
Crossover point for LNA-first and SIS-first receivers is about 100 GHz.

## Slide 22: Custom mm-wave MMICs
Various Functions:
  Power amplifiers
  Schottky-diode mixers
  Varactor multipliers
  Switches
  Variable Attenuators
Broadband
Typically 50-100 GHz

## Slide 23: Integrated Modules
Analog-Digital-Photonic subassemblies.
cm-wave to mm-wave
Wideband, warm receiver chains
  RF-baseband conversion
  Analog-digital conversion
  Copper-fiber conversion
  Filtering
  Power leveling
Compact laboratory signal sources and testers

## Slide 24: Full Receiver Assemblies
ALMA Band 6 (211–275 GHz)
Warm and Cold Cartridges
Full 10-Band ALMA Cryostat

## Slide 25: Digital Correlators
The correlator converts data from multiple telescopes into images.
  Actually, hyperspectral image cubes
The ALMA Correlator is one of the most powerful supercomputers in the world:
  134 million processors
  17 peta-ops
Notes: 1 The supercomputer operating at the highest altitude in the world
200 Kilometers of fiber opticconnect ALMA to the city of Calama, where it connects to Antofagasta, Santiago and the rest of the world
17 PetaOperations (17 trillion operations per second), equivalent to billions of dollars in personal computers to make the necessary calculations. This is the fastest computer ever used in an astronomical site
134 Million processors
2912 Printed circuits
5200 Cables of interface
20 Million welding points
2016 Antenna pairings which make the correlator capable of simultaneously running the interferometry
1 Second every three million years is the possible delay in the atomic watch (hydrogen maser) that allows ALMA to observe in synchronization with other telescopes

## Slide 26: Technical Focus: Reflectionless Filters

## Slide 27: What is a Reflectionless Filter?
Pass-Band
x(t)
y(t)
Pass-Band
Stop-Band
Stop-Band

## Slide 28: Issues with Conventional Filters
Spurs Recirculate
Standing Waves
Accumulate
Switching
Transients
Rebound
Harmonics
Trapped
×N

## Slide 29: Benefits of Reflectionless Filters
Spurs Minimized
Standing Waves
Eliminated
Switching
Transients
Absorbed
Harmonics
Dissipated
×N

## Slide 30: A Symmetric Two-Port Network, “N”
Port 1
(Input)
Port 2
(Output)
(symmetry plane)

## Slide 31: A Symmetric Two-Port Network, “N”
(wires)
Identical half-circuits

## Slide 32: Even-Mode Excitation
i = 0
X
+
+

## Slide 33: Even-Mode Excitation
Even-Mode
Equivalent Circuit

## Slide 34: Odd-Mode Excitation
+
–
v = 0

## Slide 35: Odd-Mode Excitation
Odd-Mode
Equivalent Circuit

## Slide 36: Even and Odd-Mode Analysis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd
 = ½(even + odd)
T = ½(even – odd)

## Slide 37: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd
 = ½(even + odd)
T = ½(even – odd)
= 0
= T(f)
Therefore...
even = –odd
even = T(f)
duality
~high-pass transformation

## Slide 38: Duality

## Slide 39: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd
LC High-
Pass Filter
?
DUAL

## Slide 40: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd
DUAL

## Slide 41: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd

## Slide 42: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd
?

## Slide 43: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd

## Slide 44: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd

## Slide 45: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd

## Slide 46: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd

## Slide 47: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd

## Slide 48: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd

## Slide 49: Even and Odd-Mode Synthesis
Odd-Mode
Equivalent Circuit
Even-Mode
Equivalent Circuit
even
odd

## Slide 50: Even and Odd-Mode Synthesis
symmetry
duality
x
x
x
x
x
x
x
x

## Slide 51: A Third-Order Reflectionless Filter
s11
1
1
(Element values are normalized
for frequency and impedance.)
1
1
1
1
1
1
1
1

## Slide 52: Higher-Order Responses Not So Great
s11
1
1
1
1
1
1
1
1
1
1
(Element values are normalized
for frequency and impedance.)
1
1
1
1

## Slide 53: Higher-Order Responses Not So Great
s11
1
1
1
1
1
1
1
1
1
1
(Element values are normalized
for frequency and impedance.)
1
1
1
1
1
1
1
1

## Slide 54: Subnetwork Expansion

## Slide 55: Subnetwork Expansion
termination
termination
H
H
H
H
P
P
P
P
a1
b2
b3
a4
b1
a2
a3
b4
Port 1
Port 2
"Port 3"
"Port 4"
reflectionless
a1
b1

## Slide 56: Subnetwork Expansion
H
H
H
H
P
P
P
P
a1
b2
b3
a4
b1
a2
a3
b4
A
A
termination
termination
Pt. 3 common Pt. 4
Matched, Two-Port
Subnetwork

## Slide 57: Subnetwork Expansion
Pt. 3 common Pt. 4
Matched, Two-Port
Subnetwork

## Slide 58: A Seventh-Order Reflectionless Filter
s11
1
(Element values are normalized
for frequency and impedance.)
1
2x
x
x
y
y
2y
x
x
2x
y
y
z
z
2y
2z
z
z
2z
x = y = z = 1

## Slide 59: Element Value Generalization
s11
(Element values are normalized
for frequency and impedance.)
2/g1
1/g2
1/g2
1/g2
1/g2
2/(g3–g2)
1/g4
2/(g3–g4)
1/g4
1/g4
1/g4
2/(g5–g4)
1/g6
2/(g5–g6)
1/g6
1/g6
1/g6
2/g7
g1 = g2
g6 = g7
1
1

## Slide 60: Topological Generalization
s11
(Element values are normalized
for frequency and impedance.)
2/g1
1/g2
1/g2
1/g2
1/g2
2/(g3–g2)
1/g4
2/(g3–g4)
1/g4
1/g4
1/g4
2/(g5–g4)
1/g6
2/(g5–g6)
1/g6
1/g6
1/g6
2/g7
1
1
2/(g7–g6)
2/(g1–g2)

## Slide 61: Limiting Ripple Factor
(Element values are normalized
for frequency and impedance.)
2/g1
1/g2
1/g2
1/g2
1/g2
2/(g3–g2)
1/g4
2/(g3–g4)
1/g4
1/g4
1/g4
2/(g5–g4)
1/g6
2/(g5–g6)
1/g6
1/g6
1/g6
2/g7
1
1
2/(g1–g2)
2/(g7–g6)

## Slide 62: Negative Element Mitigation
(Element values are normalized
for frequency and impedance.)
2/g1
1/g2
1/g2
1/g2
1/g2
2/(g3–g2)
1/g4
2/(g3–g4)
1/g4
1/g4
1/g4
2/(g5–g4)
1/g6
2/(g5–g6)
1/g6
1/g6
1/g6
2/g7
1
1
2/(g1–g2)
2/(g7–g6)
–
+
+
+
+
+
=

## Slide 63: Negative Element Mitigation
(Element values are normalized
for frequency and impedance.)
2/g1
1/g2
1/g2
1/g2
1/g2
2/(g3–g2)
1/g4
2/(g3–g4)
1/g4
1/g4
1/g4
2/(g5–g4)
1/g6
2/(g5–g6)
1/g6
2/g7
1
1
2/(g1–g2)
1/g7
1/g7
2/(g6–g7)
1:1
The rest of the filter...

## Slide 64: Negative Element Mitigation
(Element values are normalized
for frequency and impedance.)
2/g1
1/g2
1/g2
2/(g1–g2)
The rest of the filter...

## Slide 65: Negative Element Mitigation
(Element values are normalized
for frequency and impedance.)
2/g1
1/g2
1/g2
2/(g1–g2)
The rest of the filter...
ia
ia+ib
ib

## Slide 66: Negative Element Mitigation
(Element values are normalized
for frequency and impedance.)
2/g1
1/g2
1/g2
2/(g1–g2)
The rest of the filter...
ia
ib
ia
ib

## Slide 67: Negative Element Mitigation
(Element values are normalized
for frequency and impedance.)
2/g1
2/(g1–g2)
The rest of the filter...
1/g2
1/g2
–
+
+
+
+
+
=

## Slide 68: Negative Element Mitigation
2/g1
1/g1
1/g1
2/(g2–g1)
1/g2
1/g2
A little redundant...
2/(g2–g1)
1:1
2/(g3–g2)
1/g4
2/(g3–g4)
1/g4
1/g4
1/g4
2/(g5–g4)
1/g6
2/(g5–g6)
1/g6
2/g7
1
1
1/g7
1/g7
2/(g6–g7)
1:1

## Slide 69: No More Negative Elements!
2/g1
1/g1
1/g1
1/g2
1/g2
2/(g2–g1)
1:1
2/(g3–g2)
1/g4
2/(g3–g4)
1/g4
1/g4
1/g4
2/(g5–g4)
1/g6
2/(g5–g6)
1/g6
2/g7
1
1
1/g7
1/g7
2/(g6–g7)
1:1
s11

## Slide 70: Elliptic Filters
A. Guilabert, M. Morgan, and T. Boyd, “Reflectionless filters for generalized elliptic transmission functions,” IEEE Transactions on Circuits and Systems I, vol. 66, no. 12, pp. 4606-4618, December 2019.
R1
1:1
L1
L3
C4
L5
C6
1:1
L4
C5
L6
C10
L8
C12
1:1
L7
C11
C13
C15
C14
1:1
C16
C1
C3
C2
C7
C9
C8
R2
1:1
L2

## Slide 71: Transmission-Line Solutions As Well...
ze = √ρ, zo = 1/√ρ
(x–x–1) –1
(x–x–1) –1
x–x–1
x–x–1
1
1
(x–x–1) –1
(x–x–1) –1
x–x–1
x–x–1
1
1
x
x
ρ = (x+√(x2–1))2
ρ = 1+2(x–x–1)+2 √((x–x–1)(1+x–x–1))
ze = 2ρ/(ρ +1), zo = 2/(ρ +1)
s11

## Slide 72: Planar Die Implementation

## Slide 73: Planar Die Implementation

## Slide 74: Now Marketed by Mini-Circuits

## Slide 75: Adopted by Industry
Key Application Areas:
  Test and Measurement
    VNAs
    Signal sources
    Spectrum analyzers
  Telecommunications
    Not in handsets themselves, but in handset verification systems
    Base station hardware
  Defense
Nearly 900 technology companies now taking advantage of reflectionless filters, including:
ANRITSU
NOKIA
TERADYNE
KEYSIGHT
ROCKWELL
NORTHROP GRUMMAN
COBHAM
ANALOG DEVICES
SPACE EXPLORATION TECHNOLOGIES
BAE
RAYTHEON
ROHDE & SCHWARZ
NATIONAL INSTRUMENTS
ADVANTEST
LOCKHEED-MARTIN
MERCURY SYSTEMS
APPLE COMPUTER
TEKTRONIX INC
VIASAT
QUALCOMM
MITSUBISHI
L3 HARRIS

## Slide 76: References
Books and Book Chapters
M. Morgan, Reflectionless Filters, Norwood, MA: Artech House, January 2017.
M. Morgan, “Reflectionless filter topologies,” Wiley Encyclopedia of Electrical and Electronics Engineering, pp. 1-13, August 2019.
M. Morgan, “Planar reflectionless filters.” In J. Hong, ed., Advances in Planar Filters Design, London: SciTech Publishing, 2019.
Academic Papers and Magazine Articles
A. Guilabert, M. Morgan, and T. Boyd, “Reflectionless filters for generalized elliptic transmission functions,” IEEE Transactions on Circuits and Systems I, vol. 66, no. 12, pp. 4606-4618, December 2019.
R. Shrotriya and M. Morgan, “Filtering without reflections: flattening multiplier chain conversion efficiency & more,” Microwave Journal White Paper, September 2019.
M. Morgan, W. Groves, and T. Boyd, “Reflectionless filter topologies supporting arbitrary low-pass ladder prototypes,” IEEE Transactions on Circuits and Systems I, vol. 66, no. 2, pp. 594-604, February 2019.
M. Morgan, “Think outside the band: design and miniaturization of absorptive filters,” IEEE Microwave Magazine, vol. 19, no. 7, pp. 54-62, November 2018.
M. Morgan, “A better way to filter -- part I,” NRAO Blog, March 29, 2018.
R. Setty, B. Kaplan, M. Morgan, and T. Boyd, “Combining MMIC reflectionless filters to create UWB bandpass filters,” Microwave Journal, vol. 61, no. 3, pp. 60-72, March 2018.
M. Morgan and T. Boyd, “Reflectionless filter structures,” IEEE Trans. Microw. Theory Techn., vol. 63, no. 4, pp. 1263-1271, April 2015.
M. Morgan and T. Boyd, “Theoretical and experimental study of a new class of reflectionless filter,” IEEE Trans. Microwave Theory Tech., vol. 59, no. 5, pp. 1214-1221, May 2011.
Application Notes
“Advantages of cascading reflectionless filters,” Mini-Circuits Application Note, AN75-008.
“Pairing mixers with reflectionless filters to improve system performance,” Mini-Circuits Application Note, AN75-007.
Patents
M. Morgan, “Deep rejection reflectionless filters,” U.S. Patent No. 10,530,321, January 7, 2020, Taiwan Patent No. I699970B, July 21, 2021.
M. Morgan, “Sub-network enhanced reflectionless filter topology,” U.S. Patent No. 9,705,467, July 11, 2017, No. 10,230,348, March 12, 2019, Taiwan Patent No. I581494B, May 1, 2017, People’s Republic of China Patent No. 107078708B, February 9, 2021.
M. Morgan, “Optimal response reflectionless filter topologies,” U.S. Patent No. 10,516,378, December 24, 2019.
M. Morgan, “Optimal response reflectionless filters,” U.S. Patent No. 10,374,577, August 6, 2019, No. 10,263,592, April 16, 2019. Taiwan Patent No. I653826B, March 11, 2019.
M. Morgan, “Transmission line reflectionless filters,” U.S. Patent No. 9,923,540, March 20, 2018, No. 10,277,189, April 30, 2019, Japan Patent No. 6652970B2, January 28, 2020, 6964152B2, October 20, 2021.
M. Morgan, “Reflectionless filters,” U.S. Patent No. 8,392,495, March 5, 2013. People's Republic of China Patent No.102365784B, July 30, 2014.

## Slide 77: Thank You!