## Slide 1: CEBAF – unique accelerator, present and future Continuous Electron Beam Accelerator Facility
Andrei Seryi
Jefferson Lab Associate Director for Accelerator Operations and R&D
Low-Level Radio Frequency (LLRF) Workshop 2025
13-16 October

## Slide 2: Outline
Jefferson Lab and CEBAF – mission and history
Recent run highlights
CEBAF overview
  6 GeV era
  12 GeV era
Future CEBAF upgrades
  Polarized positrons
  22 GeV upgrade
Coffee break LLRF challenge

## Slide 3: Location and History
Thomas Jefferson National Accelerator Facility, or JLab, is located in Newport News, Virginia, next to many historical landmarks
1984-1987 – funding, selection of SC RF, start of construction
1995 – start of CEBAF operation at 4 GeV
2000 – CEBAF reached 6 GeV
2017 – completion of 12 GeV upgrade project
Fort Monroe. 20min drive from JLab
Jefferson Lab by the numbers: ~ 960 employees
~ 1,600 Active Users worldwide

## Slide 4: Jefferson Lab’s Scientific Mission
CEBAF Upgrade completed in September 2017
  CW electron beam
  Emax = 12 GeV
  Imax = 90 mA
  Polmax ~ 90%
B
A
D
C
Physics Operation
  4 halls running simultaneously since January 2018
Nuclear experiments at ultra-high luminosities, up to 1039 electrons-nucleons /cm2/ s
World-record polarized electron beams
Highest intensity tagged photon beam at 9 GeV
Unprecedented stability and control of beam properties  Excellent for low energy Standard Model tests
Ability to deliver a range of beam energies and currents to multiple experimental halls simultaneously
CEBAF World-leading Capabilities
INJECTOR
LINACS
RECIRCULATION ARCS
1
2
2
3
3
Located in Newport News (VA) – In operation since 1995
Our mission is to understand the subatomic constituents of protons and neutrons and the force that holds them together – the strongest force in the Universe
Our primary research tool is CEBAF - a superconducting high-energy electron particle accelerator

## Slide 5: CEBAF at Jefferson Lab
1
Polarized injector
The injector produces polarized electron beams for the experiments
2
Linear accelerators 1497 MHz
Straight sections have 25 cryomodules each. Beam travels up to 5.5 passes through linacs to get to 12 GeV
3
Central Helium Liquefier
CHL keeps SRF cavities at 2K temperature
4
Recirculation magnets
Dipoles and quadrupole magnets to focus and steer beam as it pass along each arc
Circumference of the tunnel is 1.4km

## Slide 6: CEBAF at Jefferson Lab
5
Experimental Hall A
Two High Resolution Spectrometers for precise measurements of nuclei inner structure
6
Experimental Hall B
CEBAF Larch Acceptance Spectrometer (CLAS12) surrounds the target to measure many angles simultaneously
7
Experimental Hall C
High Momentum Spectrometer measures nuclei structure at high energy and high beam current
8
Experimental Hall D
Equipped with SC magnet and detector to study strong force that binds quarks together
Circumference of the tunnel is 1.4km

## Slide 7: CEBAF Accelerator – Technical Scope
>800 Beam Position Monitors
52-1/4 Cryomodules with 418 SRF Cavities to Accelerate Electrons in CEBAF
~500 Large Dipoles powered by >40 HVPS
>2800 Magnets to Focus and Steer Beam
16 RF Deflectors for Extracting Beams
Capable of delivering 4 independent CW polarized electron beams simultaneously to experiment Halls.
Over 7 km of beamline ~800 BPMs, 60 harps, 150 viewers, and 7 synchrotron light monitors.
>580,000 data channels on a distributed network of over 600 local computers with 200 kHz data rate.
418 Klystrons for 52.25 Cryomodules
High Power Exp Hall Beam Dump

## Slide 8: CEBAF FY25 Run – excellent run, best in 12 GeV era
CEBAF reliability, weekly and average since 03/19 (beginning of the run) until 09/03.
The figure also shows the CEBAF average FY24 run reliability (09/23 – 05/24), 75.2%, for reference.
22 weeks of Physics + 2 weeks of beam restore
Energy gain 1060 MeV/linac (E5.5 = 11.7 GeV)
Beam power up to 830 kW
Polarized beams to Halls A, B, C, D
FY25 Delivered Beam Statistics (hours):
Total delivered beam (h) | 3236
Delivered research (h) | 2767.4
Delivered beam study (h) | 142.9
Delivered tuning, setup, restore (h) | 325.7
Unscheduled failure (h) | 500
Total scheduled (h) | 3736
Reliability (%) | 86.6
DOE Requirement for FY25,
total delivered 3000 h,
exceeded by 8%.
Exceeded DOE Requirements of 85% reliability

## Slide 9: CEBAF Construction
Construction started ~1987
Cut and cover tunnel construction
Tunnel is below water table
Good ground water protection

## Slide 10: CEBAF Construction
Tunnels before hardware installations
Arcs in 6 GeV era (four beamlines)

## Slide 11: CEBAF three halls era – 6 GeV
6 GeV era configuration

## Slide 12: CEBAF Injector
Dump
6 GeV era configuration
RF cavity
(499 MHz)
RF cavity
(499 MHz)
5 MeV Dump
DC light, most beam thrown away
Three RF-pulsed lasers
Pre-buncher added

## Slide 13: CEBAF load-lock polarized gun
100kV gun (circa 2007). Lifetime limited to 30C. Path to higher lifetime and beam quality – higher voltage
Laser light that shines on the Gallium Arsenide photocathode is RF pulsed at 499 MHz and creates an RF microstructure on the electron beam
499 MHz is a sub-harmonic of the fundamental accelerator operating frequency 1497 MHz
During three-hall operations, three separate 499 MHz lasers—one for each hall—are used to generate three interlaced electron beams
Continuous Wave Beam for Physics
Pulsed beam for optics tuning

## Slide 14: CEBAF polarized source and performance evolution
Technology advances for e-beam polarization improvements
  Bulk GaAs
  Strained GaAs
  Strained Superlattice GaAs/GaAsP
  Strained Superlattice – Distributed Bragg Reflectors
Polarization above 85%
Electron gun design also advanced
New experiments demanded longer lifetime of cathodes and new design of guns
  ILC played a stimulating role for development of new ILC/CEBAF “Inverted gun”

## Slide 15: CEBAF Inverted Gun
Inverted CEBAF/ILC Gun#1 installed at CEBAF, July 2009
Higher voltage, higher lifetime
200 kV for CEBAF, 350 kV for ILC

## Slide 16: CEBAF Diagnostics
Synchrotron Light monitors
BPMs
Beam size wire monitors
Pathlength monitors
Beam Loss monitors
Etc.
Beam viewer

## Slide 17: CEBAF Tune Beam
Continuous Wave Beam for Physics
Pulsed low power beam for accelerator optics tuning
The 250 ms pulse width at 60 Hz provides a 1.5% duty cycle
Nominal pulse height is 4 mA
Beam power is 720 W for a 12 GeV beam at this duty factor
The 4 ms trailing pulse is for measuring linac BPM orbits and linac arrival time

## Slide 18: CEBAF SRF cavities and cryomodules
Cryomodule types
  C20 – has four pairs of C20 5-cell cavities
  C50 – improved performance C20
  C100 – eight 7-cell cavities assembled in string
    Installed during 12 GeV upgrade, use higher power klystrons
  C75 – upgraded C20 with new cell shape, ingot Nb, enhanced cleanness & magnetic hygiene
    Being implemented now, to increase and maintain the energy
C20 SRF cavity pair
7-cell SRF cavity for C100

## Slide 19: CEBAF 12 GeV Upgrade
Double maximum accelerator energy
  Ten new high gradient cryomodules
  Double Helium refrigeration plant capacity
  Civil construction and upgraded utilities
Add 10th arc of magnets for 5.5 paths machine
Add 4th experimental hall D
New experimental equipment in halls B, C, D
Project completed in September 2017

## Slide 20: Enabling simultaneous four hall availability in 12 GeV
With addition of the new Hall D and new Arc 10, there was a need to re-configure the separation system to allow sending the beam to hall D too
Instead of 500MHz system, use 750 MHz (half of fundamental frequency) separator for 5th pass

## Slide 21: 750MHz separator hardware
500MHz RF separator cavities (two higher beamlines) and the new 750 MHz separator cavity (lowest beamline)

## Slide 22: Spreaders and recombiners
Vertically achromatic system designed to accept broad range of multi-pass input parameters for recirculation transport
Recombiner is mirror-symmetric to the Spreader
West recombiner
West spreader

## Slide 23: Recirculation arcs
Sixteen dipoles for Arc 1 and Arc 2 and thirty-two dipoles for Arc 3-10
The arcs radius is 80 m
Each Arc has 32 quadrupole girders grouped in 4 families to control achromaticity, momentum compaction and the betatron tune
Arc dipoles
Arc quadrupoles

## Slide 24: Extraction system
Horizontal extraction systems at 500 MHz for 1st through 4th pass
Vertical extraction system at 500 MHz for 5th pass
Horizontal extraction system at 750 MHz for 5th pass to enable simultaneous four hall operation
750MHz
500MHz

## Slide 25: CEBAF four hall operations – since April 2018
Four-Hall and Full Power Operations
Stable Full Power Operation demonstrated on April 23rd 2018
Routine 4-Hall Operations from Spring 2018 Run and beyond
Injector
65 mA
Hall A
22 mA
Hall B
150 nA
Hall C
40 mA
Hall D
150 nA
Injector
85 mA
Injector
98 mA
Hall C
10.6 GeV
85 mA
Hall A
4.6 GeV
23 mA
Hall C
10.6 GeV
75 mA
Beam Power 900 kW
Fast Recovery to Full Power
Simultaneous 4-Hall Beam Delivery (~90 minute time slice)
Full Power Beam Delivery (~45 minute time slice)

## Slide 26: CEBAF 12 GeV Science is Exciting and Impactful
CEBAF experimental schedule extends ~10 years into the future. Every year new experiments are approved

## Slide 27: Electron-Ion Collider & CEBAF upgrade
JLAB is strongly engaged in EIC project
  Lead and co-lead several technical areas
(*) CEBAF upgrade is not yet an approved project or program. It represents JLAB and community efforts on defining our future. CEBAF upgrade is positively described in the recent NP Long Range Plan.
CEBAF upgrade*
  Will create complementary to EIC experimental program, boosting NP science portfolio
    22 GeV and polarized positrons

## Slide 28: CEBAF 12 GeV Upgrade – was done with added SRF cryomodules
Double maximum accelerator energy
  Ten new high gradient cryomodules
  Double Helium refrigeration plant capacity
  Civil construction and upgraded utilities
Add 10th arc of magnets for 5.5 paths machine
Add 4th experimental hall D
New experimental equipment in halls B, C, D
Project completed in September 2017
CEBAF 22 GeV upgrade will be done without adding more RF

## Slide 29: Energy upgrade foundation
CEBAF – separate arc for each different energy
EMMA (Electron Model for Multiple Applications) –demonstrated that orbits can be compacted to within 10 mm in radius over an electron momentum range of 12–18 MeV/c
Acceleration in the linear non-scaling fixed-field alternating-gradient accelerator EMMA, S. Machida, et al., Nature Physics volume 8, pages 243–247 (2012)

## Slide 30: Energy upgrade foundation
CEBAF – separate arc for each different energy
CBETA (Cornell-Brookhaven energy recovery linac Test Accelerator) – the fixed-field alternating-gradient optical system used for the return loop successfully transported electron bunches of 42, 78, 114, and 150 MeV in a common vacuum chamber
CBETA: First Multipass Superconducting Linear Accelerator with Energy Recovery, A. Bartnik, et al., Phys.Rev.Lett. 125 (2020) 4, 044803
EMMA & CBETA FFA approach: we can increase number of passes through CEBAF linac without the need to increase the number of arcs

## Slide 31: Compact FFA FODO Cell – How Does it Work?
Large momentum acceptance FFA cell, configured with combined function magnets capable of transporting multiple energy beams through the same string of permanent magnets (six beams with energies spanning a factor of two)
1 T
50 T/m
magnets: from 38cm2 to 78cm2
BD
BF
BD
BF
BD
BD
Closely spaced orbits for all six beams (~ 1 cm)
Extremally low dispersion (a few mm) in a combined function lattice
Self similar beta functions for different energy beams

## Slide 32: Energy: Four Different Energy Beams Bending in One FFA Line
Four beams from different passes Bending in the Arc through one FFA beamline.
FFA Arc
Passes 4,5,6, and 7
in one pipe
Stephen Brooks
BNL

## Slide 33: Polarized positrons capability foundation
Joe Grames et al.
Production of Highly Polarized Positrons Using Polarized Electrons at MeV Energies
D. Abbott et al. (PEPPo Collaboration), Phys. Rev. Lett. 116, 214801 – Published 27 May 2016

## Slide 34: CEBAF polarized e+ design
Design of Ce+BAF injector and critical risk areas
Plan to test two prototype targets at LERF
  Rotating solid tungsten (JLab/ODU) and liquid GaInSn (Xelera SBIR Phase 2)
LDRD for high current photogun at GTS & Beam Degrader
  Aim for 10 mA @ 10 MeV, up to 90% polarization, long lifetime
  Degrade e- beam to mimic larger emittance e+ beam
Positron generation and capture simulations
  Integrated optimized design is emerging
GaInSn and Tungsten Targets
Polarized e- Source
Joe Grames and the team

## Slide 35: CEBAF 22 GeV upgrade design
Increase the energy without additional RF
Increase the number of recirculation passes with Fixed Field Accelerator (FFA) technology
  Remove the highest recirculation pass (Arc 9 & A) and replace them with two compact FFA arcs
  Include time-of-flight (TOF) Splitter bend systems.
  New 650 MeV recirculating injector
  LDRD on permanent magnets; Fruitful collaboration with BNL and ORNL
Focusing Magnet BF
Defocusing Magnet BD
Permanent Magnets for FFA arcs – BNL fruitful collaboration
FFA arc
FFA arc
Alex Bogacz and the team

## Slide 36: LLRF Workshop Coffee Breaks Challenge – 100mA multi-pass ERL LLRF
Future high energy (multi-GeV), high current (hundreds of mA) beams would require GW RF systems
Energy recovery alleviates extreme RF power demands
Successful GeV scale ELR demo at CEBAF: ratio of accelerated : recovered energies (50:1)
https://accelconf.web.cern.ch/p03/PAPERS/TOAC006.PDF
Beam is injected into the North Linac at 56 MeV where it is accelerated to 556 MeV. The beam traverses Arc1 and then begins acceleration through the South Linac where it reaches a maximum energy of 1056 MeV. Following the South Linac, the beam passes through a newly installed phase delay chicane. The chicane was designed to create a path length differential of exactly ½-RF wavelength so that upon re-entry into the North Linac, the beam is 1800 out of phase with the cavities and will subsequently be decelerated to 556 MeV. After traversing Arc1 the beam enters the South Linac - still out of phase with the cavities - and is decelerated to 56 MeV at which point the spent electron beam is sent to a dump. In this way the beam gives energy back to the RF system, which may be used to accelerate subsequent beam.
What are LLRF features and challenges for CEBAF-like, 5-pass ERL with 100 mA injected current?

## Slide 37: Summary
CEBAF provides unique opportunities for nuclear physics studies
  12 GeV upgrade completed in 2017
  Four halls running simultaneously since January 2018
  Recent run exceeded DOE requirements in delivered hours and reliability
  Large numbed of planned and approved experiments for decade into the future
CEBAF 22 GeV staged approach via e+ : modern, energy efficient and affordable, complementary to EIC
Thank you!