## Slide 1: High energy and slow positron sources at KEK
2026/3/26
KEK Accelerator Lab.
Yoshinori Enomoto

## Slide 2: Outline
Introduction of positron facilities in KEK
Difficulties and challenges for R&D of positron sources
----------------------------------------------------------
Slow positron source with deceleration cavity
  High energy positron source technology adopted to slow positron production

## Slide 3
SPF (slow positron facility)
SuperKEKB
PF
Injector linac
Positron source for SuperKEKB
Main entrance
R&D area
Positron source for ILC
Google street view is available

## Slide 4: Slow positron facilities in Japan
Tokyo university of science
RI & Trap
KURNS-LINAC(Kyoto University,Institute for Integrated Radiation and Nuclear Science)
Linac
KUR (Kyoto University Research Reactor)
Reactor
AIST (National Institute of Advanced Industrial Science and Technology),
Linac
QST (National Institute for Quantum Science and Technology)
RI

## Slide 5: positron facilities and KEK injector linac
A few tens meter distance
Positron source
(SPF)

## Slide 6
https://www2.kek.jp/imss/spf/eng/

## Slide 7: KEK and high energy positron source
From TRISTAN to ILC
  KEK LINAC has keep providing positron beam to e+e- collider experiment since 1980s.
  Positron source for SuperKEKB is world’s most intense positron source in operation.
TRISTAN
KEKB
SuperKEKB

## Slide 8: Prototype for ILC

## Slide 9: Big Jump from Present to Future
Chart: e- beam power (kW)
| 8.9999999999999993E-3 | 1.52E-2 | 4.2999999999999997E-2 | 0.125 | 4 | 0.91200000000000003 | 1 | 3.5 | 4 | 13.32 | 27 | 56.32 | 62.9 | 73.260000000000005
Ne+/Ne-/GeV | 0.073 | 0.063 | 0.05 | 0.014 | 0.0375 | 0.013 | 0.03 | 0.114 | 0.025 | 0.11667 | 0.036 | 0.28 | 0 | 0.43
●past
▲present
◆future
ILC e-driven
High power
High efficiency
SLC
SuperKEKB
FCCee
(many options)
ILC undulator
CLIC
CEPC
KEKB
BEPC
DAFNE
VEPP-5
 | SKEKB | ILC
e- energy | 3.2 GeV | 3 GeV
e- charge/bunch | 10 nC | 3.7 nC
Repetition | 50 (25) Hz | 5 Hz
Num. bunches | 2 | 1320 = (33+33) x 20
Total charge / s | 1000 (500) nC | 24667 nC
Beam power on target | 3.2 | 74
yield | 0.4 | 1.1
Beam power requirement for Ce+BAF is close to ILC

## Slide 10: Schedule and status
FY |  | 2022 |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  | 
year |  |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  |  | 
Quarter |  | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1
Test bench |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
High power test bench |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
W-Cu connection |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Target unit | Rotation mechanism |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Disk |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FC base | 1st unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
magnet | Solenoid |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Power supply |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Chamber, vacuum, support |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Acc. structure | 1st unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FC power supply |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design
Manufacturing
test
Now!
This work was supported by 【MEXT Development of key element technologies to improve the performance of future accelerators Program】 Japan Grant Number JPMXP1423812204.

## Slide 12
https://www2.kek.jp/imss/mb-linq/
MB-LINQ: Multi quantum-Beam facility with superconducting LINac for material-Quantum-life sciences

## Slide 13: MB-LINQ
CDR published
  Details of facility are not yet fixed
In the context of PF (photon factory, a 40 years old SR light source in KEK) upgrade
  Number of users for light source is much larger than that for slow positron beam
Multi beam
  XFEL, SR, Laser
  Slow Positron
https://www2.kek.jp/imss/mb-linq/library/mblinq_cdr_ver2.0.pdf
Topmost-Layer Surface structure Science
Petahertz Quantum Materials Science
Attosecond Materials and Life Science
Extreme Nonlinear Optics
Leptonic-Atom Extreme-Precision Spectroscopy
Increase slow positron x100
108 →1010 slow e+/s
1 kW → 100 kW e- on target

## Slide 14: Positron source in KEK
Long history and operation experience of positron source
Both high energy physics and material science users
Both present and future projects
Everything goes well…..?

## Slide 15: Organization of KEK

## Slide 16: Importance of integrated system design and prototyping
Positron source is one of a most complex component in the accelerator
Slight change of layout affect the result
Integrated design including replacement mechanism etc.. is important
Initial cost is relatively high
For Slow positron
  High efficiency moderator
  Beamline for very low energy positron beam

## Slide 17: Importance and difficulties of beam test
Beam experiment is highly desirable to validate performance and reliability under high radiation environment
There are limited high power facilities
  SuperKEKB@KEK (3.5 kW)
  BEPC@IHEP
  VEPP@BINP
  --------------------------
  P3@PSI (Swiss FEL, < 10 W)
LERF@Jlab will be a valuable facility in this field.

## Slide 18: Comparison of high-power targets in Japan
Chart: 
 | 0.5 | 18.8 | 3.1 | 480 | 20 | 7.4 | 18
 | 2.5 | 55.2 | 996.9 | 520 | 730 | 87.6 | 64
Chart: 
 | 0.5 | 18.8 | 3.1 | 480 | 20 | 7.4 | 18
 | 2.5 | 55.2 | 996.9 | 520 | 730 | 87.6 | 64
 | e+ | e+ | μ | n | Neutrinos | Hadrons | RIBF
Institute | KEK (SuperKEKB) | ILC (e-driven) | J-PARC | J-PARC | J-PARC | J-PARC | RIKEN
Primary particle | e- | e- | p | p | p | p | C~U
Target material | W | W | C | Hg | C | Au | Be, W
Energy [GeV] | 3 | 3 | 3.5 | 3 | 30 | 30 | 0.345/u
Charge/pulse [nC] | 10 ✕ 2 | 3.7 ✕ 66 | 13300 | 13300 | 52900 | 16470 | CW
Repetition [Hz] | 50 | 100 / 300 | 25 | 25 | 0.47 | 0.19 | CW (1puA)
Beam Power [kW] | 3 | 74 | 1000 | 1000 | 750 | 95 | 82
Beam size σx ✕ σy [mm] | 0.5 ✕ 0.5 | 2 ✕ 2 | 3.5 ✕ 3.5 | 37 ✕ 17 | 4.2 ✕ 4.2 | 2.5 ✕ 1.0 | 0.42 ✕ 0.42
Thickness [mm] | 14 | 16 | 20 | 2000 | 909 | 66 (6 ✕ 11) | ~mm
Deposited power [kW] | 0.5 | 18.8 | 3.1 | 480 | 20 | 7.4 | 18
PEDD [J/g] | 27.5 | 33.6 | 20 | 1.1 | 190 | Slow extraction | CW
Cooling | Water | Water | Radiation | Water | He | Water | Water
structure | Fixed | Rotating | Rotating | Liquid | Fixed | Fixed | Rotating
Power (kW)
■■ beam power
■ deposited power
ILC
RIBF
n
H
μ
ν
ILC
RIBF
n
H
μ
ν
SKEKB
SKEKB

## Slide 19: Positron source in accelerator science
https://proceedings.jacow.org/ipac2024/classification/index.html
Number of people working on the positron source is very limited
  < 100 all the people in the world
Very limited investment for R&D
The left list is Table of classification of IPAC’24 PROCEEDINGS
  There are electron source, ion source, proton source, neutron source but there isn’t positron source
Most of the technologies were developed at SLAC in 1980s for the SLC.
We still rely on these data and experiences

## Slide 20: Difficulties and challenges for R&D of positron sources
High initial cost
Limited resource
Limited number of users
Wide and integrated knowledge

## Slide 21: Difficulties and challenges for R&D of positron sources
High initial cost
Limited resource
Limited number of users
Wide and integrated knowledge
Blue ocean!

## Slide 22: Situation in slow positron facility
p.459
1010 slow e+ /s by 100 kW e- beam is next goal

## Slide 23: Jlab’s accelerator technology and positron source
CW SC linac
  Bunch structure is suitable for some of slow positron experiment
    w/o buncher or stretcher
    Complementary to 50 Hz, NC linac in KEK
High-energy, high-power e- beam fixed target experience
  High power target and beam dump
  Radiation protection and safety
    Difficult for light source facilities

## Slide 24: Summary
KEK/Japan have several positron facilities and project
  Both high energy (GeV) and low energy (< a few tens keV)
  Both present and future
  Coherent R&D plan is necessary beyond projects and institute
Beam test is important
  Such facility is limited
Many difficulties and challenges exist
  Blue ocean
Jefferson lab’s positron project will bring valuable experiences and knowledge for intense positron source development in the world
Accelerator parameters are complementary to linac in KEK

## Slide 31: AMD (adiabatic matching device)
e+
e-
target
e+
target
Electron hit small point of the target.
Positron comes from small spot.
Angle distribution is large.
Adiabatically expand position distribution.
Angle distribution decrease.
Matched to the aperture of the following section.
B1
B２
Velocity : v1
Position : r1
Angle :φ1
Velocity : v2
Position : r2
Angle :φ2

## Slide 32: Deceleration injection to moderator
Fast
deceleration
Slow-
AMD
Converter
cavity
Moderator
Solenoid
Count
Count
0.1－35 keV
Realized for high energy positron source.
For slow positron production, replace downstream acc. cavities with moderator.
Cross sectional view of positron source for SuperKEKB
Technically difficult
1011 slow e+/s will be possible

## Slide 33
Back up

## Slide 34: High power electron beam
ACT2@NIFS (National Institute for Fusion Science)
  300 kW, 40 kV, electron beam test facility
Low energy (w/o RF acc.) high power DC electron beam is available
→ elector energy of > MeV is desirable for test facility

## Slide 35: Particle sources and positron source
Neutron source
Muon source
Neutrino source
Electron source
Ion source
Primary particle source
secondary particle source
Positron source is installed in the middle of accelerator
Collection and acceleration of secondary particles
need high power primary beam for full test
  Usually impossible before construction
Positron source source
Accelerator
High quality beam for acceleration
Stand alone test is possible
No radiational, thermal requirement
Low beam quality is acceptable
Need high power primary beam
Severe radiational, thermal requirement