## Slide 1: A high-power positron converter based on a recirculated liquid metal in-vacuum target
V.O. Kostroun, Joe Conway, Colwyn Gulliford, Will Hutter, Karl Smolenski, Nick Taylor
Xelera Research LLC
March 23, 2026
LEEPP Workshop

## Slide 2: Liquid metal (LM) targets: Introduction
The very large power in electron beams needed to generate positrons require that solid tantalum, tungsten, or tungsten-rhenium targets have some means of heat removal, e.g. by cooling high speed rotating discs of such materials.
The mechanical complexity of such rotating discs in the ultra high vacuum of an accelerator beam line suggests that other target possibilities be considered.
A free surface liquid metal jet target possesses some advantages. It is conceptually simple compared to a solid metal target, it can operate directly in an ultra high vacuum environment due to the very low vapor pressure of LMs used, it can handle very high heat loads and act directly as target coolant.
Two possible eutectics are GaInSn and PbBi. GaInSn is a liquid at 20°C while PbBi requires operation at 150°C. PbBi is preferable for positron production because of its higher Z and density. But since GaInSn is a liquid at room temperature, it was selected for this prototype.

## Slide 3
    Fixed targets (such as CESR) – tungsten windows / paddles, typically water cooled. Power density (melting, thermal stress) and cooling capacity (boiling of coolant) quickly limit maximum power capability
    Rotating targets – spread power deposition over a larger surface. Failure mode analysis, large / bulky, brute force, but still complex, thermal fatigue, radiation damage
    Liquid targets (Xelera)– power deposited in liquid itself, higher ultimate powers possible. Coolant and converter are one. Sufficiently novel to be considered for an SBIR grant / research funding.
Targets

## Slide 4: Options for Positron Converter Targets
Fixed
Moving / Rotating
Liquid Jet
Typical Objections
  Vacuum contamination
  Complexity
  Activation
  Stability of Jet
  Droplet formation

## Slide 5: GaInSn Positron Yield (proposed 10 MeV)
All GaInSn properties presented were calculated with the MCNP6.2 code
Positron Yield vs. thickness (cm and Xo)

## Slide 6
Energy and angular distribution of positrons from 3 mm thick GaInSn target
Angular and energy spread of positrons

## Slide 7
Positron production by 10 MeV electrons in various targets of roughly the same radiation length thickness
The PEPPo experiment at Jlab was designed to evaluate and demonstrate the PEPPo concept. A few mA, 85% polarized 8.25 Mev/c continuous electron beam generated positrons in a 0.1-1.0 mm tungsten target. (E. Voutier, Nucl. Theory 33, (2014))
From Yu. S. Tsai, “Pair Production and Bremmstrahlung of Charged Leptons”, Rev. Mod. Phys., 46:4, 815 (1974), one gets the radiation lengths for various elements. Xo for tungsten, (divided by the density of 19.25 g/cm3) is 0.3513 cm. Thus in the Jlab experiment the W thicknesses were 0.02847 – 0.2847 Xo.

## Slide 8: The properties of a GaInSn liquid metal nozzle were calculated using OpenFOAM, a free, open source CFD software.(https://openfoam.org) The basic nozzle design was taken from the paper by Gordeev et al. The nozzle contraction ratio given is four. Since the GaInSn positron target thickness at 10 MeV is 3mm, the rest of the nozzle dimensions were scaled accordingly, except for the nozzle width, which was set at 10mm. The shape of the nozzle is given by a fifth order polynomial as discussed in the paper by Bell and Mehta (JIAA TR-84. April 1988) y(x’)/Hi = 1-(1-He/Hi)(6 x’5 -15 x’4 + 10 x’3) Where 0 < x’< 1. x’ = x/L, L is the length of the contraction region and Hi and He are half the heights of the nozzle at input and exit respectively. (If the widths of the input, Wi and output, We, are the same, Hi/He is the contraction ratio, otherwise it is HiWi/HeWe.) The calculation was carried out using the OpenFOAM standard solver simpleFoam a steady-state solver for incompressible, turbulent flow, using the SIMPLE algorithm. As per Gordeev et al, the V2F model results exhibited a reasonably good agreement with measured results and therefore the v2f version in OpenFOAM was used in the present calculations.
Nozzle Design and CFD Simulation

## Slide 9
The GaInSn flow is shown in red and the nozzle walls in blue. So far, the best flow occurred for an input velocity U = 6 m/s.
Since the input area is 1.2 cm2, the flow of GaInSn has to be 1.2 cm2 times 600 cm/s or 0.72 l/s (11.41 gpm).
Nozzle Geometry

## Slide 10: View of the prototype positron converter

## Slide 11: View of the prototype positron converter

## Slide 12: Accomplishments along the way
Jet Laser doppler velocity measurements (through vacuum window)
EPICS control system for remote control
Impact of magnetic field on Jet
Liquid metal flow meters (Keyence vs. home made) (Calibration)
Jet thickness / stability image processing
Radioisotope production (in Backup)
Operational Gamma Field (neutrons too) (in Backup)

## Slide 13: Calibration of Laser Doppler Velocimeter (miniLDV)
Calibration method is based on a spinning wheel.
At a wheel rpm=3201, measured with a
CyberTech Digital Tachometer, w = 335.21
rad/s. The following data was obtained:
r(mm) v = rw (m/s) v (miniLDV)
18.13 6.077 6.075
21.78 7.300 7.296
24.56 8.233 8.226
28.35 9.503 9.497
32.15 10.777 10.770

## Slide 14: Example of Liquid Metal Jet Velocity Measurement
Digitized profile, fitted to
With a = 708, vo = 6.427 m/s
b = 0.308
Fitted vo = 6.427 (m/s), s = 0.218
miniLDV = 6.450 (m/s), s =0.268

## Slide 15: EPICS based control system
Remote control of 2 RPI cameras, viewing the thickness and width of the GaInSn jet
Online analysis of jet thickness (discussed later)
Remote control of the Dura Impulse GS 20 sensor-less drive (VFD) controlling the Liquiflo gear pump motor.
Readout of Measurement Science Enterprise miniLDV laser Doppler velocimeter
Readout of the Leybold Turbolab 300 l/s turbomolecular pump vacuum and Gamma Vacuum ion pump
Readout of the Keyence MD-MZ50AYK flow meter.
Flow Monitors:
Temperature Monitors:
Jet Characterization:
Gear pump and Vacuum:
Readout of thermocouples (K-type) by serving DataQ instruments Di808 data logger to EPICS
Water inlet/outlet
GaInSn coming inlet/outlet
LiquiFlo Gear Pump

## Slide 16: Example of Data Logged and Stored (6.5 m/s)
Dashboards via Holoviews Python package Basic dashboard served securely over web EPICS PVs updated on 1 - 10 Hz range
Data logging script for saving comprehensive data set for a single experimental run (tested over hours)
Scripts for combing logged camera images into movies
Scripts for plotting logged data traces over the course of a full experiment

## Slide 17
25 Hour Duration Run (Thermal / Vacuum)
1st Run
Note: with solenoid magnet

## Slide 18
36 Hour Duration Run (Thermal / Vacuum)
2nd Run
Thermocouple fell off
Note: with solenoid magnet

## Slide 19
Heat Exchanger tests (Thermal / Vacuum)
Short Run
Note: with solenoid magnet removed
minutes

## Slide 20: 36 Hour Duration Gun (Start / End)

## Slide 21: Time Lapse video

## Slide 22: Jet Images (beam direction / side view)

## Slide 23: Effect of magnetic field on jet flow (6.5 m/s)
A 3 x 1 ½” NdFeB N52 magnet was used to investigate the effect of a magnetic field on the jet behavior.
At the jet center, 19.5 mm from the magnet, the B field is 2400 Gauss – no measurable impact on jet

## Slide 24: Liquiflo Gear Pump: Flow vs Speed Curve
Pump manufacture data gives Flow = 6.14 x 10-3 * Pump RPM - 0.76
At 1588 RPM, the fitted flow rate is 8.99 GPM, while the Liquiflo curve gives 9 GPM
Also plotted in red is the curve Flow = 9/1588 speed, based on the amount pumped per revolution.
The Flow (GPM) vs Speed Curve (RPM) and the Performance Curve provided by the manufacturer for a 2.45 cP fluid (viscosity of GaInSn at room temperature) are needed
The performance curve shows that the flow rate is essentially independent of the differential pressure.

## Slide 25: Calibration of the Variable Frequency Drive
At 60 Hz, the motor rated speed is 1750 RPM. Giving 29.167 RPM/Hz.
Speed was measured with the CyberTech digital tachometer at different VFD frequencies
A linear fit to the data gives
speed = 29.73 x freq-1.0
To convert frequency to pump flow, replace speed in
flow = 6.14522 x 10-3 speed - 0.76451923 with speed = 29.73333 x freq-1.0
So that
flow = 0.1827179 x freq-0.7706645
The resulting plot of flow vs frequency is
At 6 Hz, the flow rate is 0.326 GPM
at 6 Hz, pump speed is 177 RPM
177 RPM corresponds to 0.323 GPM
At 60 Hz, the flow rate is 10.192 GPM
at 60 Hz, pump speed is 1760 RPM
1760 RPM corresponds to 10.051 GPM

## Slide 26: GaInSn Jet
The jet flow in GPM is obtained from the measured jet velocity as follows:
From the properties of the nozzle, vinAin= voutAout , so that vin= voutAout/Ain
since Aout / Ain=0.150, vin= 0.15vout
Inflow(GPM) = vinAin = 0.15voutAin
= 0.15 vout (m/s) 100 (cm/m) Ain (cm2) 60 (s/min)
/1000 (cm3/l)/2.7853 (l/gal)
Outflow = Inflow
Problem:
Plot of flow vs frequency obtained from jet velocity measurements
does not agree with the Keyence flowmeter data or with the flow vs frequency data derived from plot provided by Liquiflo. While
the overall trends are similar, the values do not agree with one another.

## Slide 27: Flow meter cont’d
Flow meter dimensions and materials
Flow meter as constructed with KF flanges
Magnet holder
B field as calculated with FEMM
Assembled flow meter being leak checked
Comparison of voltages generated using equations
given in the above mentioned references for GaInSn
flowing in a 4747 gauss field.

## Slide 28: Jet Thickness Measurement – image processing
It is critical that the target thickness remains constant
Summer undergraduate intern developed a image processing technique to measure the variation of the jet thickness in time was implemented using Python + Open CV:
ROI and noise reduction applied to image from the RPi camera
Canny edge detection is then applied to each processed subarea. This is a binary pixel map that highlights high contrast pixels.
The Hough lines algorithm is then applied to probabilistically find straight lines in the Canny Edge map.
The lines that are farthest apart are selected. The change in distance between the line pairs is then determined.
Assuming that the change in width is constant, the known starting width (3mm) and distance between the nozzle and the flow capturing tube (20mm) are then used to find the width halfway between the nozzle and the receptacle.

## Slide 29: Flow width measurement – image processing
Preliminary test taken at a frequency of 3 Hz provided an average width measurement of 3.17 mm with a standard deviation of 0.057 mm (1.78%).
Algorithm is a convenient and reliable method to visually measure changes in the width of the liquid metal jet
Sensitive to lighting conditions and camera mounting (Sealed Camera volume)
Example of Hough Lines used.
Typical camera image used

## Slide 30: Readiness for JLab LERF beam test
A second system is being built incorporating all the improvements we’ve developed over the past two years, to be delivered later this spring to Jlab for testing.

## Slide 31: Next steps
Continue experiments that investigate jet properties, new 3D printed nozzles
Investigate new designs for jet collector (almost complete) – can we reduce droplets formation to zero – unsteady start up flow (?)
Construct final version of positron converter and incorporate lessons learned from the prototype for delivery to Jlab for upcoming LERF tests
This work is based upon work supported by the U.S. Department of Energy under Award Number DE-SC0023574

## Slide 32: Backup Slides
Backup Slides

## Slide 33: Radioisotope production in the GaInSn target

## Slide 34: Radio isotope production

## Slide 35
Gamma dose rates in (rem/h)/(el/s) in GaInSn and W targets by 10 MeV electrons

## Slide 36
In both cases, 3 cm from target, the dose rate is ~4.0E-07 (rem/h)/(el/s). 1 mA corresponds to 6.242E+15
(el/s), so dose rate is 2.5E+09 rem/h. For gammas, rem=rad, so dose rate is 2.5E+09 rad/h.
The GigaRad/h dose rates is a problem for the magnetic field needed to collect the positrons. No known magnet wire insulation can withstand such high dose rates. Need bare conductor coils with many turns and several kA currents.
Gamma dose near target (LM and W)

## Slide 37: Energy per gram deposited in the GaInSn target by 10 MeV electrons
Energy deposited into a 1.2 cm2 area of GaInSn vs. target thickness. At 0.3 cm, the energy deposited is 1.15 MeV/g/el, or 2.67 MeV/el. For a 1 mA beam, this corresponds to 2.67 kW.

## Slide 38: Flow meter
Purchased a model MD-MZ50AYK flow meter from Keyence and incorporated it into the system. Initially behavior of the device was very erratic, but it settled with time. Not much information about the device was available. This, combined with the fact that the device electronics probably would not survive in a high radiation field led to a design and construction of a device, based two papers available on the web.
G.E. Turner, "Liquid Metal Flow Measurement (Sodium) State-of-the-Art Study", LMEC-Memo-68-9
R. M. Carroll, "A Simple Electromagnetic Flowmeter for Liquid Metals", ORNL-1461
Magnetic flowmeter operation is based on the physical phenomenon discovered by Faraday, namely, that a potential is developed across a moving conductor in a magnetic field. This potential is proportional to the object’s velocity and magnetic field strength, and is developed at right angles to both the magnetic field and the direction of movement of the object.

## Slide 39: Front and Back View of Cameras Used
Each camera used is a Raspberry Pi Camera Module 3, 12MP IMX708 75°(D) Autofocus Pi Camera V3.

## Slide 40
25 Hour Duration Gun (Thermal / Vacuum)
3rd Run
Note: with solenoid magnet removed

## Slide 41
36 Hour Duration Gun (Thermal / Vacuum)
4th Run
Note: with solenoid magnet removed