## Slide 1: Resonance and Interlocks for EIC
James Latshaw
11/13/2025
SRF Frontiers Workshop

## Slide 2: Outline
Introduction
  System needs
Preliminary Design
  Motivation for a Scalable Design
  Generic Slot Concept
  Integration into a Common Platform Daughter (CPD) chassis
  Block Diagram
  Initial Testing of Arc Detectors
Summary and Next Steps
  PDR2
  Planned Cavity Testing (RHIC 197 MHz Cavity)
  FDR

## Slide 3: Introduction
Resonance control
  Extend performance range of system by making it tunable
    Motor, Piezo, Ferrite, Thermal Control (Warm cavities)
  Some cavities need to be moved off and then back on reference when a beam loss event occurs.
Interlocks
  Kill RF if a fault is detected
    HPRF permit, RF DAC drive inhibit
  System protection
    Arc detectors, Temperature Monitoring
  Subsystem Interlocks
    Vacuum, HPRF/SSA Interlocks, Coupler Bias, etc.
  System Diagnostics
    Temperature sensors, readbacks from subsystems
  Fault Annunciation, clearly show why RF is off
Currently there are 7+ cavity types for EIC (SC and NC)
  Common interlock types but varying channel count needs
  Work has been to develop a scalable system which can be used for all cavity types
Two vacuum gauges
One vacuum side arc detector
Air side arc detector #1
a dry air flow inlet on the other side
One air side arc detector #2
Temperature and flow switch at every water channel

## Slide 4: Motivation for a Scalable Design

## Slide 5: Preliminary Design – Generic Slot
A scalable slot design is being pursued
  Leveraging the common signal types
By adding enough slots, all system needs will be met
  Economy of scale, the same PCB can be used on all cavity types
  Less slots will be used for the less demanding cavity types
Each slot (shown on right) contains the below IO interfaces
  1, Stepper Motor Driver
  3, Temperature Sensing 24 bit ADC (targeted towards RTD sensors)
  2, 16 bit DACs with +/- 10V Drive range
  2, Dry Relay, compatible IO (5 to 24V compatible)
  4, 100 KSPS 16 bit ADCs (with instrumentation buffers, +/- 12V)

## Slide 6: Preliminary Design – Generic Slot

## Slide 7: Preliminary Design – Integrating into BNL CPC/CPD Design
Up to 8 Generic Slot boards will go into a 5U chassis which will leverage BNL’s common platform system architecture
  Artix Ultrascale + FPGA
Common platform will provide power needs including a 48VDC for motor drivers
Fast ferrite, high power RF SSAs, coaxial couple bias, vacuum systems are external subsystems which this chassis will interface with
Piezo needs are TBD, but most likely this chassis will provide low level drive signals and the piezo’s will be driven by an external subsystem
PDU
Extended Carrier
DIO
Generic Slot
Mother Board

## Slide 8: Carrier to Daughter Interface – Block Diagram
Carrier
Daughter, Artix US+, XCAU25P
Zynq US+
MPSoC
DDR4
Register Map
Aurora PHY 64B/66B
AXI
Slave IF
AXI-Lite
Master IF
Aurora PHY 64B/66B
AXI
Master IF
AXI-Lite
Slave IF
DMA
Stream Data
M_AXI_
S_AXI_
C2C_Slave_0
C2C_Master
Application Top
Aurora PHY 64B/66B
AXI
Master IF
AXI-Lite
Slave IF
C2C_Slave_1
8 Stepper Motor Drivers
48V, 10Amps, Bipolar
24 Temperature Sensors ADCs, 24 bit
16 DAC Channels
16 bit, +/- 10V
16 Dry Relay Contacts
5 to 24V, Configurable IO
32 ADC Channels
16 bit, 100 KSPS, +/-12V
UART Debugger
Peripheral Management

## Slide 9: Arc Detector Selection
The Fundamental Power Coupler (FPC) is planned to be equipped with arc detectors (ESR FPC shown on right)
An effort lead by Kyle Fahey at BNL was to test various arc detectors with the planned for this FPC
  PMT
  Photodiode
Goal is to use light pipes to detectors arc events as well as to send a test light to validate the arc detector functionality
CEBAF Arc Detector
FPC

## Slide 10: Summary and Next Steps
Continue lab testing of prototype boards
  Evaluate results and determine if a re-spin is required.
Preliminary Design Review part 2
  Address Review committees comments
  Incorporate any additional recommendations
Cavity Testing
  Test prototype system on one of BNL’s RHIC 197 MHz Cavity (notionally 4/2025)
  Incorporate any lessons learned
Final Design Review

## Slide 11: Thank you!
Questions?