## Slide 1: Applications of Compact SRF Accelerators
SRF Frontiers Workshop @ JLab ‘25
2025-11-13
John Vennekate
Notes: Tip: Keep titles under 60 characters for readability
To change the photo: Right-click on photo and select change photo

## Slide 2: My Definition of Compact SRF Accelerators
compact machines
single cryomodule single cavity
depending on application/energy need single-cell vs. multicell cavity
compact cryogenics
conduction-cooling (typically)
Nb3Sn (and all its challenges) & cryocoolers @ 4 K
injector & booster
  separate normal conducting
  integrated SRF gun concept (and all its challenges)
Notes: Guidelines: 6-8 bullets per slide; Use sentence fragments for bullets

## Slide 3: The Science Case – Euclid Beamlabs
Application: UEM/UED see session VIII on Friday
1.3 GHz, 1.5-cell cavity
  collaboration with FNAL, BNL, ANL
0.5 pC beam current 2 W RF power
single cooler
user facility @ BNL
Notes: Guidelines: 6-8 bullets per slide; Use sentence fragments for bullets

## Slide 4: Outside of Research Realm – Industrial Applications
industrial application means irradiation typically energies 1-10 MeV
direct use of electron vs X-ray conversion
low penetration (cm) vs low conversion efficiency (15 %)
main advantage of SRF
extremely high power conversion efficiency (RF to beam) after offset of cryogenics
deliver high-power beams contemporary NC RF machines 100 kW
either same dose faster = more throughput
or higher doses
Notes: Guidelines: 6-8 bullets per slide; Use sentence fragments for bullets

## Slide 5: Spectrum of Applications
food irradiation
  up to 30 kGy
  eliminate microorganisms/pests, reduce spoilage & prevent sprouting
  replace pesticides & extend shelf life
medical device sterilization
  15 - 40 kGy
  destroy microorganisms, prevent infections replace fumigation (ETO) & gamma sources
  largest margins
industrial chemical processes
  50 - 200 kGy
  induce chemical reactions enhance properties by curing/crosslinking
  replace additives or long heat treatment, precise control of process, enhance lifetime/support recycling of polymers
decontamination/environmental
  100s of kGy PFAS 1-2 MGy
  contaminated soil, biosolids, leachate, wastewater
  mineralize contaminants, “reset” filtration material
Notes: Guidelines: 6-8 bullets per slide; Use sentence fragments for bullets

## Slide 6: Summary
Technology: Nb3Sn & cryocooler
Main Edge: efficient delivery of high (100 kW) beam power
more throughput or higher doses
          extend existing applications (food, medical device, …)
          enable new fields of use (ICPs, environmental, …)
Challenge: technology transfer to industry
reliable & reproduceable performance of SRF
address application specific interface requirements
Competition: Rhodotron complex, expensive, long lead time, proprietary efficiency 60 %
Notes: Guidelines: 6-8 bullets per slide; Use sentence fragments for bullets

## Slide 7: Exotic Application – Production of Radioisotopes
Niowave: Compact SRF Accelerator for Commercial Production of Radioisotopes
photon generation via liquid metal target
production of radioisotopes from uranium & radium
20 MeV via recirculation through 3-cell cavity
115 W @4.2 K plant custom development with Linde
started 10 kW, 60 kW tetrode licensed up to 100 kW
Notes: Guidelines: 6-8 bullets per slide; Use sentence fragments for bullets

## Slide 8: QUESTIONS?
Notes: Before sharing your presentation, confirm:
Fonts are consistent
Images meet quality standards
Charts use template colors
Footer information is current
Spell check completed
Links are working
File size is optimized