## Slide 1: Materials science drivers for UEMs
11/14/2025 Jlab SRF workshop
Andrew R Lupini
Center for Nanophase Materials Sciences Oak Ridge National Laboratory

## Slide 2: Electron microscopy at CNMS

## Slide 3: Scanning Transmission Electron Microscopy
Scan over sample
Pixelated detector
Lens
Electron
beam
J.M. Ok et al. APL Materials 8 (5), 051104 (2020)
Buffer layer (CuCrO2) essential for single phase growth

## Slide 4: Ideal lens
Ideal lens is diffraction limited:
Higher energies reduce wavelength
High-angle rays
Minimum probe diameter
Point source
Low-angle rays
Objective lens
Gaussian focal plane
Aperture
Source size needs to be small or be demagnified

## Slide 5
Real lens is limited by aberrations to ~ 50 wavelengths
Scherzer Theorem (1936) – Correction ideas (1947)
High-angle rays
Minimum probe diameter
Point source
Low-angle rays
Objective lens
Gaussian focal plane
Aperture
Over-focus
Aberrations
Notes: Explain name spherical

## Slide 6: Spatial Resolution
Pennycook et al. MRS Bulletin, 31, 2006
Practical success by:
Krivanek et al. and Haider et al.
~2000

## Slide 7: How else could the microscope be improved? Energy spread
Krivanek et al (2014)
Hachtel et al (2018)
Energy spread needs to be small

## Slide 8: Phonon Spectroscopy in the Electron Microscope
Principle of detailed balance

## Slide 9
Scanning Transmission Electron Microscope
Heavy
Light
“Z-contrast”
Scattering to high angles depends on atomic number Z
EELS: Chemical AND electronic information
Many other signals: BF, LAADF, MAADF, X-rays, secondary electrons, …
In HAADF mode we are not using most of the electrons that interact with the sample
A probe is focused onto the sample. Images are formed by scanning the probe and detecting the scattering on various detectors. HAADF only uses a small fraction of the electrons.
Counts
Energy
Ti-L
O-K
Aberration corrector has hundreds of optical elements
Monochromator
Sample–

## Slide 10: 1977: First movies of single atoms
More motion at higher temperatures

## Slide 11: Moving Atoms in STEM 2D materials at 60 kV
T. Susi et al., Phys. Rev. Lett. 113, 115501 (2014).
Susi, T. et. al. Ultramicroscopy, 180, 163-172 (2017).
Dyck, O. et. al. Appl. Phys. Lett. 111, 113104 (2017).
Lee, J. et. al. Nat Commun, 4, 1650 (2013)
Zhou, W. (2011)

## Slide 12
Kalinin, Borisevich, Jesse, Nature 539, 485–487 (24 November 2016) doi:10.1038/539485a
Dyck, O., Ziatdinov, M., Lingerfelt, D.B. et al. Atom-by-atom fabrication with electron beams. Nat Rev Mater 4, 497–507 (2019). https://doi.org/10.1038/s41578-019-0118-z
STEM Platform
High-precision beam (~1 Å)
Energy range (30-300 kV)
Can access material interior
Higher energies penetrate deeper but also cause more damage

## Slide 13: Automation: Higher speed and novel scans
Traditional Raster Scan for Imaging
Rapid change in direction,
Scan coils can’t keep up
Distortion due to mismatch of intended and actual beam position
In a spiral scan, the signal to both scan coils is a single frequency sinusoid
MoS2
Directed Defect formation

## Slide 14: Automation: Higher speed and novel scans
10 ms/frame
Traditional Raster Scan for Imaging
Rapid change in direction,
Scan coils can’t keep up
Distortion due to mismatch of intended and actual beam position
In a spiral scan, the signal to both scan coils is a single frequency sinusoid
Atom removal

## Slide 15
Dyck, O.; Yeom, S.; Lupini, A. R.; Swett, J. L.; Hensley, D.; Yoon, M.; Jesse, S. Top-down Fabrication of Atomic Patterns in Twisted Bilayer Graphene. arXiv January 4, 2023. https://doi.org/10.48550/arXiv.2301.01674.
Automation:
FPGA-based
Feedback Control
Single Location:
Array of Locations:

## Slide 16
Dyck, O.; Yeom, S.; Lupini, A. R.; Swett, J. L.; Hensley, D.; Yoon, M.; Jesse, S. Top-down Fabrication of Atomic Patterns in Twisted Bilayer Graphene. arXiv January 4, 2023. https://doi.org/10.48550/arXiv.2301.01674.
Towards arrays of atoms

## Slide 17: High speed excitation? Laser concept

## Slide 18
Laser illumination
Want:
Sample heating / cleaning
Differential (local) heating
Optical excitation
Problem:
Don’t want to have to tilt
UHV
Maintain existing capabilities
Budget!
Fiber-optically coupled laser

## Slide 19: High- speed detectors: TimePix4
~200 pS time resolution
Merlin EELS
Quantum Detectors Merlin TimePix4
Design and model: Alexander Reifsnyder
Mathieu Benoit (ORNL) and CERN

## Slide 22: Electrons hit multiple pixels
Escape peak
1e-
2e-
Need to separate/cluster events
Determine probe position at that time
Extensive processing to images
~ 160GB/sec!

## Slide 23: Discussion: Could SRF technologies work with S/TEM?
From this talk:
  Source size needs to be small or be demagnified
  Energy spread should be small
  Higher voltages damage/change the sample more (roughly speaking) – I’d want 20-300kV
  Fast feedback can mitigate/use these changes
  Fast blanking would be useful
Pulsed source:
  S/TEM Time resolution? Detectors/laser approaching ~ nS
  Current source: ~uA, STEM beam (~pA) ~1 electron every few nanoseconds
  What if we knew when the electron left the source?
Other:
  Cryogenic S/TEM is improving (damage and ‘quantum’ materials)
  Interest in superconducting lenses
  Very fast scanning?
  Ultrafast projects: – mostly diffraction and TEM?
    e.g. Ruedi project in the UK
Electron microscopy is quite good at solving materials problems…

## Slide 24
Center for Nanophase Materials Sciences A DOE User Facility for Creating, Characterizing, and Understanding Nanomaterials
Proposals:
Simple, two-page narrative
Two general calls per year
Short-term projects accepted continuously
Joint proposals with neutron sources (SNS, HFIR)
Research areas:
Synthesis – Soft matter (precision synthesis, selective deuteration), 2D materials, hybrid structures, epitaxial oxides
Nanofabrication – Direct-write (3D) fabrication, e-beam lithography, multiscale fluidics, 10,000 sq. ft. cleanroom
Advanced Microscopy – AFM, STM, aberration-corrected and in situ TEM/STEM, He-ion microscopy, atom-probe tomography
Chemical Imaging – Multiple approaches based on mass spectrometry or optical spectroscopies
Functional Characterization – Laser spectroscopy, transport, magnetism, electromechanical phenomena
Theory/Modeling, Data Analytics – Including interactions and co-development with leadership-class, high-performance computing
Gateway to Neutron Sciences – deuterated materials, sample environments, multimodal measurements
Providing free access to staff expertise and equipment if intent is to publish results.
cnms.ornl.gov

## Slide 25: Acknowledgements
This work was supported by the U.S. Department of Energy, Office of Basic Energy Sciences, Division of Materials Sciences and Engineering. Experiments were performed at the Center for Nanophase Materials Sciences (CNMS), a U.S. DOE Office of Science User Facility at Oak Ridge National Laboratory (ORNL).
Collaborations with, Waviks Inc., Quantum Detectors and Nion Co. are gratefully acknowledged.
Includes contributions from:
Ondrej Dyck, Alexander Reifsnyder, Jacob Swett, Mina Yoon, Stephen Jesse, Miaofang Chi, Maxim Ziatdinov, David Lingerfelt, Ray Unocic, Bethany Hudak, Sergei Kalinin, Albina Borisevich, Songkil Kim, Cheng Zhang, Philip Rack, Jason Fowlkes, Bobby Sumpter, Elisa Jimenez-Izal, Ivan Kravchenko, Leslie Wilson, Ivan Vlassiouk, Ryo Ishikawa, Sangmoon Yoon, Ho Nyung Lee, Yueming Guo, Lizhi Zhang, Sinchul Yeom, Sarah Dillender, Dale Hensley, Jan Mol, Dave Geohegan, Toma Susi, Alexander Markevich, Steven Stevenson, Harry Dorn, Tanisha Richardson, Wu Zhou, Mathieu Benoit, Jordan Hachtel
Slides for: SRF Frontiers Workshop at Jefferson Lab, 2025/11/14