## Slide 1
FY25 run
Strengths, weaknesses, and opportunities for improvement
Operational goals and technical plans
October 7, 2025
Joe Grames
CIS perspective and plans
Notes: Tip: Keep titles under 60 characters for readability
To change the photo: Right-click on photo and select change photo

## Slide 2
CIS – Key CEBAF objectives
Complete the 200 keV injector upgrade
Improve reliability
Prepare for Moller

## Slide 3
FY25 SAM – correcting work flow design errors
All solenoids repaired:
https://tasklists.jlab.org/atlis/tasks/110664
before
after
As built:
Notch caused skew multipoles
Repaired:
Correct response
https://tasklists.jlab.org/bslist/tasks/109864
Notch in center plate
Short focal length of R30-3 gun led to overfocusing. Fixed by lowering cathode focusing strength
R30-3, 2023 (25 deg)
R30-4, 2024 (16 deg)
25° cathode angle
16° cathode angle
M. Bruker, C. Hernandez-Garcia, A. Hofler, G. Palacios-Serrano, "Photogun simulation workflow: from geometry to beam dynamics". Technical Note JLAB-TN-24-015

## Slide 4
FY25 SAM – improving drive laser reliability
In FY24 we had a beam strike event, traced back to a misconfigured shutter on the laser table
The RAR process resulted in developing various laser system improvements
  Replacing hand-aligned with tool-aligned fixturing
  Developing configuration control of the laser table layout
  Overhauling the hot-checkout process, now a detailed laser checklist
  Installing a remote laser-control health check that Ops runs daily
  Installing a new fast MPS laser shutter (this SAM)

## Slide 5
FY25 Restoration – over-cycled hardware
Chart: Bellows Cycles
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025
FC1 | 4672 | 808 | 276 | 21310 | 24142 | 30462
FC2 | 35296 | 22971 | 66569 | 20879 | 617 | 1298
Bellows rate lifetime: 5,000-10,000 cycles.
Insertable Faraday cups were not designed to be cycled as often as FSD trips
  Bellows failures on FC1 and FC2
  Bearings failure on FC1 (during FY25 restoration)

## Slide 6
FY25 Restoration – 25+ year old chopper bellows failed
Chopper viewer bellows failed
  Catching early indicators can help us avoid vacuum loss
  Diagnosis was easy, but repair was confounded by unknown captured part
Options to react, e.g.
P > 5x10-5 Torr: Hard trip, close valves, pumps off
P > 1x10-6 Torr: Fast trip, close valves
P > 1x10-7 Torr: Slow trip – after 45 minutes above

## Slide 7
FY25 Spring Run source performance
Polarized Electron Source
  Gun ran reliably @ 200 kV
  Beam to 4 halls as needed
  Produced 300 C from two spots (lifetime 100-150C)
  Beam polarization was expectedly high 85-90%
150 C
150 C
Recent Downtime
FY24 – 350 hours
FY25 – ½ hour
Beam Current (uA)

## Slide 8
FY25 – keeping hardware on our radar
Like the RF system our lasers need amplifiers to boost the power needed for the program, typically 50-100 mW
They do have a finite lifetime, we use them as long as possible b/c they’re not cheap $25k
During the Spring run Ops struggled with transporting beam, until we ”coincidentally” swapped the aging Hall A amplifier…
No beam diagnostic revealed a smoking gun, but we can lobby for funds to replace amps sooner, and we’re adding some additional remote diagnostics for operators
Spring run - squeaking out last bit of power from Hall A amp
24 months
Power to cathode (Watts)

## Slide 9: Now, FY26…

## Slide 10
FY26 SAM – End of run HCO
We have now begun doing pre-SAM walkthroughs for equipment we provide or use for injector operations
  Vacuum system
  High voltage system
  Magnets and RF
  Laser
Identified some issues !!!
  Failed air fitting seals at the pneumatics
  Air core magnets that are deformed or cracked
  Viewer that does not have proper stroke
  Communication issues with laser amplifiers and possibly with LLRF stepper motor chassis (used for laser table stepper motors)

## Slide 11
FY26 SAM – Prioritizing safety & inspection
SF6 relief valve exchange every 5 years (CATS item)
Upgrading driver laser room with CANS (CATS item)
Working with FML to prioritize our breaker panel PM (CAT1 PPE)

## Slide 12
FY26 SAM –
Gun HVPS system
SF6 relief valve
Regrease HV connections
200 keV Wien filters
Evaluate root cause trips
Test prototype solution
Vacuum system
Eliminate JLab UHV for I&C solution
Evaluate chopper ion pumps
Laser jobs (Moller)
Measure photocathode anisotropy
Characterize laser setup for 9/3 BS
Test prototype RTP switch
Measure IA risetime
Laser jobs (reliability)
Laser room CANS system
Upgrade helicity generator
Install fast MPS laser shutter
Install remote laser profile/position monitor
Evaluate root cause Hall A laser issues
Prepare for Beam studies
Moller PQB studies (Dec FC1)
Degrader studies (Jan FC2)

## Slide 13
FY25 – 200 keV Wien filters
Wien filters upgraded SAM 2021
  130 keV, 90 deg: 11 kV / electrode, B= 2,500 G-cm (~10 A)
  200 keV, 90 deg: 18 kV / electrode, B = 3,633 G-cm (14.5 A)
Performance at 200 keV limited
  In January learned 90 deg spin angle resulted in vacuum activity
  Limited each Wien to 60 deg; then used both Wiens together to reach requirements for Spring program, worked well
Evaluated SAM 2025
  Applied 19 kV per electrode over 3 days, no issues with magnet off
  No vacuum issues with magnet set to 3,145 G-cm (12.5 A) and 19 kV per electrode (magnet yoke temp ~ 42 C)
  Vacuum activity present with magnet set to 3,755 G-cm (15 A) and 19 kV per electrode (magnet yoke temp ~ 55 C)
  Vacuum activity looks related to vacuum load due to magnet temp (heating beam pipe)
  Cooling schemes will be tested this SAM
13
No vacuum activity: Electrodes at 19 kV, magnet up to 12.5 A
Vacuum activity: Electrodes at 19 kV, magnet 14.5 A

## Slide 14
FY26 – Chopping chamber remediation plan
Chopping chamber critical for CEBAF operations
  but, bellows of 6 critical function devices beyond end of life, have started to fail
  and, not well documented, also those who serviced it have retired
Plan A – proposal submitted to design and build a new chopping chamber, improved alignment, fixturing, serviceability, solenoids
Plan B – in the meantime, develop an “emergency repair” by stakeholders involved in doing Plan A

## Slide 15
CIS R&D – Commercializing insulators (KEK/Kyocera/JLAB)
Compact inverted insulators are ideal for mating a photogun to the high voltage power supply via a cable
Compared with cylindrical insulators, an inverted insulator reduces the electrode surface exposed to high voltage
The photogun vacuum chamber volume and surface area are reduced to reach lower ultimate vacuum
KEK received funding for Kyocera to manufacture a test insulator with low secondary electron yield
JLab manufactured test electrodes
JLab will be high voltage testing the Kyocera insulator with electrodes under vacuum
96 cm
Slide courtesy Carlos Hernandez-Garcia, Jefferson Lab

## Slide 16
CIS R&D – strained AlGaAs/InAlGaAs high polarization photocathodes grown by MBE (UCSB/JLAB)
GaAs/GaAsP: phosphorus
  Complicated in MBE systems
InAlGaAs: all common in MBE
  Easier for commercial vendors
    Commercial vendor can’t procure substrate GaAs at this time
  Independent control of strain and band gap
  Arsenic caps
Can increase polarization (strain) and bandgap (wavelength)
simultaneously
AlGaAs/InAlGaAs | Polarization (%) | QE (%)
Standard (green) | 85 ± 0.9 | 0.48
Best Pol. (orange) | 90 ± 1 | 0.33
Best overall (red) | 88 ± 4 | 0.95
Slide courtesy Marcy Stutzman, Jefferson Lab

## Slide 17: CIS R&D – strained GaAs/GaAsP spin polarized electron sources grown by MOCVD (ODU/JLAB)
Device Structure
No DBR: QE: 1.4%; Pol: 90% @ 780nm
SPES successfully grown by MOCVD with and without Diffracted Bragg Reflector (DBR)
Polarization above 90% can be obtained
QE above 1% without DBR and above 2% with DBR can be obtained
Devices achieved 11 nC with the free limit range and 9 nC with an 8 mm diameter laser
Slide courtesy Professor Sylvain Marsillac, Old Dominion University
DBR: QE: 2.3%, Pol: 92% @ 780nm

## Slide 18
The polarized source and injector contain critical and unique components
  some are single points of failure, so require high reliability
  some push the limits of performance, so require time to test-fail-learn
  some like our photocathodes and insulator rely on critical R&D
The changing face of CIS
  None of the “original” EGG are with the group, many were technical staff and the R&D was highly NP oriented
  Today we have an older group, experienced scientists who are able to contribute to broader R&D interests, consequently less focused
  We’re starting to move the needle, but need the lab’s support to hire, train and retain new and younger staff, to set priorities is essential
Outlook

## Slide 19: Questions ???