## Slide 1: JLab Hypernuclear Beamline Update
Hypernuclear Collaboration Meeting
Dave Gaskell
Jefferson Lab
February 12-13, 2026

## Slide 2: Hypernuclear Setup in Hall C and Beam Requirements
Hypernuclear target 6.6 meters downstream of nominal target position
Key requirements:
  Successfully transport beam to dump, mitigating stray fields from magnets close to beamline
  Beam energy spread <= 3 x 10-5 (70 keV at 2.24 GeV)
  Beam position precision and stability at target: s = 0.1 mm

## Slide 3: Beam Position
Existing BPMs (3H07A/B/C) are too far from hypernuclear target to provide required precision (0.1 mm) by themselves
  DzBPM-target = 9.8/8.8/7.9 meters for existing BPMs
  Assuming sx/y=0.1 mm for each BPM, starget = 0.65 mm
Additional position monitors will be added between pivot and hypernuclear target
  Will use existing polarized target girder
  Has 2 BPMs  3.9 and 2.2 meters from target
  Using 3H07A/B/C + new BPMs, starget = 0.11 mm
In addition to girder installation work, BPM and harp readout will require support from I&C and Accelerator Software
Reminder

## Slide 4: Polarized Target Girder
Superharps
M20 (3 inch) BPMs
Add extra BPM?

## Slide 5: Downstream Diagnostic Girder
Dean Spiers
Hall C Pivot
Hypernuclear target
Enge
Diagnostic girder

## Slide 6: Polarized Target Girder
Polarized target girder was on top shelf at the back of Physics Storage
One harp has been removed  used elsewhere in machine
 Could not verify from floor that both BPMs are still there

## Slide 7: Polarized Target Girder in ESB
Since last collaboration meeting, Hall C techs have removed girder from shelf in Physics Storage
Staged in ESB
 SEM has been removed  presence of beryllium made this a little problematic
Missing components now clearly visible
3-inch BPM – I&C has located a spare in good condition
Harp  need to find one from other location

## Slide 8: “Spare” Harps and BPMs
Girder used during Q-Weak experiment is stored in ESB  2 harps and 2 BPMs available (and other things)

## Slide 9: BPM readout
Hypernuclear experiments will require event-by-event readout of BPM information
  This has not been done in Hall C since Q-Weak experiment (2012)
  Hardware still in place  spares will become available after MOLLER installation in Hall A (switching to new technology)
  Will need additional FADC channels for readout  could “borrow” from HMS and/or SHMS

## Slide 10: BPM readout
Located patch panels for connections from sample and hold cards
Beamline BPMs (3C12, etc.) in 1st floor electronics room in CH
Hall BPMs on 2nd floor (”G0 cage”)
VME crate, 1st floor CH

## Slide 11: BPM readout test
BPM 3C12
y position
x position
Connected BPM signals from 3C12 to spare FADC channels in HMS/SHMS DAQ
Verified analog outputs from SEE BPM electronics still functional
BPM class has been added to hcana to simplify analysis
Would like to add more signals from Hall BPMs if time allows
Bill Henry

## Slide 12: Synchrotron Light Interferometer (SLI)
Beam energy spread will be continuously monitored using new Synchrotron Radiation Interferometer
3C12 GIRDER
TURNING MIRROR
(TW0 AXIS SERVO)
Dedicated beam test performed at end of last run period
High gradient beam (10.6 GeV at 5 pass  MOLLER run conditions)
Set up 1 pass beam in Hall C  Hypernuclear run conditions
Joe Gubeli
CAMERA, SLIT STAGE

## Slide 13: SLI Beam test Summary
Brief high level summary
  SLI saw synchrotron light and interference pattern
    Central peak too large/bright – could not fit interference pattern
  Used superharp scan to constrain beam energy spread: dE/E = 3.2 x 10-5
  Removed slit and monitored beam size overnight  energy spread drifted up to dE/E = 4.5 x 10-5
Nick Sereno (CASA) gave a more detailed summary at Physics staff meeting
  added full presentation to this meeting Indico
  a few excerpts in following slides

## Slide 14
Nick Sereno

## Slide 15
Nick Sereno

## Slide 16
Nick Sereno

## Slide 17
Nick Sereno

## Slide 18: Summary
Making some progress on Hypernuclear beamline preparations
Highest priority is more tests with SLI to understand bright central peak
Will continue to work on adding a couple more BPMs to DAQ
Polarized target girder needs work, primarily from I&C and Vacuum group
  Both are busy with MOLLER preparations and getting ready for upcoming run
  Might be more cycles when 2026 CEBAF run starts

## Slide 19: Backup

## Slide 20: Beam Energy Stability: 9th Dipole
Additional information about relative beam energy can be provided using “9th dipole”
System used during previous hypernuclear experiment in Hall C
Not used for absolute beam energy measurement a la Hall A
BE magnet wired in series with Hall C arc magnets
NMR probe placed at fixed position in dipole
BE magnet still in place in BSY service building – needs modest amount of work to revive
Re-cable magnet leads
Locate and install NMR
Implement remote NMR readout

## Slide 21: Downstream Diagnostic Girder
Dean Spiers

## Slide 22: Polarized Target Girder
M20 (3 inch) BPMs
Superharps
Viewer

## Slide 23: MEASURING THE BEAM SIZE [NON-INVASIVE]
SYNCHROTRON RADIATION INTERFEROMETER
Joe Gubeli

## Slide 24: SYNCHROTRON RADIATION WORKSHOP (SRW) SIMULATIONS
TYPICAL FULL CAMERA FRAME
TYPICAL ZOOMED IN CAMERA IMAGE
HORIZONTAL SLICE THROUGH IMAGE CENTER
Joe Gubeli